Zhengzhou Rail Transit Line3 Project

Environmental and

Social Management Plan

Environmental Protection Center of Ministry of Transportation Assessment

Certificate of National Environment Assessment: Jia Zi No. 1038

April, 2014 Beijing

1 Introduction	3

1.1 Project Origin	3

1.2 The brief introduction of the project	6

1.3 Project summary	6

1.4 Purpose of Environmental and Social Management Plan	21

1.5 The preparation of the Environmental and Social Management Plan	21

2 Policies, laws and regulations framework and compilation basis	23

2.1 Laws and regulations	23

2.2 Technical regulations and standards	26

2.3 Safety insurance policies of the World Bank	27

2.4 Assessment standard	27

3 Environmental Management System	33

3.1 Set of Environmental Management System	33

3.2 Environmental Management Organ, capability and Duties	37

3.3 Environmental Management Training	48

3.4 Abstract of Environmental Protection Measures	50

4 Environmental Monitoring	117

4.1 Purpose of Monitoring	117

4.2 Monitoring Plan	117

5 Estimation of Environmental Protection Expenses and Analysis of Econoic Profit and Losses	120

5.1 Estimation of Environmental Protection Expesnes	120

5.2 Analysis of Economic Gains and Lossed due to Environmental Impacts	121

5 .3Conclusion:	125

6 Sources of funds	125

7  Information management of the Environmental and Social Management Plan	127

7.1 Reorganize and save of monitoring data	127

7.2 Information exchange	127

7.3 Record	127

7.4 Report	128

# 1 Introduction

## 1.1 Project Origin

As the provincial capital of Henan Province, Zhengzhou City is located in the hinterland of the Central Plain, with "an important hub controlling advantageous positions." Zhengzhou is always one of China’s important transportation and communication hubs, an important city of the new Eurasian Continental Bridge, and a national open and historical and cultural city. Zhengzhou is an important center city of the central region, the first city in Henan province and the urban agglomeration in the Central Plain, has unique and important geographic conditions, and is Henan Province’s political, economic and cultural center.

Zhengzhou City has a long history. The Shang Dynasty had its capital here. It is the birthplace of the Chinese Civilization and one of China’s oldest cities. Its north is near the Yellow River, its southwest is hilly land, and its southeast is a vast plain. In the pattern of China’s economic development, it has an important role in linking the east and west, north and south.

Zhengzhou now has under its jurisdiction six districts, five county-level cities, one county and two state-level development zones. The city's total area is 7446.2 square kilometers. In recent years, Zhengzhou’s economic construction and development is rapid. Throughout 2011, Zhengzhou completed 491.27 billion yuan of GDP, ranking 20th among Chinese large and medium-sized cities, and the annual general budget revenue of its local fiancé was 50.23 billion yuan, ranking 17th among Chinese large and medium-sized cities.

With the rapid development of the city, Zhengzhou presents such problems as population growth, the rapid growth of its motor vehicles, traffic jams and so on. Although, in recent years, Zhengzhou has been increasing investment in the construction of its urban traffic, the increase of its traffic supply is still far less than the growth of its traffic demand and its traffic supply and demand contradiction has an intensifying momentum.

To solve the problem of metropolitan traffic congestion, the general experience of domestic and international cities is to build rapid rail transit systems and construct integrated transport systems so as to solve traffic pressure and promote cities’ healthy development. To this end, in September 2000, Zhengzhou began the preparation of the planning of its urban rail transit lines and networks. In 2004, according to Zhengzhou’s overall urban planning-related local adjustment program and to experts’ review comments, the planning of Zhengzhou’s rail lines and networks experienced a local adjustment.

In August 2005, the Henan Development and Reform Commission organized and convened an experts’ review meeting on Zhengzhou City’s urban rail transit construction planning. The meeting proposed an opinion of further optimizing the forward line and network solutions. In January 2006, Zhengzhou’s rail transit construction plan was completed. In January 2008, in Zhengzhou, the China International Engineering Consulting Corporation (CIECC) organized and convened an evaluation meeting for "Zhengzhou City’s Rapid Rail Transit Construction Plan"; in March, the CIECC completed an assessment report and submitted it to the National Development and Reform Commission.

In April 2008, in Zhengzhou, the Ministry of Environmental Protection organized and convened an experts’ review meeting, comprehensively reviewing and passing in principle the "Environmental Impact Report for Zhengzhou City’s Rail Transit Lines and Networks Construction Planning." In February 2009, the National Development and Reform Commission printed and issued the "Circular of the National Development and Reform Commission Regarding the Request for the Examination and Approval of the Recent Construction Plan (2008 ~ 2015) for Zhengzhou’s Urban Rapid Rail Transit" (NDRC Basic Document No. [2009] 369.).

According to the construction plan, the Phase-1 project of Line 1 for rail transit started in June 2009, and the Phase-1 project of Line 3 started in December 2010.

Meanwhile, in order to coordinate the construction of Lines 1 and 2, do a good job of the reserved projects and provide technical support, the Zhengzhou Rail Transit Office organized and carried out the preliminary study of Lines 3, 4, 5 and 6, so as to provide a technical resource guarantee for along-the-line land use control planning, urban construction and the interim construction plan.

In July 2009, the Zhengzhou Rail Transit Office entrusted relevant units to formulate and complete the pre-feasibility study report (draft for review) for Line 3 project of Zhengzhou’s rail transit, which passed experts’ review. According to the experts’ review comments and related units’ opinions, the report underwent corresponding modification. In November 2009, the pre-feasibility study report (final draft) of Line 3 project of Zhengzhou’s Rail Transit was completed.

In 2010, in order to maintain the sustainability, feasibility and rationality of Zhengzhou’s rail transit construction, give play to the overall efficiency of Zhengzhou’s rail transit lines and networks as soon as possible, accelerate the process of building rail transit, and provide the construction basis for the follow-up projects of its rail transit, Zhengzhou started the preparation of "Zhengzhou City’s Rail Transit Construction Plan" (2013 - 2020). Currently, this planning report has been basically completed, initially having the conditions for being reported to a higher body.  .

Combining with the progress of the original construction plan and with Zhengzhou’s recent years’ development, this plan proposes that after the phase-1 projects of Line 1 and 2, the Phase-2 project of Line 1, the Phase-2 project of Line 3, the Phase-1 project of Line 3, the Phase-1 project of Line 4 and Line 5 be constructed. Among them, the project of Line 3 will be constructed in 2014 and will be completed and opened to traffic in 2016.

In October 2010, in order to coordinate the formulation of its rail transit construction plan and to carry out in advance the research work for the relevant lines, the Zhengzhou Rail Transit Office entrusted the Beijing Urban Construction Survey and Design Institute to carry out the feasibility study work for Line 3 project for Zhengzhou’s rail transit. In 2012, the institute completed a first draft feasibility study report. This EIA report is based on this first draft.

The Line 3 project of Zhengzhou City’s rail transit was included in the projects using the World Bank’s loans in 2011, which needed preparing an EA report, environmental assessment summary and environmental management plan (EMP) and other documents in line with the World Bank’s requirements. After accepting the entrustment, our unit organized experienced EIA staff members to undergo field research and collect the information and data related to the project, and completed the preparation of this report in December 2012.

## 1.2 The brief introduction of the project

Line 3 will be an oblique radial rail backbone line from northwest to southeast in the city’s center. The north end of the Phase-1 project of Line 3 will start from Xinliu Road Station at the provincial sports center in Huiji District, and the south section will end at East Hanghai Road Station at the Economic Development Seventeenth Street in the Economic Development Zone. The length of the line will be about 25.2km, all underground, with 21 stations, one car depot and one parking lot. The line will be constructed along Changxing Road, Nanyang Road, Minggong Road, Jiefang Road, West Street, East Street, Zhengbian Road, Nandu Road and Economic Development Seventeenth Street, and will connect the Feb 7 Square’s Commercial Center, Economic Development Zone’s center and other urban functional centers. The line’s average station spacing will be 1.29km, and its length will be about 25.2km, with 21 stations, one car depot and one parking lot.

## 1.3 Project summary

See Figure 3.3-1 “Sketch of Zhengzhou Urban Rail Transit Line 3” for the line details.

Figure 3.3-1 Sketch of Zhengzhou Urban Rail Transit Line 3

### 1.3.3 Station

Twenty one stations are laid in the first-stage project of Line 3 totally, all of which are underground stations. See Table 3.3-1 for the station distribution.

The table 1.3-1  The station distribution table Phase I Project of Zhengzhou Rail Transit Line 3

| SN | Station | mileage | Length (m) | Form of station | Notes |
| --- | --- | --- | --- | --- | --- |
|  | starting point. | K0+0 |  |  | The starting point of the Phase I Project. |
|  |  |  | 130 |  |  |
| 1 | Xinliu road station | K0+130 |  | Second floor underground island station | Set single crossover and out of line |
|  |  |  | 1430 |  |  |
| 2 | Samen road station | K1+560 |  | Second floor underground island station |  |
|  |  |  | 1310 |  |  |
| 3 | Xinglongpu road station | K2+870 |  | Second floor underground island station | Set single crossover before the Station |
|  |  |  | 1630 |  |  |
| 4 | Dongfeng road station | K4+500 |  | Second floor underground island station | And the 8th line transfer |
|  |  |  | 1220 |  |  |
| 5 | Agriculture road station | K5+720 |  | Second floor underground island station |  |
|  |  |  | 1480 |  |  |
| 6 | Huanghe road station | K7+200 |  | Second floor underground island station | And the 5th line transfer Set double stop line |
|  |  |  | 1135 |  |  |
| 7 | Jinshui road station | K8+335 |  | Detached island station |  |
|  |  |  | 910 |  |  |
| 8 | Taikang road station | K9+245 |  | Second floor underground island station |  |
|  |  |  | 890 |  |  |
| 9 | Erqi square station | K10+135 |  | Third floor underground island station | And the first and 7th line transfer |
|  |  |  | 780 |  |  |
| 10 | Shuncheng Sreet station | K10+915 |  | Second floor underground island station |  |
|  |  |  | 990 |  |  |
| 11 | Dongdajie Street station | K11+905 |  | Third floor underground island station | And the second line transfer Set single crossover |
|  |  |  | 795 |  |  |
| 12 | Chengdong road station | K12+700 |  | Third floor underground island station |  |
|  |  |  | 1145 |  |  |
| 13 | Future road station | K13+845 |  | Second floor underground island station | And the 6th line transfer |
|  |  |  | 930 |  |  |
| 14 | Fengtai south road station | K14+775 |  | Second floor underground island station |  |
|  |  |  | 1010 |  |  |
| 15 | Zhongzhou avenue station | K15+785 |  | Third floor underground island station | And the 4th line transfer |
|  |  |  | 940 |  |  |
| 16 | Tongtai road station | K16+725 |  | Second floor underground island station | Set double stop line |
|  |  |  | 1080 |  |  |
| 17 | Huanghe east road station | K17+805 |  | Second floor underground island station | And the 13th line transfer |
|  |  |  | 1020 |  |  |
| 18 | Agriculture east road station | K18+825 |  | Second floor underground island station |  |
|  |  |  | 1465 |  |  |
| 19 | Zhongxing road station | K20+290 |  | Second floor underground island station | And the 5th line transfer Set single crossover and connecting line |
|  |  |  | 1850 |  |  |
| 20 | Boxue road station | K22+140 |  | Second floor underground island station | And the 5th line transfer Set connecting line |
|  |  |  | 2840 |  |  |
| 21 | Hanghai east road station | K24+980 |  | Second floor underground island station | Behind the terminal station, there will be incoming and outgoing lines. |
|  |  |  | 2500 |  |  |

Line 3 is proposed to choose Type-A cars , A main technical specifications for Type-A cars, see Table 1.3-2.

Table1.3-2  the main technical specifications for Type-A cars

| SN | name | A type vehicle |
| --- | --- | --- |
| 1 | Body length of the basic /mm | 22000 |
| 2 | Body width of the basic /mm | 3000 |
| 3 | The maximum height of vehicle | The inverter vehicle | 3800 |
|  |  | Motor Car with pantograph | 3810 |
|  |  | Pantograph working height | 3900~5600 |
| 4 | interior height /mm | ≥2100 |
| 5 | High floor /mm | 1130 |
| 6 | axle weight /t | ≤16 |
| 7 | length between truck centers /mm | 15700 |
| 8 | rigid wheel base /mm | 2200~2500 |
| 9 | Each side door number | 5 |
| 10 | Passenger capacity | Fixed number of staff members or passengers（6 peoples/m2） | 310 |
|  |  | overman（9 peoples /m2） | 432 |

The total length of line 3 is 31.3km, including one car and one parking lot in the whole line. The car depot is located in the area south of Jingnan 3rd Road, east of Beijing-Hongkong Expressway, west of Circle-city Railway and north of Xin’an Road, covering a surface of about 33.9ha; the parking lot is located in the plot which is south of Jialu River, east of Changxing Road, north of Lianyungang-Huoerguosi Expressway and west of Jinbei Road, covering an area of about 8.9ha.

The overall layout of Xinliu Road parking lot is designed on the basis of stub-end depot type. According to technologic needs, the scheme plans such production rooms like application depot and project garage, and production support constructions like complex building, canteen and bathroom, drivers’ apartment, combined substation, signal cabin and sewage treatment station etc.

There are two accesses connecting to outside in Xinliu Road parking lot. The main access is located at the west part of the plot, opening to the planned Changxing Road and being close to the life and office area in front of plant; the secondary access is located at the east part of the plot, opening to the planned Guhe Road.

The overall layout of Xinliu Road parking lot is shown in Figure 1.3-2.

Main overhauling tasks assumed by Xinliu Road parking lot are shown in Table 1.3-3.

Table 1.3-3  Main overhauling tasks assumed by Xinliu Road parking lot

|  | Intermediate repair | Temporary repair | month examination | Parking lot |
| --- | --- | --- | --- | --- |
|  |  |  |  | initial stage | Short-term | Long-term |
| Hanghai east road car depot | 3+3 | 2 | 2 | 32 | 32 | 32 |
| Xinliu road parking lot | 0 | 0 | 2 | 16 | 16 | 32 |
| total | 3+3 | 2 | 4 | 48 | 48 | 64 |

Figure 1.3-2 Layout Plan of Xinliu Road Parking Lot

East Hanghai Road car depot

The overall layout of the scheme is designed with paralleled stub-end depot type. According technological needs, the scheme plans production rooms like application depot, unite overhauling house, track garage, scheduling machine house and service shop etc. and such production supporting houses as complex buildings, drivers’ apartments, canteens and bath rooms, material depots, combined substations and signal cabins and so on.

The overall layout of East Hanghai Road car depot is shown in Figure 1.3-3.

Figure 1.3-3 Layout Plan of Hanghai east Road Parking Lot

1）Designed year

Initial stage: 2022; short-term: 2029; long-term: 2044

2）Passenger flow volume

Table 1.3-4   Predicted Passenger Flow of Zhengzhou Subway Line 3

| design period | Total passenger traffic volume of all day (10,000 person-time/day | Passenger transport intensity (10,000 person-time/km) | Maximum section of passenger flow of all day(10,000 person-time) | Average riding distance (km) |
| --- | --- | --- | --- | --- |
| Initial stage（2022） | 42.38 | 1.35 | 2.23 | 7.94 |
| short-term（2029） | 86.92 | 2.77 | 2.90 | 6.79 |
| long-term（2044） | 117.47 | 3.75 | 4.05 | 6.96 |

3）Traffic organization

① Marshalling:Marshalling form of six-car metro train including four motor cars and two trailers in initial stage,short-term and long-term.The maximum driving speed is 80km/h, and operation speed is 35 km/h.

② Operating time：Operating time in the whole day is 18 hours from 5 o’clock to 23 o’clock.

③ Number of trains：In initial stage: 129/day; in short-term: 181/day; in long-term: 247/day.

④ Operating plan

Table 1.3-5  Driving Plan of Whole Day (number of trains/day)

| Time period | Initial stage | short-term | long-term |
| --- | --- | --- | --- |
| 5:00-6:00 | 4 | 6 | 8 |
| 6:00-7:00 | 8 | 10 | 15 |
| 7:00-8:00 | 15 | 15+3 | 20+5 |
| 8:00-9:00 | 8 | 15+3 | 20+5 |
| 9:00-10:00 | 6 | 10 | 15 |
| 10:00-11:00 | 6 | 8 | 10 |
| 11:00-12:00 | 6 | 8 | 10 |
| 12:00-13:00 | 6 | 8 | 10 |
| 13:00-14:00 | 6 | 8 | 10 |
| 14:00-15:00 | 6 | 8 | 10 |
| 15:00-16:00 | 6 | 8 | 10 |
| 16:00-17:00 | 8 | 8 | 15 |
| 17:00-18:00 | 12 | 15+3 | 20+5 |
| 18:00-19:00 | 8 | 12+3 | 15+5 |
| 19:00-20:00 | 8 | 10 | 15 |
| 20:00-21:00 | 6 | 8 | 10 |
| 21:00-22:00 | 6 | 6 | 8 |
| 22:00-23:00 | 4 | 6 | 6 |
| Total | 129 | 169+12 | 227+20 |

4) Construction methods

Phase I Project of Zhengzhou Metro Line 3 runs through current city zones of Zhengzhou and passes through prosperous commercial trade center of Zhengzhou. All adopt open-cut method except Jinshui Road Station. See Table 3.3-6.

Underground interval tunnel of this project adopts open-cut and shield methods for construction, see Table 1.3-7.

Table 1.3-6 Summary of Construction Method and Structural Shape of Line 3 Stations

| SN | Name of station | Form of station | Construction method | Structural shape of station | Depth of foundation pit (m) | Containment form | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Xinliu Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 4 |
| 2 | Shamen Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 3 | Xinglongpu Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 4 | Dongfeng Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 8 |
| 5 | Agricultural Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 6 | Huanghe Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 5 |
| 7 | Jinshui Road Station | Second floor underground separted island station | Cover dig method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 8 | Taikang Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 9 | Erqi square Station | Third floor underground island station | Open-cut method | Three-layer three-span box frame | 23 | The underground continuous wall | Transfer with Line 1 and 7 |
| 10 | Shunchengjie Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 11 | Dongdajie Station | Third floor underground island station | Open-cut method | Three-layer three-span box frame | 23 | The underground continuous wall | Transfer with Line 3 |
| 12 | Chengdong Road Station | Third floor underground island station | Open-cut method | Three-layer three-span box frame | 23 | The underground continuous wall |  |
| 13 | Weilaidadao Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 6 |
| 14 | Fengtai south Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 15 | Zhongzhoudadao Station | Third floor underground island station | Open-cut method | Three-layer three-span box frame | 23 | The underground continuous wall | Transfer with Line 4 |
| 16 | Tongtai Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 17 | Huanghe east Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 13 |
| 18 | Agricultural east Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 19 | Zhongxing Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 5 |
| 20 | Boxue Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 9 |
| 21 | Huanghai east Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | The terminal station of first phase of line 3 |
| 22 | Nansanhuan Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 23 | Jingba south Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain | Transfer with Line 11 |
| 24 | Jingnan 12 Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |
| 25 | Jingnan 15 Road Station | Second floor underground island station | Open-cut method | Double-layer three-span box frame | 17 | Cast-in-situ bored pile & waterproof curtain |  |

Table1.3-7 Construction Method of Interval Tunnel

| SN | Name of interval | Construction method | Structural shape of interval | Length of interval (m) | Buried depth (m) | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Xinliu Road-Shamen Road Station Interval | Shield & open-cut methods | Circular section and rectangular section | 1090 | 10-16 | Distributing area of Xinliu Road Station adopts open-cut method. |
| 2 | Shamen Road-Xinglongpu Road Station Interval | Shield methods | Circular section | 1130 | 10~18 |  |
| 3 | Xinglongpu Road -Dongfeng Road Station Interval | Shield & open-cut methods | Circular section and rectangular section | 1300 | 10~16 | Distributing area of Xinglongpu Road Station adopts open-cut method. |
| 4 | Xinglongpu Road- Agricultural Road Station Interval | Shield methods | Circular section | 980 | 10~16 |  |
| 5 | Agricultural Road- Huanhhe Road Station Interval | Shield & open-cut methods | Circular section and rectangular section | 900 | 10~11 | Distributing area of Hunaghe Road Station adopts open-cut method. |
| 6 | Huanghe Road- Jinshui Road Station Interval | Shield methods | Circular section | 900 | 10~16 |  |
| 7 | Jinshui Road- Taikang Road Station Interval | Shield methods | Circular section | 740 | 10~16 |  |
| 8 | Taikang Road- Erqi square Station Interval | Shield & open-cut methods | Circular section and rectangular section | 605 | 10~16 | Distributing area of Taikang Road Station adopts open-cut method. |
| 9 | Erqi square- Shunchengjie Station Interval | Shield methods | Circular section | 630 | 10~19 |  |
| 10 | Shunchengjie- Dongdajie Station Interval | Shield methods | Circular section | 760 | 10~11 |  |
| 11 | Dongdajie- Chengdong Road Station Interval | Shield & open-cut methods | Circular section and rectangular section | 480 | 10~16 | Distributing area of Dongdajie Station adopts open-cut method. |
| 12 | Chengdong Road- Weilaidadao Station Interval | Shield methods | Circular section | 950 | 10~16 |  |
| 13 | Weilaidadao- Fengtai south Road Station Interval | Shield methods | Circular section | 670 | 10~15 |  |
| 14 | Fengtai south Road- Zhongzhoudadao Station Interval | Shield methods | Circular section | 785 | 10~18 |  |
| 15 | Zhongzhoudadao – Tongtai Road Station Interval | Shield & open-cut methods | Circular section and rectangular section | 470 | 10~16 | Distributing area of Tongtai Road Station adopts open-cut method. |
| 16 | Tongtai Road – Huanghe east Road Station Interval | Shield methods | Circular section | 890 | 10~19 |  |
| 17 | Huanghe east Road –Agricultural east Road Station Interval | Shield methods | Circular section | 785 | 10~16 |  |
| 18 | Agricultural east Road ~Zhongxing Road Station Interva | Shield methods | Circular section | 1250 | 10~15 |  |
| 19 | Zhongxing road – Boxue Road Station Interval | Shield & open-cut methods | Circular section and rectangular section | 1520 | 10~20 | Distributing area of Zhongxing Road Station adopts open-cut method. |
| 20 | Boxue Road – Hanghai east Road Station Interval | Shield methods | Circular section | 2590 | 10~16 |  |

### 1.3.14. Quantity of Major Works

1.3.14.1. Construction Site

(1) The layout of a construction site should make full use of a station’s building land, and as far as possible, combine development plots, green belts, squares, etc, which will be used as temporary construction sites, but should be subject to consent of the municipal environmental protection and planning departments. For a location whose site layout is difficult and whose traffic volume is smaller, after a traffic police department’s approval, its roads may be temporarily closed or part of its roads may be occupied as a construction site.

(2) The construction site for an underground station normally will take about 25 thousand square meters. Each station’s geographical location is different, with a different environment and a different construction method, and some construction sites are relatively concentrated, and some are more dispersed, which requires that a construction team’s comprehensive ability be stronger and its construction management level be higher.

(3) A shield shaft should be used as the assembly shaft and construction-related earth-going shaft of a shield.

(4) In order to ensure the smooth progress of the work of laying tracks, the track laying for the Phase-1 project of Line 3 should have two track panel bases at the car depot and parking lot to facilitate the track-laying operation.

1.3.14.2. Earthwork

The total amount of earthwork of Zhengzhou’s Metro Line 3 will be approximately 4,974,000 cubic meters, of which the station excavation will be approximately 2,661,000 m3, and filling will be 293,000 m3; the interval shield soil excavation will be approximately 531,000 cubic meters, and the filling will be approximately 58,000 cubic meters; the Xinliu Road station’s car park’s dredging excavation will be a total of 120,000 cubic meters, and the filling will be 279,000 cubic meters; Hanghai East Road’s car depot’s excavation will be about 393,000 cubic meters, and the filling will be about 638,000 cubic meters. For the earthwork quantity of the project of Line 3, see Table1.3-8.

Table 1.3-8.Earthwork Quantity of Phase-1 Project of Zhengzhou’s Metro Line 3

| Item | Excavation (ten thousand cubic meters) | Filling (ten thousand cubic meters) | Total (ten thousand cubic meters) |
| --- | --- | --- | --- |
| Station | 266.1 | 29.3 | 295.3 |
| Interval | 53.1 | 5.8 | 58.9 |
| Parking lot | 12.0 | 27.9 | 39.9 |
| Car depot | 39.3 | 63.8 | 103.2 |
| Total (ten thousand cubic meters) | 370.5 | 126.9 | 497.4 |

1.3.14.3 Project Land

For the land covering situation of the Phase-1 project of Zhengzhou’s Metro Line 3, see Table 1.3-9.

Table 1.3-9 Along-the-Line of Quantity of Land for the Project:  Unit: hm 2

|  | Vegetable plot | Arable land | Orchard | Woodland | Other land | Total |
| --- | --- | --- | --- | --- | --- | --- |
| Parking lot | 5.5 | 6.4 | 0 | 0 | 2.3 | 14.2 |
| Car depot | 0 | 7.7 | 7.5 | 19.1 | 3.9 | 38.2 |
| Station |  |  |  |  | 2.9 | 2.9 |
| Interval | 0 | 0 | 0 | 0 | 0 | 0 |
| Total |  |  |  |  |  | 55.3 |

1.3.14.4 Quantity of Major Works

For the quantity of major works of the Phase-1 project of Zhengzhou’s Metro Line 3, see Table 1.3-10.

Table 1.3-10. Quantities of Major Works

| Item | Unit | Quantity | Remark |
| --- | --- | --- | --- |
| Length of line | km | 25.2 | All underground lines |
| Station | set | 21 | All underground stations |
| Car depot and parking lot | Set | 2 | Hanghai East Road’s parking lot and Xinliu Road Station and car depot |
| Main substation | Set | 1 | Boxue Road Station’s main substation |
| Demolition of buildings | m 2 | 101660 |  |
| Permanent site | Chinese acre | 829.68 |  |
| Project investment | Ten thousand yuan | 1820853 |  |

### 1.3.15 Management organization and seating capacity

This project will be managed by zhengzhou Rail Transit Co., Ltd. after completion. According to the design document and line length as well as quantity of stations, seating capacity required by operating agency of Line 3 is taken as 62 persons/km and 69 persons/station in the initial stage; and taken as 66 persons/km and 72 persons/station in short-term; and taken as 73 persons/km and 87 persons/station in long-term for calculation. According to calculation by the above principle, quantity of operating management personnel of Line 3 is 3011 in initial stage, 3175 in short-term and 3666  in long-term.

## 1.4 Purpose of Environmental and Social Management Plan

Environmental management is part of engineering management, and an important link for effective implementation of engineering environmental protection. Environment management for project of Rail Transit Line 3 of Zhengzhou City is intended to guarantee smooth implementation of various environmental protection measures of the project, and reduce the adverse influences caused by project construction on environment, guarantee smooth implementation of environmental protection in the project zone and resettlement zone so as to coordinate project construction, ecological environmental protection and economic development.

## 1.5 The preparation of the Environmental and Social Management Plan

The Environmental and Social Management Plan of Rail Transit Line 3 of Zhengzhou City is compiled based on environmental impact assessment, and the major contents include environmental management system, environmental management training, and environmental protection measures for the adverse influences during environmental impact assessment, and estimation of investment on environmental protection. At the same time, according to the measures taken against the construction and operation period’s impact to the social and natural environment,《World Bank loans Zhengzhou rail transit Line 3  project social management plan》(ESMP)is also developed  separately.

# 2 Policies, laws and regulations framework and compilation basis

## 2.1 Laws and regulations

(1) Environmental Protection Law of the People’s Republic of China (implemented on 1989.12.26)

(2) Environmental Impact Assessment Law of the People’s Republic of China (implemented on 2003.9.1)

(3) Air Pollution Prevention Law of the People’s Republic of China (implemented on 2000.9.1)

(4) Environmental Noise Pollution Prevention Law of the People’s Republic of China (implemented on 1997.3.1)

(5) Water Pollution Prevention Law of the People’s Republic of China (revised on February 28, 2008, implemented on June 1, 2008)

(6) Solid Waste Pollution Prevention Law of the People’s Republic of China (implemented on 2005.4.1)

(7) Urban and Rural Planning Law of the People’s Republic of China (implemented on 2008.1.1)

(8) Soil and Water Conservation Act of the People’s Republic of China (revised on December 25, 2010, implemented on march1, 2011)

(9) Cultural Relics Protection Law of the People’s Republic of China (implemented on 2007.12.29)

(10) Cleaner Production Promotion Law of the People’s Republic of China (implemented on 2003.1.1)

(11) Energy Conservation Law of the People’s Republic of China (implemented on 2008.4.1)

(12) State Council of the People's Republic of China (1998) Decree No. 253 Construction Project Environmental Protection Management Regulations (1998.12.12)

(13) State Council of the People's Republic of China (2001), No. 305 Urban Housing Demolition Management Regulations (2001.11.1); Ministry of Construction of the People’s Republic of China Urban Housing Units Specification for Administrative Adjudication (implemented on 2004.3.1)

(14) The People's Republic of China State Council Order No. 257 of the Basic Farmland Protection Ordinance (implemented on 1999.1.1)

(15) State [2005] No. 39 Decision to Strengthen Environmental Protection by the State Council on the Implementation of the Scientific Concept of Development;

(16) SEPA UNCED [2006] No. 28 Interim Measures for environmental impact assessment of public participation (implemented on 2006.3.18)

(17) State Environmental Protection Administration Decree 14 "Construction Project Environmental Impact Assessment Classification Catalogue (implemented on 2008.10.1)

(18) SEPA 18 orders Electromagnetic Radiation Environmental Protection Management Approach (implemented on 1997.3.25)

(19) General Office [2003] No. 81, Notice on the General Office of the State Council on Strengthening Urban Rapid Rail Transit Construction Management (2003.9.27)

(20)Implementation approaches of the Water Law of the People's Republic of China in Henan Province (come into effect since August 1st, 2006);

(21)Henan Province’s Implementation approaches of the Cultural Relics Protection Law (Amendment) (come into effect since February 23rd, 1984);

(22)Circular of Henan Provincial People’s Government on Intensifying Land Control and Strict Land Management (No.33 [2007] of the People’s Government of Henan Province)

(23)Circular of Henan Provincial People’s Government on Issuing the Five-Year Energy Development Plan (No.36 [2012] of the People’s Government of Henan Province)

(24)Opinions of the People's Government of Henan Province on Implementing the Decision of the State Council on Implementing the Scientific Development View and Strengthening the Environmental Protection (No.36 [2006] of the People’s Government of Henan Province)

(25)Circular of the People's Government of Henan Province on Issuing the Implementation Scheme for Energy Conservation and Emission Reduction (No.46 [2007] of the People’s Government of Henan Province)

(26)Notice of Designating Water Source Protection Areas on the Two Sides of Main Channel of North-South Water Transfer First-Stage Project Middle Route (No.134 [2006] of State Council North-South Water Transfer Office for Environmental Protection and Resettlement)

(27)Circular of the People's Government of Henan Province on Issuing the Implementation Opinion for the Water Source Protection Areas Designation on the Two Sides of Main Channel of North-South Water Transfer First-Stage Project Middle Route (No.32 [2007] of the People’s Government of Henan Province);

(28)Circular of Zhengzhou Municipal People's Government on Issuing the Implementation Opinion for the Water Source Protection Areas Designation on the Two Sides of Main Channel of North-South Water Transfer First-Stage Project Middle Route (No.74 [2007] of Zhengzhou Municipal Government);

(29)Zhengzhou Municipal Government’s Opinion on Implementing the Water Source Protection Areas Designation on the Two Sides of Main Channel of North-South Water Transfer First-Stage Project Middle Route & Implementation Scheme;

(30)Notification of Zhengzhou Municipal People's Government on Urban Groundwater Resources Protection and Self-supply Wells Closing (No.227 [2002] of Zhengzhou Municipal Government);

(31)Notification of Zhengzhou Municipal People's Government on Issuing the Zhengzhou National Economic and Social Development Plan of 2007 (No.13 [2007] of Zhengzhou Municipal Government);

(32)Zhengzhou Control Measures of Environmental Noise Pollution (No. 154 of Zhengzhou Municipal Government Notice);

(33) Zhengzhou Municipal Regulation on Air Pollution Control (come into effect since November 1st, 2005);

(34) Zhengzhou Water Resources Management Ordinance (come into effect since August 1st, 2003);

(35)Zhengzhou Urban Drinking Water Sources Protection and Pollution Control Ordinance (come into effect since January 1st, 2000).

## 2.2 Technical regulations and standards

- The People's Republic of China Environmental Protection Industry Standard  Environmental Impact Assessment Technology Guidelines – Master HJ/T2.1-93

- The People's Republic of China Environmental Protection Industry Standard Technical Guidelines on Environmental Impact Assessment - Atmospheric Environment HJ2.2-2008

- The People's Republic of China Environmental Protection Industry Standard Environmental Impact Assessment Technology Guidelines - Surface Water Environment HJ/T2.3-93

- The People's Republic of China Environmental Protection Industry Standard Environmental Impact Assessment Technology Guidelines - Sound Environment HJ2.4 -2009

- The People's Republic of China Environmental Protection Industry Standard "Environmental Impact Assessment Technology Guidelines - Non - ecological impact "HJ/T19 - 1997

- The People's Republic of China Environmental Protection Industry Standard Environmental Impact Assessment Of Electromagnetic Radiation Of 500kv High Pressure Transmission And Distribution Project HJ/T24-1998

- The People's Republic of China Environmental Protection Industry Standard Guidelines for Environmental Management of radiation- Electromagnetic Radiation, Environmental Impact Assessment Methods and Standards HJ/T10.3-1996

- The People's Republic of China Environmental Protection Industry Standard Division of application technical specification of environmental noise of urban area GB/T15190-94

- The People's Republic of China Environmental Protection Industry Standard Environmental Impact Assessment Technology Guidelines - Urban Mass Transit  HJ453-2008

- The People's Republic of China Environmental Protection Industry Standard Environmental Impact Assessment Technology Guidelines – Ground Water Environment HJ/T2.3-93

## 2.3 Safety insurance policies of the World Bank

In this environment impact assessment, analyze the relationship between World Bank loan part and related projects of Zhengzhou rail transit line 3 project and World Bank security policy/procedures, and list the results in table 2.3-1.

Table 2.3-1 Schedule of relationship between Zhengzhou Rail Transit Line 3 project and World Bank security policy/procedures

| Policy/procedure | Zhengzhou Rail Transit Line 3 Project |
| --- | --- |
| World Bank business policy/procedure Environment Assessment (OP/BP4.01) | Relevant |
| World Bank business policy/procedure Natural Habitats (OP/BP4.04) | Irrelevant |
| World Bank business policy/procedure Involuntary Resettlement (OP/BP4.12) | Relevant |
| World Bank business policy/procedure Pest Management Irrelevant | Irrelevant |
| World Bank business policy/procedure Physical Cultural Resources (OP4.11) | Relevant |
| World Bank business policy/procedure Dam Safety (OP/BP4.37) | Irrelevant |
| World Bank business policy/procedure Minority Nationalities (OP/BP 4.10) | Irrelevant |
| World Bank business policy/procedure Forest (OP 4.36) | Irrelevant |
| World Bank business policy/procedure International Watercourses (OP7.50) | Irrelevant |
| World Bank business policy/procedure Projects in Disputed Areas (OP7.60) | Irrelevant |
| World Bank business policy/procedure Projects in Disputed Areas (OP7.60) | Relevant |

## 2.4  2.4.2 Assessment standard

#### 2.4.2.1 Noise standard

The noise standard consulted in this assessment is shown in table 2.4-1, according to the Acoustic Environmental Function Zoning Plan of Zhengzhou City (2011) and the Confirmation of Environmental Impact Assessment Standard for Zhengzhou Metro Line 3 First-stage Project issued by the Environmental Protection Bureau of Henan Province.

Table 2.4-1 Summary table of acoustic environmental impact assessment

| Name and No. of standard | Standard value and grade (type) | Scope of application |
| --- | --- | --- |
| Environmental Quality Standard for Noise GB3096-2008 | Type 4a: Daytime 70dB Nighttime 55dB | (1) Areas of 20-50m away from the motor lane border on the road sides; (2) Areas of 50m away from the railway outer track; (3) Areas within 35m from the two sides of car depot access line. |
|  | Type 3: Daytime 65dB Nighttime 55dB | Certain distances away from the two sides of Boxue Road Station to East Hanghai Road Station (included). |
|  | Type 2： Daytime 60dB Nighttime 50dB | Certain distances away from the two sides of Jinshui Road Station to Bocue road station (included). |
|  | Type 1： Daytime 55dB Nighttime 45dB | Certain distances away from the two sides of Xinliu Road Station (included) to Jinshui road station (included) |
| Emission Standard for Industrial Enterprises Noise at Boundary GB12348-2008 | Type 1： Daytime 55dB Nighttime 45dB | 1m outside the parking lots |
|  | Type 3: Daytime 65dB Nighttime 55dB | 1m outside the car depot |
| Noise Limits for Construction Site GB12523-2011 | Type 4a: Daytime 70dB Nighttime 55dB | Construction site |

At the same time, according to General Guide on Environment, Health and Safety, the noise should not exceed relevant requirements of Table 2.4-1, or the increase of noise of the nearest receiving point outside the construction site should not exceed 3 db (A).

Containue to Table 2.4-1 General Guide on Environment, Health and Safety

| Receiver | dB (A)2/h |
| --- | --- |
|  | Day 07:00-22:00 | Night 22:00-07:00 |
| Residence, office, school | 55 | 45 |
| Industry, business facilities | 70 | 70 |

The above two tables show that the class 1 standard of Acoustic Environmental Quality Standard is the same as the standard limit of residence, office and school in General Guide on Environment, Health and Safety. The function zoning of class 2, 3, 4 standards of Acoustic Environmental Quality Standard is the same as the industry and business facilities function zoning in General Guide on Environment, Health and Safety, that is, they have same standard implementation scope. The standard limit of the class 2, 3, 4 standards of Acoustic Environmental Quality Standard is stricter than that of the industry and business facilities in General Guide on Environment, Health and Safety. So, in the process of analysis and evaluation, Acoustic Environmental Quality Standard is taken as the basis for the evaluation.

2.4.2.2 Vibration standard

(I) Executive standard

Refer to Table 2.4-2 for executive standard of vibration environmental impact assessment.

Table 2.4-2 Executive standard of vibration environmental impact assessment

| Scope of application | Daytime | Nighttime | Remarks |
| --- | --- | --- | --- |
| Residence and cultural and educational area standard | 70dB | 67dB | VLz10 |
| Mixing area and central business district | 75dB | 72dB |  |
| industrial concentration district | 75dB | 72dB |  |
| Both sides of arterial traffic standard | 75dB | 72dB |  |

(II) Reference standard

The assessment of Metro running vibration impact is carried out according to the allowable vibration velocity limits of historic brick masonry structures defined in Technical Specifications for Protection of Historic Buildings against Man-made Vibration (GB/T50452-2008), see table 2.4-3.

Table 2.4-3 Permissible vibration velocities of brick masonry structure of historic buildings

| Ancient brick structure | Level of protection | Position of control point | Direction of control point | Brick masonry VP(m/s) |
| --- | --- | --- | --- | --- |
|  |  |  |  | <1600 | 1600～2100 | >2100 |
|  | National key cultural relic protection unit | Highest position of bearing structure | Horizontal | 0.15 | 0.15～0.20 | 0.20 |
|  | Provincial level cultural relic protection unit | Highest position of bearing structure | Horizontal | 0.27 | 0.27～0.36 | 0.36 |
| Ancient stone structure | Level of protection | Control point position | Control the direction | Stone masonry VP(m/s) |
|  |  |  |  | <2300 | 2300～2900 | >2900 |
|  | National key cultural relic protection unit | Highest position of bearing structure | Horizontal | 0.20 | 0.20～0.25 | 0.25 |
|  | Provincial level cultural relic protection unit | Highest position of bearing structure | Horizontal | 0.36 | 0.36～0.45 | 0.45 |
| Ancient wood structure | Level of protection | Control point position | Control the direction | Wood masonry VP(m/s) |
|  |  |  |  | <4600 | 4600～5600 | >5600 |
|  | National key cultural relic protection unit | Top of pillars | Horizontal | 0.18 | 0.18～0.22 | 0.22 |
|  | Provincial level cultural relic protection unit | Top of pillars | Horizontal | 0.25 | 0.25～0.30 | 0.30 |

(III) Reference Standard

According to GBJ118-88 Code for Design of Sound Insulation of Civil Buildings, the primary standard of residential bedrooms, special rooms requiring quiet environment at schools and hospital wards is: the indoor noise in residences, classrooms and hospitals shall be lower than or equal to 40dB(A). As for secondary structural noise, the standard applied in the assessment is: the indoor secondary structural noise caused by vibration of subway shall be lower than or equal to 40dB (A).

"Limits and Measurement Method Standards for Urban Rail Transit Causing Secondary Radiation Noise and Building Vibration " JGJ / T 170-2009;

"Metro Noise and Vibration Control Specification" DB11/T838-2011.

#### 2.4.2.3 Water environment

The metro line passes Jialu River, Jinshui River, Xiong’er River, Weihe River, Qili River and Chaohe River, and Level IV standards of the Environmental Quality Standards for Surface Water (GB3838-2002) shall be executed here;

For the underground water environment along the Metro line, Environmental Quality Standards for Ground Water (GB/T14848-93) Level III standard shall be executed.

The sewage of the vehicle base and the stations has conditions to be included in the existing or planned drainage pipe network, entering relevant urban sewage treatment plant. The sewage discharge of the vehicle base and the stations perform the standard of urban sewage treatment plant, class 3 standard of Sewage Discharge Standard (GB8978-1996). See table 2.4-4 , table 2.4-5 and table 2.4-6 for the details.

Table 2.4-4 Executive standard of ground water environmental impact assessment ( mg /L) ( Except the pH)

| SN | items | standard value |
| --- | --- | --- |
| 1 | pH value | 6～9 |
| 2 | Do | ≥3 |
| 3 | permanganate index | ≤10 |
| 4 | COD | ≤30 |
| 5 | BOD5 | ≤6 |
| 6 | NH3-N | ≤1.5 |
| 7 | TP | ≤0.3 |
| 8 | As | ≤0.1 |
| 9 | Hg | ≤0.001 |
| 10 | Cr | ≤0.05 |
| 11 | cyanide | ≤0.2 |
| 12 | Ar-OH | ≤0.01 |
| 13 | Oil Type | ≤0.5 |
| 14 | sulfide | ≤0.5 |

Table 2.4-5Standard of ground water Quality Standard ( mg /L)( Except the pH)

| items | standard value | items | standard value |
| --- | --- | --- | --- |
| pH | 6.5～8.5 | Mn | ≤0.1 |
| Total hardness | ≤450 | Cu | ≤1.0 |
| Total soluble solids | ≤1000 | Pb | ≤0.05 |
| CODMN | ≤3.0 | Zn | ≤1.0 |
| fluoride | ≤1.0 | Cd | ≤0.01 |
| Nitrates | ≤20 | Cr+6 | ≤0.05 |
| Nitrites | ≤0.02 | Hg | ≤0.001 |
| sulfate | ≤250 | As | ≤0.05 |
| ammonia nitrogen | ≤0.2 | Total Plate Count (个/mL) | ≤100 |
| Ar-OH | ≤0.002 | The total coliforms (个/L) | ≤3.0 |
| Fe | ≤0.3 |  |  |

Table 2.4-6 Integrated Wastewater Discharge Standard

| Primary standard value | pH value | SS (mg/L) | BOD5 (mg/L) | CODCr (mg/L) | Oil (mg/L) | Animal and vegetable oils (mg/L) | Ammonia nitrogen (mg/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Level three | 6-9 | 400 | 300 | 500 | 20 | 100 | / |

2.4.2.4 Ambient air

(I)According to ambient air quality functional zone classification, the project site belongs to the class 2 area, so within the scope of the evaluation, the ambient air quality standard is level 2 standard of Ambient Air Quality Standard (GB3095-2012). See Table 2.4-7for standard values.

Table 2.4-7 Level 2 Standard of Ambient Air Quality Standard (GB3095-2012)

| SN | Pollutants | secondary standard mg/Nm3 | The standard source |
| --- | --- | --- | --- |
|  |  | annual mean | daily mean | hourly mean |  |
| 1 | SO2 | 0.06 | 0.15 | 0.5 | standard of Ambient Air Quality Standard （GB3095-2012） |
| 2 | NO2 | 0.04 | 0.08 | 0.2 |  |
| 3 | Nitrogen oxides | 0.05 | 0.1 | 0.25 |  |
| 4 | TSP | 0.2 | 0.3 |  |  |
| 5 | PM10 | 0.07 | 0.15 |  |  |
| 6 | PM2.5 | 0.035 | 0.075 |  |  |
| 7 | CO |  | 4.0 | 10.0 |  |

(II) Emission Standard for Odor Pollutants (GB14554-93) is referred and implemented for air exhaust of ventilation system of stations.

(III) For construction dust, execute the Fugitive Emission Limit Values in " Integrated Standards of Air Pollutant Emission " (GB16297-1996) that is, particulate matter 1.0mg / m 3.

2.4.2.5 Electromagnetic radiation

(I) The strength of power frequency electric field and magnetic field of power transmission and transfer facilities is in accordance with stipulations in Technical Regulations on Environmental Impact Assessment of Electromagnetic Radiation Produced by 500 KV Ultrahigh Voltage Transmission and Transfer Power Engineering (HJ/T24-1998), it’s recommended that take 4kV/m as the assessment standard for power frequency electric field of residential area and take 0.1mT which is the power frequency limit value for public being exposed all day long stipulated by National Radiation Protection Association as the assessment standard for magnetic induction.

(II) For impact of electromagnetic interference at entrance-exit ground section on quality of television reception, take the damage measuring method recommended by International Radio Consultative Committee (CCIR) as reference, and the assessment standard is 35dB higher than signal to noise ratio.

# 3 Environmental Management System

## 3.1 Set of Environmental Management System

Environmental management for phase I project of Rail Transit Line 3 of Zhengzhou includes external management and internal management. The management period is divided into three phases of first phase of construction, construction period and operation period.

(1) External management: Various environmental management administrative departments and World Bank will carry out external management, and will determine the corresponding standards and requirements environmental protection of the construction project shall reach based on the relevant World Bank and state laws and rules, take charge of irregular supervision, inspection of work in various phases, and completion acceptance etc. of the environmental protection project.

(2) Internal management: The owner shall take charge of organizing implementation of internal management, and optimize, organize and implement environmental protection measures of the project, and guarantee the requirements of environmental protection for World Bank and state construction project, and local environmental protection department are reached. The internal environmental management system of the project is managed by the owner, supervisory unit (project supervisory unit) and contractor respectively. Meanwhile, the design unit, environment assessment unit, risk consultation unit, safety monitoring and environment monitoring unit shall actively cooperate in the work, and subject to the supervision of World Bank.

3.1.1 Environment management system in first phase of construction of project

The environment management in first phase of project construction is mainly implemented by Zhengzhou Rail Transit Group Co., Ltd. and coordinated by environment assessment unit and design unit and also supervised by Ministry of Environment Protection, Provincial Environment Protection Bureau, Zhengzhou Municipal Environment Protection Bureau and World Bank.

3.1.2 Environment management systems in construction period and operation period

The details of management systems in construction period and operation period see figures 3.1-a and 3.1-b. The responsibilities of all organs of management system

Refer to tables 3.1-a and 3.2-b.

Risk consultation unit	The third party environment monitoring unit	Safety supervision agency		Engineering management agency		Safety supervision agency

Figure 3.1-a Environmental Protection Management System of Phase I Project of Rail Transit Line 3 of Zhengzhou in Construction Period

Figure 3-1-b Environment protection system of phase I project of No.3 rail of Zhengzhou in operation period

## 3.2 Environmental Management Organ, capability and Duties

### 3.2.1 Environmental Management Organ, Capability and Duties in First Phase of Project Construction

Organ and personnel: in first phase of construction, the owner unit is the main body of environment management. In first phase of construction, the owner unit assigns a full-time or part-time environment protection management staff to take charge of coordinating environmental protection in the first phase of project construction.

Capacity requirements: the environment management staff shall graduate from major related to civil engineering and have received environment management training, have environment management qualification and participate in No.1 line project environment management, and have related experiences of subway project environment management.

Duties: ① Protect the benefits of the units subject to land requisition and resettlement and the residents during land requisition and relocation. The owner unit shall strictly comply with state and Zhengzhou city resettlement regulations and determine reasonable compensation and setting modes for the units and residents subject to the relocation.

② Entrust the environment assessment unit to prepare the environment assessment report to conduct environment impact prediction and evaluation in project construction period and operation period and put forward various environment assessment measures; the preparation of report shall meet the requirements of World Bank, state and local environment protection laws and regulations and related technical policies. Through the implementation of measures in report in the design documents by the design unit and including the environment protection project investment into the project estimate (budget), it can realize the requirements for “simultaneous design” in “three simultaneously” in environmental protection project.

③ The construction unit shall attach equal attention to environmental protection project and the major project during project contracting, and make it definite in the tender of the engineering construction. In addition, it shall put forth requirement for environmental protection to the construction organizational program of the construction unit, and give priority to the construction unit and team with strong sense of environmental protection, better achievements in environmental protection and stronger capacity to lay foundation for civilized construction, and “simultaneous construction” with high quality in environment protection.

### 3.2.2 Environmental Management Organ, capability and Duties in construction period

The environment management in construction period consists of three parts of owner unit environment management, project supervision unit  and contractor environment management, and is also supervised and inspected by World Bank, Ministry of Environment Protection, Principal Environment Protection Bureau and Zhengzhou Municipal Environment Protection Bureau, in which the contractor is the implementation unit of various environment protection measures in this phase, and the design unit, environment assessment unit, risk consultation unit, safety monitoring and environment monitoring unit shall actively cooperate in the work and provide the services.

3.2.2.1 Environment management of owner unit

Organ staff: In project construction period, the owner unit shall assign 2 full-time environmental protection managerial persons to take charge of environmental management and environmental supervision in construction period, and also of disposing complaints toward environmental problems.

Capacity requirements: the environment management staff shall graduate from major related to civil engineering and have received environment management training, have environment management qualification and participate in No.1 line project environment management, and have related experiences of subway project environment management.

Duties: urge the contractor to establish and improve the construction management institutions and system, encourage the contractor to fulfill the construction environment management according to ISO14001 environment management system (EMS) and safety and health management according to 18000 occupational safety and health management system; from global view, timely master the construction environment protection tendencies of entire line; regularly check and summarize the implementation conditions of environment protection measures and fund utilization conditions; actively organize and solve in case of major environment protection issue or dispute and assist the contractors to deal with the relationships with the environment protection department, the public and the interested parties.

3.2.2.2 Environment management of project supervision unit

The project supervision unit mainly takes charge of project supervision works and the supervision and implementation of project risk prevention measures in construction period. The supervision unit shall consider various environment protection works and measures specified in EA, ESMP, environment protection works design documents and construction contract as the main contents of supervision works, strictly control the environment protection works quality and supervise the implementation of various environment protection measures by the contractor. The project supervision agency of this project designates a full-time environment supervision engineer which is directly led by general supervision engineer.

(1) Purpose of Environmental Supervision

Carry out environmental supervision during construction period according to requirements for design of environmental protection during project construction, and comprehensively supervise and inspect implementation and effect of the environmental protection measures by the contractors, dispose of and solve environmental pollution accidents in time; Meanwhile, the supervisory achievements during the construction will be taken as the basis of acceptance inspection for development project, and the necessary special report in the acceptance inspection report.

(2) Duties

Environmental supervision is an important part of project supervision during project construction, and the main duties are as follows: carry out environmental supervision over implementation of the environmental protection measures during the project construction period and operational period, and supervise, inspect and manage the environmental protection by the project contractor and professional parts of the environmental protection project; supervise, review and assess the implementation of various environment protection measures by the contractor according to the contract provisions and national laws, regulations and policies of environment protection as well as the environment monitoring data and inspection results; timely find out and correct the construction actions against the environment protection provisions in the contract and national environment protection requirements.

In this project, the main contents of supervision works are as follows: carry out supervision and inspection of environmental protection of all contractors on the construction site and residential camps, for example the implementation of noise reduction measures on construction site, handling measures of construction spoil and construction wastes, treatment measures for production wastewater, sprinkling and dedusting measures, waterproof and water stop measures for construction in station and section, environment control device noise reduction measures, underground section vibration reduction measures, ground traffic dispersion measures, land requisition and relocation measures, compensation measures, construction risk and geologic risk preventive measures in construction period, EHS protection measures in construction period and material culture resource protection measures in construction period; The main duties should include supervision of geologic risks in construction period and risks due to construction accident, and the management and implementation of risk prevention when passing through major municipal works. at same time, the effectiveness of measures can be the ground to bring forward correction requirements to the contractor under the coordination of the third party environment monitoring agency and safety monitoring agency and in reference to the monitoring data provided by them (such as construction period noise, raise dust, vibration, production sewage drainage, underground water level and ground settlement) (see table 3.4-1 – 3.4-3 for details).

The working methods are as follows:

① Dispatch supervisors to carry out site inspection and monitoring of the construction area and residential area of the contractors, and comprehensively supervise and inspect implementation of environmental protection measures, and put forth rectification requirements within a prescribed time limit to the unqualified items below the standard, and compile environmental supervision diary for project construction.

② Assist environment management organs and relevant departments in disposing of environmental pollution and environmental disputes caused by the project according to the environmental protection laws, rules, engineering design documents and project contracts.

③ Compile weekly, monthly and annual report on environmental supervision, and put forth significant environmental problems and proposals on solution to the problems. Delivery the environment supervision report after construction completed.

④ Participate in acceptance inspection during project construction and completion acceptance;

(3) Management Organ and Working Methods

Environmental supervision is an important part of environmental management, and is relatively independent. Thus independent environmental supervisory organ shall be established. Such function shall be undertaken by unit with supervisory qualification, which will supervise, examine and assess implementation of various environmental protection measures of construction unit according to the contract provisions, the requirements of state environmental protection laws, rules and policies, and the environmental monitoring data and results of circuit inspection. Discover and rectify construction in violation of environmental protection provisions under the contract, and the requirements of state environmental protection provisions.

1 full-time/part-time environmental protection supervisor under the leading of general supervision engineer will be assigned for each bid section according to the particularity and complexity of special environment supervision of this project and the specialty requirements. The environment supervisor shall have received environment protection training, have participated in No.2 environment management training and have the capacity of environment management.

Establish level I linear supervisory organizational organ according to the characteristics of the project: See Figure 3.2-1 for the supervisory organizational organ:

3.2.2.3 Contractor environment management in construction period

Staff: The contractor shall assign 2 full-time/part-time personnel for each bid section to take charge of the environment protection works in construction period.

Capability requirements: engineering technical personnel received environment protection training and that with training plan and having certain capability and qualification.

Duties: assume related duties and rights and make full use of frontline environment protection supervision duties; implement environment management responsibility system and environment protection assessment system; ensure the construction progress with the environment protection measures taken according to related state environment protection laws, EA and ESMP; strictly comply with the environment protection contents specified in contract provisions and bid/bidding documents; implement the environment protection tasks assumed by the contractor.

Detailed working tasks: for example the implementation of noise reduction measures on construction site, handling measures of construction spoil and construction wastes, treatment measures for production wastewater, sprinkling and dedusting measures, waterproof and water stop measures for construction in station and section, environment control device noise reduction measures, underground section vibration reduction measures, ground traffic dispersion measures, land requisition and relocation measures, compensation measures, construction risk and geologic risk preventive measures in construction period, EHS protection measures in construction period and material culture resource protection measures in construction period;

The working methods are as follows:

A. Formulate annual work plan on environmental protection

B. Inspect construction progress, quality, operation and testing of environmental protection facilities and dispose of problems during implementation:

C. The contractor shall communicate and consult with the masses in the project area, and establish bulletin in each construction unit to inform the public of the specific construction activities and construction time during construction; Meanwhile, the contractor shall provide information on the contact person and telephone number so that the public may complain or put forth proposal for the construction activities.

D. Account use of annual environmental protection expenses

E. Report information on implementation of environmental protection provisions under the contract; require the contractor to monitor its environmental activities, and provide 1 record report on environmental achievements every day or every week; The project office and construction supervision team will supervise and examine such records.

3.2.2.4 Environment management of environment consultation agencies in construction period

The environment consultation agencies in construction period include design unit, environment assessment unit, risk evaluation and consultation unit, environment monitoring unit and safety monitoring unit; their mainly duties are as follows: assigned by the owner, provide related consultation services and conduct site monitoring; provide data support and technical support for environment management of construction unit and supervision unit. The detailed working contents refer to table 3.1-a.

### 3.2.3 Environment management agencies, capabilities and duties in operation period

The environment management in operation period is responsible by Zhengzhou Rail Operation Management Company which is the subordinate unit of Zhengzhou Rail Transit Company. At same time, Zhengzhou Rail Operation Management Company entrusts environment monitoring unit to conduct long term monitoring for noise, vibration and waster water generated from No.3 line operation.

Staff and capability requirements: in project operation period, Zhengzhou Rail Operation Management Company shall assign a full-time environment protection management staff to take charge of environment protection works during project operation period of line 3, of which the works are directed and supervised by Ministry of Environment Protection, Henan Provincial and Zhengzhou Municipal Bureau of Environment Protection. The full-time environment management staff shall have received environment management training with related environment management qualification, and have been engaged in line 1 project environment management and have related experiences in subway project environment management.

Duties: take charge of environmental management of the whole company and external environmental management; do well in education and publicity to improve the awareness of environmental protection and technical levels of managerial personnel and staffs at various levels; formulate environmental management methods and operational regulations for pollution prevention and control facilities during operational period of the rail transit, regularly maintain, inspect and repair sewage treatment equipment, and noise control measures for air kiosks etc. to guarantee normal operation thereof. Cooperate with the environmental protection authority in environmental management, supervision and inspection; cooperate with the environmental protection authority in disposal of various environmental pollution accidents etc.

According to the characteristics of environmental impacts of the project and the assessment results of the report, the key points in environmental management during operational period of the project are as follows: noise monitoring and management for the environmental control equipment of the underground stations and noise in other sections; monitoring and management of the impacts on the environmental quality by the vibration of the train in underground sections along the project line; management of the depots and comprehensive drainage facilities on the base, and monitoring of the disposal effect.

### 3.2.4 Environment supervision and management of World Bank and environment protection government agencies

The World Bank, Ministry of Environment Protection, Provincial Environment Protection Bureau, Zhengzhou municipal environmental protection bureau and the environmental protection bureaus in various districts shall carry out external management, regular and irregular inspection of implementation of environmental protection facilities of Rail Transit Line 3 to guarantee implementation of various environmental protection measures of Rail Transit Line 3; Meanwhile, pay attention to the environmental protection problems reflected by the public toward Rail Transit Line 3, and mainly supervise and inspect such problems reflected by the public.

The project environment management systems and duties in construction period and operation period refer to table 3.2-1-a and table 3.2-1-b.

Table 3.2-1-a Agencies and duties of environment management system in construction period

| Agency nature | Agency name | Agency duties |
| --- | --- | --- |
| External environment management | Supervision agency | State Environmental Protection Administration, Provincial and municipal environment protection bureau | Governmental administrative supervision and management agency; take charge of the environment protection works at each phase of entire project |
| Internal environment management | Management agency | World Bank Load Project office for Zhengzhou Rail Transit No.3 line phase 1 project | Take charge of the environment protection works at each phase of entire project |
|  |  | Zhengzhou Rail Transit Group Co., Ltd. | Owner unit, take charge of the environment protection works of each phase, including the environment protection management works from start of construction to completion acceptance; take charge of the environment protection management responsibilities of entire project area |
|  | Supervision agency | World Bank | Supervise and check the implementation of environment management plan |
|  | Implementation agency | Contractor | Implementation agency; implement various environment protection measures in EA and ESMP. Include: implementation of noise reduction measures, vibration reduction measures, water pollution prevention measures, atmosphere pollution prevention measures, traffic dispersion measures, construction soil and construction waste disposal, construction staff health and safety protection measures. |
|  | Consultation service agency | Supervision agency | Entrusted by the owner unit, take charge of supervision and management of contract environment protection measures, including implementation of noise reduction measures, vibration reduction measures, water pollution prevention measures, atmosphere pollution prevention measures, traffic dispersion measures, construction soil and construction waste disposal, construction staff health and safety protection measures; at same time supervise the implementation of environment monitoring such as underground water level, waste water quality, construction noise, vibration, raise dust and ground settlement, and prepare environment monitoring report;take charge of supervision and management of geologic risk and safety management, construction accident risk and safety management and environment risk of contractor in construction period, and prepare the safety supervision report. |
|  |  | Design unit | Through design in construction phase, implement various environment protection measures in EA and EMSP into the design documents, and instruct the construction activity of contractor. |
|  |  | Environment assessment unit | Entrusted by the owner unit, provide explanation and related technical support for various environment protection measures put forward in EA and ESMP. |
|  |  | Environment monitoring unit | Entrusted by the owner unit, complete various environment monitoring such as noise, vibration, production waste water and raise dust brought forward in construction period, and prepare the safety monitoring report. |
|  |  | Safety monitoring unit | Entrusted by the owner unit, complete the monitoring including underground water level, ground settlement and building settlement provided in EA and ESMP in construction period, and prepare the safety monitoring report |
|  |  | Risk evaluation and consultation unit | Entrusted by the owner unit, prepare project risk evaluation report; provide technical support for various risk management measures mentioned in project risk evaluation report, EA and ESMP. |

Table 3.2-1-b Composition agency of environment management systems in operation period

| Agency nature | Agency name | Agency duties |
| --- | --- | --- |
| External environment management | Supervision agency | State Environmental Protection Administration, Provincial and municipal environment protection bureau | Governmental administrative supervision and management agency; take charge of the environment protection works in project operation period |
| Internal environment management | Management agency | World Bank Loan Project office for Zhengzhou Rail Transit No.3 line phase 1 project | Take charge of the environment protection works in project operation period |
|  |  | Zhengzhou Rail Transit Group Co., Ltd. | Owner unit, take charge of the environment protection works in project operation period; take charge of the environment protection management responsibilities of entire project area |
|  | Supervision agency | World Bank | Supervise and check the implementation of environment management plan |
|  | Implementation agency | Zhengzhou Rail Operation Management Company | A subordinate unit of Zhengzhou Rail Transit Group Co., Ltd.; noise monitoring and management for the environmental control equipment of the underground stations and noise in other sections; monitoring and management of the impacts on the environmental quality by the vibration of the train in underground sections along the project line; management of the depots and comprehensive drainage facilities on the base, and monitoring of the disposal effect |
|  | Consultation service agency | Environment monitoring unit | Entrusted by the owner unit, complete the environment monitoring such as noise and vibration put forward in EA and ESMP in construction period; prepare environment monitoring report. |

## 3.3 Environmental Management Training

3.3.1 Purpose of Training

It is necessary to carry out training on environmental protection and skills and training of environment management measures in EA and ESMP for the employees engaged in environment management and supervision of owner unit, supervision unit and contractor for smooth and effective implementation of the project so as to enable them fully understand and learn the environment protection of project, and cultivate the capability for environment management and supervision of line 3 and provide personnel and technical guarantee for the implementation of various environment protection measures in EA and ESMP.

3.3.2 Objects of Training

Personnel engaged in line 3 environment management and supervision of owner unit, supervision unit and contractor.

3.3.3 Contents of Training

The major contents of training involve environmental protection laws, environment protection technologies, EA and ESMP environment management measures, environment monitoring technologies and etc.

3.3.4 Training Plan

In first phase of construction, the owner unit shall organize the environment awareness training for all staff of related departments; in construction period, organize the employees on important posts including construction site management staff in owner unit, engineering supervision unit, contractor project manager and site environment protection responsible personnel to participate in environment management knowledge training; organize related personnel of rail company and contractor directly participating in management to attend the environment management skill training; in operation period, organize rail company environment protection management personnel for special training on environment management in operation period.

See Table 3.3-1 for the specific training plan

Table 3.3-1 Training Plan

| Project phase and training organization agency | Training organization agency | Training teacher |  | Contents of Training | Training objective | Training Time | Training Expenses |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Construction period | Zhengzhou Rail Transit Group Co., Ltd. | Famous experts engaged in environment protection specialty for long time, and familiar with World Bank environment protection policy, especially for subway construction technology | 3 persons of owner unit, 5 persons of project supervision unit per bid section; 5-10 persons of contractors per bid section | Related environmental protection laws in construction period; related construction spoil, noise, vibration, underground water, construction waster water, raise dust pollution control measures, impact on traffic, resident livings, resident income and vulnerable groups in construction period and relief measures, construction risk management measures in construction period, project geologic risk control measures in construction period, EHS, public participation, noise in construction period, construction waste water, vibration, TSP, underground water and ground settlement and other environment monitoring technical contents. | Fully understand the environment protection of subway project in construction period; learn the capability for environment management and supervision for line 3, and provide personnel and technical guarantee for implementation of various environment protection measures of EA and EMSP. | 2~3 Day | 150,000 yuan |
| Operation period | Zhengzhou Rail Transit Group Co., Ltd. | Famous experts engaged in environment protection specialty for long time, and familiar with World Bank environment protection policy, especially for subway operation period environment impact features. | 2 persons for Zhengzhou Rail Transit Group Co., Ltd., 3 persons for Zhengzhou Rail Operation Co., Ltd. | Related environment protection laws, standards and technical systems such as wastewater drainage, operation noise and vibration in operation period; odor and waste water monitoring and control technology in operation period, noise, vibration and electromagnetic monitoring and control technology. | Full understand the environment impact after subway operation and the adopted environment protection measures; get familiar with related environment monitoring technology and ensure normal operation of various environment protection facilities. | 3～4 Day | 50,000 yuan |

## 3.4 Abstract of Environmental Protection Measures

See Table 3.4-1 and Table 3.4-2 for summary of the environmental protection measures:

Table 3.4-1 List of Common Mitigation Measures for Environmental Impacts by Phase I Project of Rail Transit Line 3 of Zhengzhou Funded with the Loan of the World Bank

| Phase | Environmental Factors | Measures | Implementation Organ | Supervisory Organ | Monitoring Organ | Monitoring Items | Expenses(10,000 Yuan) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Feasibility Study and Design | Natural Environment | Ecological Environment | (1) Comprehensively consider the means of paving of the line, and the principle of occupying less arable fields and green land during selection of the route to reduce impact on urban ecological environment; (2) Carry out landscape design for the air kiosks, entrance and exit to make it compatible with the style of the surrounding buildings; (3) For the landscape design around car depot & integrated base and main substation, the greening shall give priority to local native plants and also the fruit trees, but favorable for evergreen and flower species, and dynamically combine the arbors, shrub, flowers and grassland with proper colors and pattern combination so as to form a beautiful seasonal landscape. | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Environmental Vibration | (1) In case the underground routes must run through the ground buildings and residential areas, the depth thereof shall be duly increased if conditions permitting to reduce vibration and nose, and interference with the ground buildings; | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Sound Environment | (1) Carry out noise control from the sonic source, and select low-noise equipment and structural type (2) Rationally plan the functional division of the land along the project line according to urban upgrading and planning, optimize layout of buildings, and avoid new environmental problems (3) Scientifically plan the layout of the buildings, and the first row of the buildings near the noise source shall be planned to be non-noise sensitive buildings such as commercial venues and offices etc.; (4) Dismantle residential houses near the sonic source first according to upgrading of the old urban areas; reserve noise prevention distance for the newly-developed houses or make use of the shielding and sound-isolation function of the non-sensitive buildings according to greening design and relocation of the buildings to put the impact on the sensitive buildings within the permitted scope under the standard; | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Electromagnetic Environment | (1) It is requested to carry out rational layout of the major transformer substation, and rational planning of the surrounding land of the major transformer substation to keep the enclosure walls thereof far away from the residential area(at least 15 meters to the residential area) | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Solid waste | (1) Explicitly prohibits the procurement of equipment containing polychlorinated biphenyls material in transformers and other equipment in the design and tender documents. | Design Unit | Project Owner Local Environmental Protection Bureau |  |  |  |
|  | Social Environment | Resident’s Life | (1) The principle of route selection is to reduce resettlement and impact on residents’ life as much as possible; (2) Do well in various preparatory work before construction, and carry out detailed survey of the roads, various underground pipelines such as power supply, telecommunication, water supply and drainage pipelines etc. along the subway line; Determine the resettlement and relocation program with relevant departments in advance; Do well in various emergency preparatory work to reduce impacts on residents’ life. | Design Unit | Project Owner |  |  | calculated into design fee |
|  |  | Traffic | (1) The routes plane shall be constructed along the urban arteries and deployed within the planned red lines of the roads. The station routes shall be parallel to the planned red lines. Reduce interference with ground traffic in addition to considering the station positions and construction methods. (2) Distribution of stations is determined after considering the major concentration points of passenger flow, and coordination with the urban comprehensive planned traffic network to attract passenger flow as much as possible, provide convenience for travel by passengers and really embody the principle of human paramount. | Design Unit | Project Owner |  |  | calculated into design fee |
|  |  | Protection of Disadvantaged Group | (1) Non-barrier passage for the disabled shall be established at various stations; (2) The toilet cesspit for females shall be increased according to due proportion at various stations. | Design Unit | Project Owner |  |  | calculated into design fee |
|  |  | Human Health | (1) It shall be definitely prohibited that the relevant materials such that contains Polychlorinated Biphenyls during purchase of the equipment of transformer substation; (2) Non-poisonous pesticide and herbicide with low residue shall be used during greening of the depots and transformer substation. |  |  |  |  |  |
|  | Material Cultural Resources | Cultural Relics | (1) As for landscape design for the sections adjacent to historical and cultural areas and protected cultural relics, the dimension, height and color design shall be compatible with the surrounding environment, especially the features and customs of the scenic area. (2) Entrust qualified unit to carry out detailed prospecting of cultural relics along the rail transit line before project construction, and avoid and protect the ancient ruins and underground buried substances discovered during prospecting and unlisted in the list of protected cultural relics at present; (3)Do well in protection of protected cultural relics and underground burial site of cultural relics before project construction, formulate specific protection program, and report to local cultural relics authority and planning department for approval. | Design Unit | Project Owner Local Environmental Protection Bureau Cultural Relics Bureau |  |  | calculated into design fee |
| Construction Period | Natural Environment | Sound Environment | (1) It is forbidden to carry out construction operation that produces environmental noise pollution at night in the concentrated area of buildings sensitive to noise in the urban areas; In case continuous operation is to be carried out due to special needs, “Nighttime Construction License” shall be handled for nighttime construction, and the approved nighttime operation shall be publically notified to the adjacent residents. (2) It is forbidden to drive pile at night. In case it is really necessary to do so, it shall be reported to Zhengzhou Municipal Environmental Protection Bureau for approval, and restrict operational time within the scope of 7:00-12:00 and 14:00-22:00. (3) The machinery with high noise such as power generator and air compressor etc. in the secluded place or inside the tunnel if possible, and keep them far away from sensitive points in sound environment such as residential area, school and hospital etc.. (4) The transport vehicles shall be enter into and get out of the construction site on the side far away from the residential area (5) Use commodity concrete, and no concrete mixer shall be placed on the construction site; (6) Incorporate measures to reduce environmental noise pollution as the contents of construction organization and design during tender invitation for the construction project, and make definite in the contract signed. (7) In addition to strict control of various sources of environment noises according to the relevant state environmental noise standards during the college entrance examination and half a month before the college entrance examination, it is forbidden to carry out construction operation that produce noise beyond standards and interfere with people’s life. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Environmental Vibration | (1)The operational rotues of the construction vehicles, especially heavey transport vehicles shall avoid areas sensitive to vibration if possible. (2)High vibration operations will be carried out in periods with a high environmental vibration background value(7:00～12:00，14:00～22:00), and construction operations with strong vibration and serious pollution will be restricted during night.(3)As for sections where shield tunneling construction is adopted, detailed survey shall be carried out toward the sensitive points near the tunnel, and keep records well and take preventive measures such as consolidation toward influences such as cracking of houses and ground settlement etc..(4) During construction period, prepare complete monitoring program for culture relics and ancient architectures affected, focus on the monitoring of their settlement, tilting and crack development, define the pre-alarm value, alarm value and control value and prepare the construction emergency plan;(5) Renovate the key buildings in advance; conduct the retaining protection for the building with poor stability;(6) Except reasonable adjustment of parameters such as soil chamber pressure, jack pushing force and grouting pressure during shield propelling, reduction of disturbance for surrounding soil mass as possible and control of surrounding stratum deformation, conduct grouting reinforcement for stratum around the ancient building foundation if necessary so as to enhance the bearing capacity and further control the ancient building deformation. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Atmospheric Environment | (1)Hard enclosure shall be established on the construction site, and the major roads shall be hardened and kept clean. (2)Special personnel shall be established for the environmental protection on the construction site. Corresponding sprinkling equipment shall be equipped to sprinkle water in time and reduce dust pollution. (3)Duly spray water when dismantling and digging dry earth ground to keep certain humidity of the operational surface. (4)The rubbish and residual earth produced during house dismantlement shall be cleaned away and transported within 3 days after dismantlement of the house, and the residual earth piles and exposed ground left over for over 2 days shall be covered with dust-proof cloth or solidified to prevent dust. (5)The vehicles transporting rubbish, residual earth and sands shall obtain “permit for transport vehicles of residual earth and sands”. The transport trucks shall be well sealed withtout leakage, and shall not be excessively full during loading to guarantee no littering during transport. In case of littering during transport, cleaning shall be carried out in time to reduce pollution. (6)Explosion, dismantlement, earth and stone operation and manual dry sweeping shall be not carried out in case of dry weather with air pollution index above 100, or strong wind above level 4. In case of air pollution index between 80-100, cleaning shall be carried out every 4 hours with alternative of sprinkling and cleaning. And denser cleaning shall be carried out in case the air pollution index is larger than 100. (7)Establish washing platform inside the gate of the construction site. The washing operational ground and the roads connecting the entrance and exit must be hardened. Frequently wash the earth on the transport vehicles and chassis. The operational vehicles shall clean the earth on the wheels when running out of the boundary to reduce earth carried by the wheels. | Construction Unit | Project Owner Local Environmental Protection Bureau | The owner entrusts qualified organ to undertake the work by means of contract. | TSP | monitoring expenses(200,000 yuan); The other expenses are calculated into engineering fee |
|  |  | Water Environment | Ground Water | (1) Do well in design of drainage system on the construction site during the construction period. The excretion sewage of the construction personnel shall be collected and disposed of by the environmental health personnel regularly. (2) Establish sediment tank at the drainage outlet on the construction site, and the construction sewage shall be recycled for washing or greening the site through sediment disposal. The construction slurry in shield tunneling shall be totally recycled through disposal by the mud-water separation system. | Construction Unit | Project Owner Local Environmental Protection Bureau | The owner entrusts qualified organ to undertake by means of contract | pH, SS, Oil, , COD | monitoring expenses(150,000 yuan); The other expenses are calculated into engineering fee |
|  |  |  | Underground Water | (1)Establish septic tank in the construction camp, and equip with anti-leakage measures to prevent pollutionon the underground water; (2)The domestic rubbish produced during construction period shall be collectively managed, and handed over to the municipal environmental health department for collective disposal to prevent pollution on the underground water source. (3)The digging construction scale of the base pit of underground station is large, and the adverse factors that influence the stability of base pit shall be comprehensively considered, and suitable protective measures shall be adopted to ensure the safety of the base pit construction, surrounding road, underground pipelines and buildings. (4) Strengthen construction monitoring, and carry out close monitoring over the enclosure structure of the base pit, horizontal and vertical movement of the sourrounding buildings, the changes of stress on the enclosure structure and underground water level, and earth pressure； | Construction Unit | Project Owner Local Environmental Protection Bureau | The owner entrusts qualified organ to undertake by means of contract | Underground water level, ground settlement extent, water quality | monitoring expenses(600,000 yuan); The other expenses are calculated into engineering fee |
|  | Ecological environment | Vegetation greening | (1) Carry out necessary restoration and compensation for the green land occupied, and restore its ecological functions as soon as possible. (2) Protect the vegetation in the land requisitioned and areas along the line during project construction, and reduce damage to the woods, grass land and bushes in the land temporaily used, and around the operational zone. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | Water and soil erosion | (1)The construction unit shall formulate construction organizational plan for the earth and stone project according to the climatic features and characteristics of rainfall in the area. The construction unit will avoid the rainy season to carry out large-scaled earth and stone project; And it will make out water and soil conservation measures during construction of earth and soil project; (2) The construction deserted dregs will be cleaned and transported in time, and the road base surface built will be stamped solid; Properly carry out protective measures; | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | Solid wastes | (1)The construction unit will sign construction rubbish transport contract with the company engaged in transport of construction rubbish, and apply for approval certification for disposal of construction rubbish.(2)The construction unit shall be equipped with managerial personnel to carry out site management of the disposal of dregs and rubbish. The vehicles transporting dregs shall be equipped with sealed cover, and shall run according to the prescribed time, site and routes.(3)The residual earth site shall be leveled in time, and be equipped with drainage pitches etc. to prevent water and soil erosion. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  | Social environment | Traffic evacuation | (1)Strengthen tariffic management during construction period and rationally arrange construction program to carry out construction with less road occupied and speed up construction progress through making out detailed traffic evacuation program during open digging of stations that influences traiffc. | Project owner | Project Owner Municipal Government |  |  | calculated into engineering fee |
|  |  | Resident income | (1)Compensation and reward measures will be taken for the impacts on resident income due to occupation of agricultural fields, and income of the businesses and relevant employees respectively. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | Resident Living | (1) Carry out survey of the roads, various underground pipelines along the subway line; Determine the resettlement and relocation program with relevant departments in advance; (2) Establish enclosure on the construction site to lower impacts on residents’ life due to construction noise; sprinkle water to reduce dust on the construction site, and the odd construction materials shall be covered to reduce impacts due to dust. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | traffic accessibility | Each station are set straight ladder, provide convenient for people with more bags | Design Unit | Project Owner |  |  | calculated into design fee |
|  |  | Human Health | (1)Carry out immunity injection for the construction personnel to improve health and prevent infection; carry out regular physical check for the construction personnel. (2)Strictly carry out working and rest system for the construction personnel operating equipment with high noise and vibration, guarantee sufficient rest, and shall not alternate shifts and work overtime except on special occasions. (3)The workers shall wear masks during tunnel construction. The ventilation system in the tunnel shall be kept in normal working state to guarantee sufficient amount of ventilation. Construction inside the tunnel shall be stopped in case the ventilation system is damaged. (4)Environmental protection materials shall be used during decoration of the tunnel and subway station, and the content of formalin therein shall meet the requirements of relevant standards. (5)The constructors shall wear corresponding gas masks and gloves during installation of the equipment of transformer substation to prevent physical damage due to poisonous substances in the equipment. |  |  |  |  |  |
|  |  | Resettlement | (1) Make out compensation and reward program for the personal households with resettled houses and requisitioned land, and the enterprises, units and shops influenced by resettlement, and the employees of the shops influenced during resettlement. (2)Make out feedback mechanism for public opinion to collect the opinions of the public influenced. | Project owner | Municipal Government |  |  | Calculated into resettlement expenses |
|  | Materials Cultural Resources | rotection of Cultural Relics | (1)In case of discovering cultural relics and ruins during construction, construction shall be stopped at onec,e and protective measures such as blockading the site, reporting to cultural relics management department of Zhengzhou City, which will organize rational measures to dig the cultural relics and ruins. Construction shall be proceed until such work is completed. (2)Formulate perfect monitoring program for the influenced cultural relics and ancient buildings; mainly monitor settlement, leaning and development of cracks etc. thereof, and set early warning value, alarming value and control value; make out emergency construction plan; | Construction Unit | Project Owner Local Environmental Protection Bureau Cultural Relics Bureau |  |  | calculated into engineering fee |
| Operational Period | Natural Environment | Sound Envrionment | (1) Regularly rectify the wheel tread;(2)Regularly grind the steel rail to keep smooth surface;(3)Strengthen operational management of the comprehensive base, and improve the awareness of environmental protection of the driver and passengers; control horning; It is forbidden to carry out commissioning and workshop production with high noise. (4)It is requested to give priority to the low and medium-rise buildings within 15 meters to the air kiosks and cooling tower when considering resettlement measures. (5)Adjust the location of the air kiosks and cooling tower to keep the distance between them and the sensitive points larger than 15 meters. (6)Install silencer on the wind pipes and ventilators for the ventilation and air kiosks to reduce impacts due to noise by the ari kiosks. | Project owner | Project Owner Local Environmental Protection Bureau |  |  | / |
|  |  | Environmental Vibration | (1) Give priority to vehicles with low noise and vibration value, and excellent structure during choice of vehicles; (2)Strengthen maintenance of the wheel rails, and regularly rotate wheels and grind steel rails; apply oil to the curves with small radius to guarantee desirable operational conditions thereof and reduce additional vibration. | Project Owner | Project Owner Local Environmental Protection Bureau |  |  | / |
|  |  | Atmospheric Environment | (1)The underground stations shall adopt decoration materials that comply with state environmental standard, which is good for protecting human health, and reducing the impacts on the surrounding environment due to the strange smell from the exhaust of the air kiosk during the preliminary operational period.(2) Buildings with a high concentration of populations such as schools, hospitals and concentrated residential areas etc. shall not be built within 15 meters to the air kiosks. | Project owner and government planning department | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | Water Envrionment | Strengthen monitoring of the dometic sewage and production sewage during operational period of the stations and depots along the project line to discharge such sewage after reaching the standard. | Project owner entrusts qualified unit | Project Owner Local Environmental Protection Bureau | The owner entrusts qualified organ to undertake by means of contract | pH, SS, , COD | 15 |
|  | Ecological Environment | Vegetation Greening | / | Project Owner | Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | Solid Wastes | (1)Estalbish dustbin for the domestic rubbish at the stations along the line, and arrange managerial staffs to clean the ground and wagon in time, and classify the rubbish and collectively transport to environmental health department for collective disposal. | Project Owner | Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  | Social Environment | Protection of Disadvantagted Populations | (1)Establish non-barrier passage for the disabled at stations; (2)The toilet cesspit for females shall be increased according to due proportion at various stations.(3)Formulate ratinal ticket price mechanism for the low-income populations; | Construction Unit | Project Owner |  |  | calculated into engineering fee |
|  |  | complaint channels | In every station location visible complaints and other complaints | Project Owner | Local Environmental Protection Bureau |  |  | Calculated into daily operational expenses |
|  |  | Human Health | (1)The staffs exposed to high-noise operation in the depot repair workshops shall wear ear plug etc.. (2)The driver and passengers of the subway train shall shorten the working time as much as possible, and regularly receive physical check to guarantee physical and mental health. (3) Guarantee normal operation of the ventilation system and carry out regular air quality test to lower air pollution in the underground sections. (4)The staffs exposed to dangerous wastes such as waste oil and dregs produced by the treatment system of oil-bearing waste water, the oily cleaning cloth of various processes, waste transformer and waste storage battery etc. shall wear protective gloves and masks. | Project Owner | Local Environmental Protection Bureau |  |  | Calculated into daily operational expenses |
|  | Material cultural ruins | Cultural relics | Strengthen own protective measures of the cultural relics and ancient buildings, properly take engineering measures, establish vibration monitoring mechanism, strengthen long-term tracing and monitoring to guarantee no adverse impact will be caused on the protected cultural relics due to operation of the train. | The project owner entrusts qualified unit | Project Owner Local Environmental Protection Bureau Cultural relics bureau |  |  | 90 |

Table 3.4-2 List of General Characteristic Mitigation Measures of the Environmental Impacts 
by Zhengzhou Rail Transit Line 3 Funded with the Loan of World Bank

| Phase | Environmental Elements | Measures | Implementation Organ | Supervisory Organ | Monitoring Organ | Monitoring Items | Expenses(100,000 Yuan) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Feasibility Study and Design Stage | Natural Environment | Environmental Vibration | (1) Adopt 60kg/m seamless routes adopted in engineering design will positively prevent vibration pollution. (2) The the protective distance for buildings on both sides of the underground routes in areas such as “mixed district, CBD”, “industrial concentrated district”, and “both sides on the traffic artery” shall be 25 meters. The protective distance for | Design unit | Project Owner Local Environmental Protection Bureau |  |  | / |
|  |  | Sound Environment | (1) It is requested that buildings sensitive to noise such as residential area, school and hospital not be built within the noise prevention distance, for example 15 metter to the air kiosk and cooling tower(category 4 area), 26 meters(category 2 area) and 50 meters(category 1 area). | Design unit | Project Owner Local Environmental Protection Bureau |  |  | Calculated into design fee |
|  |  | surface water | (1) Construction site and waste residue site are not set in the scope of 200m from both sides of river channels of Jialu River, Jinshui River, Xiong’er River, Qili River and Chaohe River. | Design unit | Project Owner Local Environmental Protection Bureau |  |  | Calculated into design fee |
|  |  | groundwater | (1) Xinliu Road Station, Shamen Road Station, Xinglongpu Road Station, Dongfeng Road Station, Nongye Road Station, Huanghe Road Station, Jinshui Road Station, Taikang Road Station, Shuncheng Street Station, Weilai Avenue Station, South Fengtai Road Station, Tongtai Road Station, East Huanghe Road Station, East Nongye Road Station, Zhongxing Road Station, Boxue Road Station and East Hanghai Road Station adopt cast-in-situ bored pile & waterproof curtain for enclosure. (2) Erqi Square Station, Dongdajie Street Station, Chengdong Road Station and Zhongzhou Avenue Station adopt underground diaphragm wall.(2) All intervals adopt shield method for construction | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | ecological environment | (1)For the design of entrances and ventilation pavilion of 10 stations including Weilai Avenue Station, Fengtainan Road Station, Zhongzhou Avenue Station, Tongtai Road Station, Huanghedong Road Station, Nongyedong Road Station, Zhongxing Road Station, Boxue Road Station, Hanghai East Road Station, it shall consider in principle their location of new district and economic development zone, which is an integrated modern new downtown and CBD of commercial, office, information and business functions, so their structures and appearances shall be uniform as possible; adopt blending landscape design handling principle to uniformly plan and construct with surrounding buildings and construct the ventilation pavilion station, pavilion and other ground buildings together to meet the design requirements of local urban regions.(2)For 5 stations in Zhengzhou old town area including Xinglongpu Road Station, Dongfeng Road Station, Nongye Road Station, Huanghe Road Station and Jinshui Road Station, there are dense buildings around the stations and the ground buildings appears crowded. The rail transit construction shall be considered together with Zhengzhou old town reconstruction planning and Nanyang Road expansion project; The along-line regions integrates the functions of resident, commercial, traffic connection, special mending and lacing, so the design of the stations and ventilation pavilions in this section shall be arranged in combination with surrounding buildings as possible, and it can consider the joint construction with existing ground buildings if conditions allow so as to ensure the coordination of station buildings with surrounding urban building landscape, reduce the impact of newly built facilities on ground landscape visual effect and make them open space presenting the urban style.(3)For Erqi Square Station and Chengdong Road Station, since they are near national and provincial historic sites to be protected such as Memorial Tower for February 7th Strike, Zhengzhou Confucius Temple and Zhengzhou Shang Dynasty Relics and there are many modern buildings such as Hualian Shopping Center, Wanda Plaza and Zhengzhou Department Store, and also near 3 historic and cultural blocks of Shuyuan Street, Confucius Temple- Chenghuang Temple, Dehua Street-Datong Road, the design of entrance/exit and ventilation pavilion of these stations shall fully consider the actual conditions and adopt the combination design concept of blending method and hidden method to both reduce the impact of station entrance/exit and ventilation pavilion on ground landscape visual effect, and not lose the eye-catching state of station building so that it can maintain the open landscape space of Zhengzhou city and surrounding grandeur feeling, but also blend into the modern atmosphere. |  |  |  |  |  |
|  | Social Environment | Resident’s life | (1)Comparison of recommended scheme and alternative scheme is made for routes of lines including section at north of North Ring Road and section between Jinshui Road Station and Erqi Square Station, and select the scheme with the least amount of demolition so as to reduce its influence on residents. | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Traffic | (1) Dashiqiao area has large traffic volume and severe congestion, so Jinshui Road Station selects cover-excavation method for construction to reduce its influence on ground traffic. (2) Nanyang Road is relatively narrow but with large traffic volume, for Dongfeng Road Station, Huanghe Road Station and Nongye Road Station which are located along the Line and adopt open-cut method for construction, since they have large traffic volume now, rationally arrange construction site, do not occupy road or occupy road as least as possible, and shorten construction time to the greatest extent; (3)For Taikang Road Station, Shuncheng Street Station, Dongdajie Station and Chengdong Road Station in prosperous area , since they have large ground traffic volume and occupy large areas of roads, main measures are to formulate traffic dispersion scheme, and vehicles can pass round in advance; elaborately arrange construction site and occupy roads as least as possible; set accommodation lane at both sides of construction site to the greatest extent to relieve traffic obstruction; accelerate construction progress, reduce time of road occupying; take priority in guaranteeing unobstructed bus route etc. | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | The traffic channel | The section of Nanyang road : Cover construction at sections crossing the intersection and fully fencing open-cut construction for stations at both sides, necessary demolition at the same time, traffic limitation, keep one driveway and one non-motor vehicle lane at either direction, and regional traffic organization.. The section of Minggong road : fully fencing open-cut construction for stations at both sides, necessary demolition at the same time, traffic limitation, keep one driveway and one non-motor vehicle lane at either direction, and regional traffic organization.. The section pf Jiefang road : During the peak period, regional organization will be used to ease the traffic on the premise of station traffic organization in Er qi square stadion. The section of east street and west street : During the peak period, regional organization will be used to ease the traffic on the premise of station traffic organization in Shunche jie sdation and in dodajie sation. | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  |  | Planning | Main opinions in Construction Planning and Planning Environmental Impact Assessment are implemented: (1) The line starts from Xinliu Road Station, passes Nanyang Road→Minggong Road→Jiefang Road→Xidajie Street→Dongdajie Street→Zhengbian Road→Shangdu Road→Crossing Lianyungang-Lanzhou Railway→Jingkai 17th Avenue. Length and direction of the line is in basic consistency with those of the planned line.(2)The whole route is totally underground line. (3)Totally 21 stations are established, which are all underground stations, including Xiuliu road station、Shamen road station、Xinglongpu road station、Dongfeng road sttion、Agricultural road station、Huanghe road station、Jinshui road station、Taikang road station、Erqi square station、Shunchenjie station、Dongdajie station、Chengdong road station、Weilaidadao station、Fengtai south station、Zhongzhoudadao station、Tongtai road station、Huanghe east station、Agricultural east station、Zhongxing road station、Boxue road station、Hanghai east station。Station setting is in conformity with the original planning.(4)Parking lot is set at southern bank of Jialu River, and car depot is set at east of East Hanghai Road Station, which are in conformity with the original planning | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
|  | Material Cultural Resources | Cultural relics | （1）Rail Transit Line 3 passes round the axis of the Memorial Tower and passes the outside of tower footing, and the depth of the line shall meet the requirement of 15m made by cultural relics protection department(2) When designing Erqi Square Station, Chengdong Road Station and Taikang Road Station near historical and cultural sites under government protection, the design of its entrance & exit, ventilation kiosk and cooling tower shall be coordinated with Shang Dynasty Culture Display Area in People’s Park and landscape belt of park at riverside of Jinshui River, Erqi Memorial Tower in honor of the Great Strike and Dehua Street Commercial Center as well as Shang Dynasty Site respectively(3) Depth of underground city wall of Shang Dynasty Site in Zhengzhou is about 8-13m, so buried depth of the metro is suggested to be 15-20m.(4)Design of rail near Erqi Memorial Tower in honor of the Great Strike, Shang Dynasty Site in Zhengzhou and Zhengzhou Confucious’ Temple adopts steel spring floating slabs to reduce the influence of metro vibration on historical and cultural sites under government protection. | Design Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into design fee |
| Construction Period | Natural Environment | Atmospheric Environm | (1)Construction site shall set hard enclosures with height of not less than 2.5m, and main roads must be hardened and keep cleaning; construction site shall appoint specially-assigned personnel to be in charge of cleaning-keeping work, and conduct sprinkling and cleaning in time to reduce dust（2）Regularly monitor sensitive points near each station construction | Construction Unit | Project Owner Local Environmental Protection Bureau |  | Tsp | Monitoring expenses: 600,000 yuan; Expenses for temporary sediment tank: 500,000 yuan |
|  |  | Sound Environment | (1)Set temporary sound insulation enclosing wall or absorbent lined barrier with height of 3-4m at sensitive points which are greatly affected by construction noise of stations. See the following table for the specific measures: see table 11.6-2a | Construction Unit | Project Owner Local Environmental Protection Bureau | The owner entrusts qualified organ to undertake by means of contract | Equivalent sound level A | Monitoring expenses: 600,000 yuan; Other expenses: 2.25 Million yuan |
|  |  | Environmental Vibration | During construction period, strengthen vibration monitoring and settlement observation for station construction site and surrounding sensitive points as well as underneath and adjacent vibration sensitive points, and reinforcement measures shall be taken if necessary.。See the following table for the specific measures: see table 11.6-2b | Construction Unit | Project Owner Local Environmental Protection Bureau | The owner entrusts qualified organ to undertake by means of contract | Vibration level Z | Monitoring expenses is 200,000 yuan; The other expenses is calculated into engineering fee |
|  |  | Water Environmen | surfacewater | (1) Construction site and waste residue site shall not be set in the scope of 200m from surface water body. Construction waste residue and dried sludge after treatment by shield mud and water separation system shall be stacked in the designated place, and enclosure measures must be taken, and they shall be sent to local residue management department for treatment.(2) Excavation and earth filling are strictly prohibited on rainstorm days. Temporary spoil and windrow must be covered with tarpaulin or other coverings on rainy days to prevent spoil from flowing into and polluting surface water body due to scour of rainstorm.(3) Waste water produced in car depot shall be treated in adjustment oil removal sedimentation basin, and waste water produced at 21 stations along the Line shall be treated in septic tanks. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  |  | groundwater | (1) Daily pumping drainage of groundwater amount is large during foundation pit dewatering process, to protect groundwater quality, it is suggested that dewatering and drainage shall be discharged into urban rainwater system after removing SS in temporary sedimentation basin. (2) It is suggested to strengthen monitoring and supervision over water level, flow direction and flow rate of groundwater along the Line (especially section of Zhongxing Road-East Hanghai Road). | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | Monitoring expenses: 100,000 yuan; Expenses for temporary sediment tank: 500,000 yuan |
|  | Environment | Vegetation Greening | (1) Protect vegetation within land acquisition and along the Line to the greatest extent during project construction, and minimize deterioration of vegetation such as forest, grass and bushwood around temporary ground and operating zone. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | Solid Wastes | (1) Spoil will be transported to southwestern hilly area for ravine filling, there are four construction waste disposal sites determined at present which are located in Houzhai Village, Honghuasi Village, Xiaoliu Village and Shawoli Village. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  | Materials Cultural Resources | Cultural Relics | It shall be reinforced before construction of Erqi Memorial Tower in honor of the Great Strike, and isolation pile measure shall be taken for shield construction of Line 3. (2) Strengthen vibration monitoring and settlement observation for cultural relics involved along the Line during construction period. Within 50 meters from Erqi Tower, the shield tunneling, especially the operation, will be under strict control to ensure equipment in good condition. The earth-pressing balance mode will be applied, the shield tunneling excavation position, earth cut from each cycle and the volume of synchronous grouting shall be under control, and secondary grouting will done to achieve tunneling in balance. The tunneling parameters of the shield tunneling machine will be studied in detail and parameters such as grouting ratio, pressure, thrust force and speed of the machine will be optimized based on specific geologies in Zhengzhou to ensure the shield tunneling machine passes below Erqi Tower in continuous and steady way in order to achieve minimal ground settlement and meet the requirement on protection of historical relics. | Construction Unit | Project Owner Local Environmental Protection Bureau Cultural Relics Bureau | The owner entrusts qualified organ to undertake by means of contract | Vibration speed | Monitoring expenses is 200,000 yuan; The other expenses is calculated into engineering fee |
|  |  | Ancient and renowned trees | (1) There is no old and famous tree along the Line. | Project Owner | Municipal Government |  |  | Calculated into resettlement expenses |
|  | Social environment | Traffic evacuation | (1) For construction of Jinshui Road Station and Taikang Road Station which most severely affect traffic during construction period, it is suggested to adopt cover-excavation method for construction. (2) Detailed construction organization and traffic dispersion scheme is required to be formulated for other stations adopting open-cut method for construction to minimize its influence on traffic, pedestrians, motor vehicles and traveling of disadvantaged groups such as the disabled. | Project Owner | Municipal Government |  |  | Calculated into resettlement expenses |
|  |  | Resident income | (1) Conduct two placement means including monetary indemnity and property right in exchange for material object for demolition of private reidence;(2) For land acquisition, it shall be compensated as the maximum uniform annual output value of local district with 28.6 times of compensation, and young crops shall be compensated as well, the above compensation fees shall be directly sent to each family. (3) Shops shall be compensated as the market price when demolished, decoration fees shall be given, and six-month business suspension compensation fees shall also be given, and the minimum salary compensation of six months at one time will be given to employees in shops. | Project Owner | Government |  |  | Calculated into immigrant relocation costs |
|  | Construction risk | Construction risk of the station | See the following table for the specific measures: see table 11.6-2c | Construction Unit | Project owner and local environmental protection bureau |  |  | Calculated into engineering supervision expenses |
|  |  | Risk of interval constrution | See the following table for the specific measures: see table 11.6-2d |  |  |  |  |  |
|  | Environmental Supevision during Construction Period |  | (1)Carry out monitoring and supervision over the environmental problems caused by construction | Construction Unit | Project owner and local environmental protection bureau |  |  | Calculated into engineering supervision expenses |
|  | Environmental Protection Organ and Personnel Training | Environmental Protection Organ and Training | (1) Training on establishment of environmental protection organs of the construction unit and building unit, environmental protection laws, construction planning, and environmental monitoring guidelines and regulations etc.. | Construction Unit | Project owner and local environmental protection bureau |  |  | 20 |
| Operational Period | Natural Environment | Sound Environment | (1) Jialu River Parking Lot is surrounded by green belt with width of 10m and enclosing walls all around, western enclosing wall is increased to 3.5m in height, which requires investment increment of 609,000 yuan; one testing line of car depot on East Hanghai Road is set with acoustic barrier with height of 2m, which requires investment increment of 1.35 million yuan.(2) Ventilation kiosk silencers at 17 ventilation kiosk areas are extended from 2m to 3m or 4m in length. Three cooling towers adopt ultra-low noise cross-flow type, and one of them is surrounded by acoustic enclosure; 7 ventilation kiosk areas and 5 cooling towers which are near to sensitive points change site selection and become over 15m from the points,Details are as follows:Table 11.6-2e | Construction Unit | Project Owner Local Environmental Protection Bureau |  | Equivalent sound level A | Monitoring expenses: 200,000 yuan; Other expenses: 62.59Million yuan |
|  |  | Environmental Vibration | (1)For three cultural relics protection units of Shanhaimomuduha Tomb ,Zhengzhou Memorial Tower for February 7th Strike, Zhengzhou Confucius Temple and Zhengzhou Shang Dynasty Relics 4 along both sides of the line in this project, set the steel spring floating slab ballast beds or equivalent moderate shock-absorbing measures., totaling 780m at both sides and requiring 1.95million yuan investment. (2)For 38 over-limit sensitive spots where the line passes just through (in 5m range from the outer rail center line just above track) such as school, hospital and residence areas, including RCC family member courtyard (Gadameilin district) so on, arrange the steel spring floating slab integral ballast beds, totaling 7052m at both sides and requiring investment of 105.78 million yuan. (3)For 45 over-limit sensitive spots within 10--15m range mainly including City bus company, family member courtyard, and Tianxiu courtyard so on, use the flexible support block type integral ballast bed or equivalent moderate shock-absorbing measures, totaling 8753m for double line and the investment of 87.53 million yuan. (4)For the environment sensitive spot with over-limit environment vibration VLz10, or VLz10 is qualified, but VLzmax exceeds the standard environment requirements, including 28 locations of Peaceful residential homes, Building 8 and so on,, use type III vibration reduction fasteners or equivalent moderate shock-absorbing measures, totaling for 5239mm and investment of 17.45 million yuan. See the following table for the specific measures: see table 11.6-2f | Construction Unit | Project owner and local environmental protection bureau | The project owner entrusts qualified organ by contract | Vibration Level | Monitoring expenses: 200,000 yuan; Other expenses: 229.3 Million yuan |
|  |  | Atmospheric Environm | (1) the distance from ventilation pavilions at Shuncheng Street Station and Taikang Road Station to the sensitive spot is less than 15m, and the odors emitted from ventilation pavilion will impact the resident livings to some extent; in combination with the control measures listed in noise topic, the environment assessment suggests to adjust the locations of 8 ventilation pavilions with the distance of less than 15m from sensitive spots. (2)To effectively relieve the odor impact, it is necessary to plant arbors around ventilation pavilion and make the outlet opposite to the sensitive spots such as residential building. | Constructin unit | Project Owner, Local Environmental Protection Bureau |  |  | Calculated into expenses for noise measures |
|  |  | Water Environment | The design adopts adjustment, oil separation and settlement tank to treat the inspection & repair oily sewage.(2)In the design, the domestic sewage is discharged after treatment with septic tank. the sewage of each station during project construction period is able to be included in existing or planned municipal sewage pipeline network and then into related urban sewage treatment plant for centralized treatment | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  |  | Electromagnetic Environment | (1)there are no environmental sensitive points around the depots and parking lots, thus no measures need be taken on such influence in the project。 (2)keep the fencing wall of main substation away from residential area as possible, and the least distance from residential area shall be more than 50m. | Project Owner | Project Owner, Local Environmental Protection Bureau | The project owner entrusts qualified organ to undertake the work by contract | Power frequency electromagnetic field, strong radio interference field | / |
|  |  | Solid Wastes | (1)The rubbish at various stations will be collected by the environmental health staffs, and collectively handed over to the urban rubbish site for disposal. (2)The dangerous substances such as waste oil and dregs, oily cleaning cloth of various processes, and waste transformer oil in the depots and comprehensive base shall be entrusted to the relevant qualified unit for harmless disposal. (3) The storage cells regularly replaced shall be recycled by the factory regularly, and anti-penetration treatment shall be carried out for the storage room of the storage cells to prevent leakage of the infiltration fluid. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  | Environment | Vegetation Greening | 1) Comprehensive greening shall be carried out for the depots, comprehensive base and transformer station etc. during operational period, and the species of the trees shall be mainly local plants. | Construction Unit | Project Owner Local Environmental Protection Bureau |  |  | calculated into engineering fee |
|  | Material cultural resources | Cultural relics | （1）For three cultural relics protection units of Shanhaimomuduha Tomb ,Zhengzhou Memorial Tower for February 7th Strike, Zhengzhou Confucius Temple and Zhengzhou Shang Dynasty Relics 4 along both sides of the line in this project, set the steel spring floating slab ballast beds or equivalent moderate shock-absorbing measures., totaling 780m at both sides and requiring 1.95million yuan investment. See the following table for the specific measures: see table 11.6-2g | Construction Unit | Project Owner, Local Environmental Protection Bureau | The project owner entrusts qualified organ to undertake the work by contract | Vibration speed | Calculated into Vibration costs |
|  | Environmental protection organ and personnel training | Environmental Protection Organ and Training during operational period | Establish environmental protection organ of the operational unit, and training on environmental noise, vibration, air, and waste water monitoring and control techniques for relevant environmental protection managerial personnel | Project Owner | Project Owner, Local Environmental Protection Bureau |  |  | 5 |
| Total Environmental Protection Investment | Total investment: 238309000yuan(excluding investment for monitoring during operational period) |

Table 11.6-2a  Summary sheet of main sensitive spots affected by construction noise

| No. | Station | Sensitive point | Position relative to stations | Size | Closest distance from the constructional boundary (m) | Predicted noise before measures (dB(A)) | Measures to reduce noise | Investment (RMB ¥:×104) | Predicted noise after measures (dB(A)) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Shamen Road Station | Chengshi Bei’an Community 1# building | North end west side | 5 units - 2 households, 6 floors, 1 building, about 60 households | 18 | 54.4 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; locate the vehicle access at the west side. | 25 | 47.4 |
| 2 |  | Changxing Building | South end west side | 5 units, 12 households each unit, about 60 households | 13 | 57.3 |  |  | 50.3 |
| 3 |  | Huiji District Changxing Road Subdistrict Office | North end east side | Subdistrict Office | 9 | 60.5 |  |  | 53.5 |
| 4 |  | Changxing Road 2# Yard 13#, 10# building | North end east side | 5 units, 2 households, 7 floor, 2 buildings, about 140 households | 24 | 51.9 |  |  | 44.9 |
| 5 |  | Baiwen Garden 1#, 2#, 6#, 7# building | South end east side | 3 units, 2 households for each stairs, 1 building; 4 units, 2 households for each stairs, 2 buildings; 8 nits, 2 households for each stair, 1 building, 6 floors (in which the first floor is for store); total about 190 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 6 | Xinglongpu Road Station | Zhengzhou Public Transportation Company Family Area | North end west side | 3 units, 2 households for each stair, 7 floors, 3 buildings; 1 units, 4 households for each stair, 7 floors, 1 building; total about 154 households | Immediately Close to | 70.0 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; locate the vehicle access at the east side. | 25 | 63.0 |
| 7 |  | Huarun Chengshi Zhiyin (Xinyu Yayuan) Community 1#, 5# building | North end east side | 2 units, 2 households, 5 floors, total about 40 households | 15 | 56.0 |  |  | 49.0 |
| 8 |  | Changjian Yufeng (in construction) | South end west side | 8 households per floor, 17 floors, total about 136 households | 22 | 52.7 |  |  | 45.7 |
| 9 | Dongfeng Road Station | Sunshine Holiday Community 3# Building Sunshine Holiday Community 2# Building | North end west side | 3 units, 2 households for each stair, 7 floors, 4 buildings, total about 84 households | 6 | 64.0 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; | 25 | 57.0 |
| 10 |  | Tongle Community 46# Building Tongle Community 61# Building Food Machinery Plant Family Area 2# Building | South end east side | 4 units, 2 households for each stair, 6 floors, 1 building; 1 units, 3 households for each stair, 4 floors, 1 building; 1 units, 3 households for each stair, 7 floors, 1 building; total about 81 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 11 |  | Tongle Community North Area 1#, 2#, 3#, 4#, 5# building | North end east side | 1 unit, 2 households for each stair, 7 floors, 2 buildings; 1 unit, 2 households for each stair, 5 floor, 1 building; 5 units, 2 households for each stair, 6 floors, 1 building; 3 units, 2 households for each stair, 7 floors, 1 building; total about 140 households | 3 | 70.0 |  |  | 63.0 |
| 12 |  | Futian Lijing Garden Community 39#, 40# building | South end west side | 7 floors, 2buildings, about 40 households each floor; total about 560 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 13 | Nongye Road Station | Ronghua Family Area 3#, 4# | North end west side | 3 units, 2 households, 5 floors, 1 building; 7 floors, 1 building; total about 72 households | 12 | 58.0 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; locate the vehicle access at the north side. | 25 | 51.0 |
| 14 |  | Zhengzhou Ceramics Factory Family Area 1#, 3# building, Nanyang Road No. 62 | South end east side | 3 units, 2 households for each stair, 5 floors, 2 buildings, total about 60 households | 6 | 64.0 |  |  | 57.0 |
| 15 |  | Nanyang Road 68# Yard Zhengtie Nanyang New Town Community 1#, 2#, 3#, 10#, 41# building | North end east side | 4 units, 2 households, 7 floors, 1 building; 1 unit, 4 households, 7 floors, 3 building; 5 units, 2 households, 7 floors, 1 building; total about 210 households. | 11 | 58.7 |  |  | 51.7 |
| 16 |  | Xiaoyuzhai (Nanyang Road 266# Yard) 3#, 5# building | South end west side | 5 units, 3 households, 6 floors, 1 building; 2 units, 3 households; 6 floors, 1 building; total about 114 households | 6 | 64.0 |  |  | 57.0 |
| 17 | Huanghe Road Station | Zhengzhou Textile Machinery Staff Apartment 18# - 20# building | North end east side | 3 units, 2 households, 7 floors, 3 buildings; total about 126 households | 7 | 62.6 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; locate the vehicle access at the east side. | 25 | 55.6 |
| 18 |  | Nanyang Road 296# Yard (Nanyang Renjia) 1#, 2#, 3# | North end west side | 2 units, 3 households, 12 floors, 1 building; 3 units, 2 households, 6 floors, 1 building; 1 unit, 2 households, 6 floors, 12 households; 9 units, 2 households, 6 floors, 1 building; total about 312 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 19 |  | Zhengzhou Textile Machinery Co., Ltd. Family Area 6#, 5#, 4#, south 3#, south 2# building | South end east side | 10 households per floor, 4 floors, 5 buildings, total about 150 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 20 |  | Huayuan Community (Nanyang Road No.300) 5# building | South end west side | 3 units, 2 households, 7 floors, 1 building, total about 42 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 21 | Jinshui Road Station | Film Bureau Family Area 6#, 7# building (Nanyang Road No. 7) | North end east side | 3 units, 2 households, 5 floors, 1 building; 1 unit, 2 households, 5 floors, 1 building; total about 32 households | Immediately Close to | 70.0 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; locate the vehicle access at the south side. | 25 | 63.0 |
| 22 |  | Zhengzhou City Library | North end east side | In library | Immediately Close to | 70.0 |  |  | 63.0 |
| 23 |  | Zhengzhou National Oil Reserve Base Family Area 1# building | South end west side | 5 units, 2 households, 7 floors, 1 building, total about 70 households | 24 | 51.9 |  |  | 44.9 |
| 24 |  | Downtown Community Phase II 1# building | South end east side | 3 units, 2 households, 18 floors, 1 building, total about 108 households | 31 | 49.7 |  |  | 42.7 |
| 25 | Taikang Road Station Jinshui Road Station | Xicai Community (Minggong Road 240# Yard)2#, 3# building | South end west side | 7 floors, 10 households 2 buildings; total about 140 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 26 |  | Minggong Road N0.245 (Xiqian Street 85# Yard 1#, 2# building) | South end west side | about 20 households for low rise; 3 units, 3 households, 7 floors, 1 building, about 63 households; total about 83 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 27 |  | Huarun Yuefu (in construction) | South end east side | 10 households per floor, 58 floors, 1 building; about 580 households | 20 | 53.5 |  |  | 46.5 |
| 28 | Erqi Square Station | Huigang New Town 1#, 2#, 3# building | Northwest end west side | 15 households per floor, 1 building; 10 households per floor, 1 building; 20 households per floor, 1 building; total about 1260 households | 10 | 59.5 | / |  | 59.5 |
| 29 |  | Xiaolou Mosque, Female Mosque | West end north side | Religion | 12 | 58.0 |  |  | 51.0 |
| 30 | Shuncheng Street Station | Hongxin Garden 1# building | East end north side | 3 units, 4 households, 7 floors, 1 building; about 约84 households | 6 | 64.0 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; locate the vehicle access at the west side. | 25 | 57.0 |
| 31 |  | Xidan Apartment 2# Building | East end north side | 7 households per floor, 7 floors, 1 building; 4 units, 4 households; 7 floors, 1 building; about 138 households | 26 | 51.2 |  |  | 44.2 |
| 32 |  | Xiandai Xingyuan 1# | West end south side | About 120 households | 9 | 60.5 |  |  | 53.5 |
| 33 |  | Yinzuo International | East end south side | 15 floors, 5 units, 2 households per stair; about 150 households | Immediately Close to | 70.0 |  |  | 63.0 |
| 34 | East Street Station | Changjiang Chengzhongcheng | West end south side | 4 units, 2 households, 7 floors, 1 building, about 42 households | Immediately Close to | 70.0 | Erect a 3m-high fence; build simple acoustic-proof shelters to house air compressors and generators; Use static-pressed piles instead of drilled and grouted piles; locate the vehicle access at the east side. | 25 | 63.0 |
| 35 |  | Hongyu Garden 1#, 2#, 3# building | West end south side | About 500 households | 20 | 53.5 |  |  | 46.5 |
| 36 |  | East Street 220# Yard | East end south side | 6 units, 2 households 6 floors, 1 building; about 72 households | 7 | 62.6 |  |  | 55.6 |
| 37 |  | Ziyan Huating 1#, 2# building | West end north side | 6 households per floor, 24 floors, 2 buildings, about 288 households | 14 | 56.6 |  |  | 49.6 |
| 38 |  | Zhengzhou Guancheng District State Administration of Taxation Office Service Hall (to be relocated) | West end north side | Government office, 8 floors | Immediately Close to | 70.0 |  |  | 63.0 |
| 39 |  | The First People’s Hospital of Zhengzhou | East end north side | 1200 beds | 19 | 54.0 |  |  | 47.0 |
| 40 | Chengdong Road Station | Dongguandongli 96# Yard 1# building | East end north side | 3 units, 2 households, 5 floors, 1 building, about 30 households | 16 | 55.5 | / | / | 55.5 |
| 41 |  | Shangcheng Garden 1# building | West end north side | 2 units, 3 households, 7 floors, about 42 households | 43 | 46.9 |  |  | 39.9 |
| 42 | Fengtainan Road Station | Zhengzhou Huimin Middle School | West end north side | About 72 classrooms, 2900 teachers and students | 25 | 51.6 | / | / | 51.6 |
| 43 |  | Zhengzhou City Public Security Bureau SWAT Detachment | East end north side | Government office, 8 floors | 27 | 50.9 |  |  | 43.9 |
|  | TOTAL |  |  |  |  |  |  | 225 |  |

Table 11.6-2b Summary list of main sensitive spots of station contruction vibration impact

| SN | station | Target Name | Mileage | section | The recent distance（m） | Buried depth（m） | Using function | Scale | Buildings Category | Sensitive point overview | Contruction year | construction way |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Xinliu road station | Yuhua ninth city, Building 1 #~ 3 # | K0+100～K0+280 | Xinliu Road-Shamen Road Station Section | 46 | 14.5 | House | 25 floors，Frame structure | I | about 1475 househlds | 2010 | Open cut methed |
| 2 | Shamen road station | Huiji District, Changxing Road, Street office | K1+454～K1+537 | Xinliu Road-Shamen Road Station Section | 30 | 14.3 | institution | 4~5 floors，mixed structure | II | Street agency | In the 1990 s | Open cut methed |
| 3 |  | Changxing Road, No. 2 Courtyard | K1+476～K1+539 | Xinliu Road-Shamen Road Station Section | 38 | 14.3 | House | 7 floors，mixed structure | Ⅱ | about 140 househlds | 2000 | Open cut methed |
| 4 |  | Cityorth Shore District, 1 # building | K1+450～K1+540 | Xinliu Road-Shamen Road Station Section | 18 | 14.5 | House | 6 floors，mixed structure | Ⅱ | about 60 househlds | 2000 | Open cut methed |
| 5 |  | Baiwen Garden, Buildings 1 #, 2 #, 6 #, 7 # | K1+587～K1+700 | Shamen Road-Xinglongpu Road Station Section | 17 | 14.7 | House | 6 floors，mixed structure | Ⅱ | about 190 househlds | 2010 | Open cut methed |
| 6 | Xinglongpu road station | CR City Concert (Xinyu Garden) district ,1 #, 5 # Buildings | K2+800～K2+900 | Shamen Road-Xinglongpu Road Station Section | 9 | 16.0 | House | 6 floors，mixed structure | Ⅱ | about 40 househlds | In the 1980 s | Open cut methed |
| 7 |  | City bus company, family member courtyard | K2+800～K2+910 | Shamen Road-Xinglongpu Road Station Section | 15 | 14.5 | House | 7 floors，mixed structure | Ⅱ | about 154 househlds | In the 1990 s | Open cut methed |
| 8 |  | Projects under construction (Chang Jian.Yufeng) | K2+940～K3+170 | Xinglongpu Road-Dongfeng Road Station Section | 50 | 14.0 | House | 17 floors，Frame structure | Ⅰ | about 136 househlds | Under contruction | Open cut methed |
| 9 | Dongfeng road station | Fun district, Northern District, fun district building 1#、2#、3#、4#、5# | K4+291～K4+463 | Xinglongpu Road-Dongfeng Road Station Section | 11 | 14.9 | House | 6～7 floors，mixed structure | Ⅱ | about 140 househlds | In the 1990 s | Open cut methed |
| 10 |  | Sunshine Holiday district, 1 #, 2 # Building | K4+286～K4+500 | Xinglongpu Road-Dongfeng Road Station Section | 10 | 14.9 | House | 7 floors，mixed structure | Ⅱ | About 80 househlds | In the 1980 s | Open cut methed |
| 11 |  | Fun district, Southern District, fun district building 46, 61 | K4+560～K4+600 | Dongfeng Road-Agricultural Road Station Section | 36 | 14.5 | House | 6 floors，mixed structure | Ⅱ | about 81 househlds | In the 1980 s | Open cut methed |
| 12 |  | Fu Tian Lijing Garden District, 39 #, 40 # Building | K4+585～K4+774 | Dongfeng Road-Agricultural Road Station Section | 17 | 15.0 | House | 7 floors，mixed structure | Ⅱ | about 560 househlds | 2000 | Open cut methed |
| 13 | Agricultural road station | Nanyang Road 68 homes, 1 #, 2 #, 3 #, 10 #, 41 # Building | K5+480～K5+679 | Dongfeng Road-Agricultural Road Station Section | 12 | 14.5 | House | 7 floors，mixed structure | Ⅱ | about 210 househlds | In the 1980 s | Open cut methed |
| 14 |  | Residential Community of Meat Product Branch of Food Company | K5+570～K5+700 | Dongfeng Road-Agricultural Road Station Section | 40 | 14.1 | House | 5～7 floors，mixed structure | Ⅱ | about 72 househlds | In the 1980 s | Open cut methed |
| 15 |  | Zhengzhou ceramics factory family member courtyard, 1 #, 3 # Building, Nanyang Road 62 | K5+790～K5+890 | Agricultural Road-Huanghe Road Station Section | 10 | 14.6 | House | 5 floors，mixed structure | Ⅱ | about 60 househlds | In the 1980 s | Open cut methed |
| 16 |  | Small Yuzhai (Nanyang Road courtyard 266--275 ) Building | K5+753～K5+832 | Agricultural Road-Huanghe Road Station Section | 20 | 14.4 | House | 6 floors，mixed structure | Ⅱ | about 114 househlds | In the 1980 s | Open cut methed |
| 17 | Huanghe road station | Zhengzhou Textile staff apartments, 18 # to 20 # buildings | K7+000～K7+100 | Agricultural Road-Huanghe Road Station Section | 37 | 14.5 | House | 7 floors，mixed structure | Ⅱ | about 126 househlds | 2000 | Open cut methed |
| 18 |  | Nanyang Road, No. 296 Courtyard, 1 #, 2 #, 3 # | K7+032～K7+168 | Agricultural Road-Huanghe Road Station Section | 15 | 13.9 | House | 6～12 floors，mixed structure | Ⅱ | about 312 househlds | In the 1990 s | Open cut methed |
| 19 |  | Buildings 6#, 5#, 4#, and Buildings 3# and 2# in the south of Community of Zhengzhou Textile Machinery Co., Ltd. | K7+214～K7+696 | Huanghe Road-Jinshui Road Station Section | 15 | 13.9 | House | 4（floors，mixed structure | Ⅱ | about 150 househlds | In the 1970 s | Open cut methed |
| 20 |  | Garden community, (Nanyang Road 300) 5 # building | K7+220～K7+320 | Huanghe Road-Jinshui Road Station Section | 14 | 13.3 | House | 7 floors，mixed structure | Ⅱ | about 42 househlds | In the 1980 s | Open cut methed |
| 21 |  | Zhengzhou Jianguo Medicine Institute | K07+280～K07+400 | Huanghe Road-Jinshui Road Station Section | 15 | 13.9 | Hospital | 4 floors，mixed structure | Ⅱ |  | In the 1980 s | Open cut methed |
| 22 | Jinshui road station | Film Bureau, family member courtyard, 6 #, 7 # F (Nanyang Road 7) | K8+174～K8+190 | Huanghe Road-Jinshui Road Station Section | 6#(12m)，7#(0m) | 14.8 | House | 5 floors，mixed structure | Ⅱ | about 32 househlds | In the 1980 s | covered excavation methed |
| 23 |  | Zhengzhou City Library | K8+250～K8+300 | Huanghe Road-Jinshui Road Station Section | 5 | 14.4 | Library | 2～6 floors，mixed structure | Ⅱ | — | In the 1980 s | covered excavation methed |
| 24 |  | Jinfeng jinan | K09+158～K09+183 | Jinshui Road-Taikang Road Station Section | 33 | 14.6 | House | 28 floors Frame | Ⅰ | about 324 househlds | Nearly 10 years | Open cut methed |
| 25 |  | Zhengzhou National Oil Reserve Depot, family member courtyard 1 # building | K8+290～K8+360 | Huanghe Road-Jinshui Road Station Section | 20 | 14.4 | House | 7 floors，mixed structure | Ⅱ | about 70 househlds | In the 1980 s | covered excavation methed |
| 26 | Taikang road station | Huarun Yue House (under construction) | K9+245～K9+610 | Taikang Road-Erqi square Station Section | 45 | 19 | House | 58 floors | Ⅰ | about 580 househlds | Under contruction | Open cut methed |
| 27 |  | West Cai district, (Ming Gong Road No. 240 Courtyard) 1 # | K9+275～K9+315 | Taikang Road-Erqi square Station Section | 0 | 14.2 | House | 4～7 floors，mixed structure | Ⅱ | about 82 househlds | In the 1980 s | Open cut methed |
| 28 |  | West Cai district, (Ming Gong Road, No. 240 Courtyard), 2 #, 3 # Building | K9+275～K9+315 | Taikang Road-Erqi square Station Section | 16 | 14.2 | House | 7 floors，mixed structure | Ⅱ | about 84 househlds | In the 1980 s | Open cut methed |
| 29 |  | Courtyard No. 85 West Front Street, 1 # Building (Ming Gong Road, No. 245 Courtyard) | K9+325～K9+410 | Taikang Road-Erqi square Station Section | 9 | 14.2 | House | 2、3，7 floors，mixed structure | Ⅱ | About 83househlds | In the 1980 s | Open cut methed |
| 30 | Erqi square station | Huigang New Town 1 #, 2 #, 3 # Building | K9+700～K9+860 | Taikang Road-Erqi square Station Section | 0 | 19.9 | House | 28 floors，Frame structure | Ⅰ | about 1260 househlds | Under contruction | Open cut methed |
| 31 |  | Small building mosques | K10+000～K10+059 | Taikang Road-Erqi square Station Section | 6 | 23.5 | Religion | 4～6 floors，mixed structure | Ⅱ | — | In the 1960 s | Open cut methed |
| 32 | Shunchengjie station | Modern XingYuan 1 # | K10+800～K10+873 | Erqi square-Shunchengjie Station Section | 23 | 14.4 | House | 14～17 floors，Frame structure | Ⅰ | about 120 househlds | 2000 | Open cut methed |
| 33 |  | Hongxin Jia Yuan 1 # building | K10+915～K10+990 | Shunchengjie-Dongdajie Station Section | 14 | 14.4 | 居住 | 7 floors，mixed structure | Ⅱ | about 84 househlds | 2000 | Open cut methed |
| 34 |  | Xidan apartments, two buildings | K11+070～K11+151 | Shunchengjie-Dongdajie Station Section | 8 | 14.9 | House | 7 floors，mixed structure | Ⅱ | about 138 househlds | 2000 | Open cut methed |
| 35 |  | Ginza International | K10+956～K11+025 | Shunchengjie-Dongdajie Station Section | 14 | 14.2 | House | 15 floors，Frame structure | Ⅰ | about 150 househlds | 2010 | Open cut methed |
| 36 | Dongdajie station | Zi Yan Huating 1 #, 2 # Building | K11+821～K11+917 | Shunchengjie-Dongdajie Station Section | 23 | 14.4 | House | 24 floors，Frame structure | Ⅰ | about 288 househlds | 2010 | Open cut methed |
| 37 |  | Yangtze River City in City | K11+580～K11+666 | Shunchengjie-Dongdajie Station Section | 13 | 16.0 | House | 7 floors，mixed structure | Ⅱ | about 42 househlds | In the 1990 s | Open cut methed |
| 38 |  | Yuhong Garden, 1 #, 2 #, 3 # Buildings | K11+675～K11+800 | Shunchengjie-Dongdajie Station Section | 25 | 14.8 | House、Office | 26 floors，Frame structure | Ⅰ | about 500 househlds | 2010 | Open cut methed |
| 39 |  | Municipal Guancheng State Taxation office services hall | K11+929～K11+978 | Dongdajie-Chengdong Road Station Section | 33 | 14.3 | institution | 8 floors，mixed structure | Ⅱ | — | In the 1990 s | Open cut methed |
| 40 |  | First People's Courtyard of Zhengzhou | K11+990～K12+055 | Dongdajie-Chengdong Road Station Section | 22 | 14.3 | Hospital | 5 floors，mixed structure | Ⅱ | -- | In the 1990 s | Open cut methed |
| 41 |  | 220 East Main Street | K11+978～K12+105 | Dongdajie-Chengdong Road Station Section | 10 | 14.3 | House | 6 floors，mixed structure | Ⅱ | about 72 househlds | In the 1990 s | Open cut methed |
| 42 | Chengdong road station | East Main Street, No. 1 Court, Building 1 | K12+716～K12+830 | Chengdong Road-Weilaidadao Station Section | 11 | 20.5 | House | 4～7 floors，mixed structure | Ⅱ | about 30 househlds | In the 1980 s | Open cut methed |
| 43 |  | East Main Street, No. 1 Court, Building 2 | K12+716～K12+830 | Chengdong Road-Weilaidadao Station Section | 32 | 20.5 | House | 4～7 floors，mixed structure | Ⅱ | about 66 househlds | In the 1980 s | Open cut methed |
| 44 |  | East Main Street, No. 1 Court, | K12+550～K12+600 | Dong dajie station- Chengdong Road Station Section | 38 | 21.2 | House | 7 floors，mixed structure | Ⅱ | about 42househlds | In the 1980 s | Open cut methed |
| 45 |  | Zhengbian road 23 | K12+820～K12+857 | Chengdong Road-Weilaidadao Station Section | 7 | 20.5 | House | 5 floors，mixed structure | Ⅱ | about 72 househlds | In the 1980 s | Open cut methed |
| 46 | Fengtai south road station | Zhengzhou Huimin High School | K14+686～K14+769 | Weilaidadao –Fengtai south Road Station Section | 47 | 14.3 | School | 5 floors，mixed structure | II | about2900 peple | In the 1990 s | Open cut methed |
| 47 |  | Zhengzhou City Public Security Bureau Police Detachment | K14+793～K14+942 | Fengtai south Road ~ Zhongzhoudadao Station Section | 27 | 14.3 | institution | 7～8floors，Frame structure | I | - | 2010 | Open cut methed |
| 48 | traction line | Dongyinggang Village | K24+300～K24+800 | Boxue Road - Hanghai east Road Station Section | 0 | 13.0 | House | Below the second floor are peasant houses | Ⅲ | about 70 househlds | In the 1990 s | Open cut methed |

Table 11.6-2c  Construction risks and measures of stations

| No. | Station | Engineering proposal | Construction method | Risk engineering category | Description of basic risk conditions | Risk classifications | Solution |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Xinliu Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | There are a DN219 gas pipe along Xinliu road with underground 2 meters depth. | Class II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for handling of existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. |
| 2 | Shamen Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | There are a DN219 gas pipe along Changxin road with underground 3 meters depth. | Class class II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for handling of existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. |
| 3 | Xinlongpu Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | There are a DN250 gas pipe along Nanyang road with underground 2 -4 meters depth. a DN400 drinkable water pipe along Xinglongpu road with underground 2 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for handling of existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. |
| 4 | Dongfeng Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | neighboring existing structures and buildings | No. 111 in Nanyang Road (TongLe Xiao Qu Nan Qu),The distance from the line is 6m. | Class IIclass II | The impact on foundation pit and the protection of surrounding buildings shall be specially considered. The design adopts drilling piles to prevent the water infiltration from surrounding soiles into the foundation pit and reinforce concrete support to reduce foundation pit deformation and prevent underwater level decrease outside of foundation pit so as to reduce the settlement of surrounding buildings and pipelines; it shall be closely monitored during construction and the grouting shall be done if necessary. Strictly control the ground settlement and horizontal displacement of bracing structures. |
|  |  |  |  | Passing under municipal pipeline | There are a DN250 gas pipe along Nanyang road with underground 2-4 meters depth. a DN600 concrete drinkable water pipe along Nanyang road with underground 2 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for handling of existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. |
| 5 | Agriculture Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | There are a DN250 gas pipe along Nanyang road and a gas pipe at Agriculture Road station with underground 2-4 meters depth, a DN600 concrete drinkable water pipe along Nanyang road with underground 2 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for handling of existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. |
| 6 | Huanghe Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | There are a electric cable at Agriculture Road station with a depth of 2 metres, a DN250 gas pipe along Nanyang road with underground 2-4 meters depth, a DN600 concrete drinkable water pipe along Nanyang road with underground 2 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for handling of existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. |
| 7 | Jinshui Road station | underground 2-floor separating island station | Cover cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of cover digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | underneath the jinshui river and jinshui overpass | Class CLASS IICLASS II | 1.Generally optimal construction parameters may be adopted while strengthening the management of excavation parameters and status control, and carrying out simultaneous pressure grouting and necessary supplementary pressure grouting measure to guarantee its safety. In case of excessively large ground load, or close distance, compensatory filling may be adopted to duly reinforce the earth surrounding tunnel, or strengthen the pipe segment structure. 2.As for intrusion of bridge pile foundation into the tunnel structure, it is necessary to dismantle such pile foundations before arrival of the shield tunnel machine. It is possible to take pile foundation underpinning, or pile dismantlement for bridge reconstruction. 3. Grouting pipes shall be reserved in the tunnel to reinforce the surrounding soil. Meanwhile, high-pressure jet sprouting piles shall be established between the bridge pile foundation and the structure of the inter-zone tunnel for isolation. |
| 8 | Taikang Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | double gas pipeline in the north side of taikang road d250, Distance from The north side of the midline is 10、12.5，Distance from The East side of the midline is 8.5 m.From west to east along taikang road D600, 8 meters depth.Minggong road ,D600,from south to north,about 4 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for handling of existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. |
| 9 | Erqi Square station | underground 3-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a three-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 23 meters, and it is proposed to adopt continuous waterproof concrete walls for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | neighboring existing structures and buildings | distance from xiaolou qingzhen temple and qingzhen woman temple is about 6 meters. | Class IIclass II | 1. Strength the construction monitoring for foundation pit bracing structure and traffic dispersion road surface. Strictly control the ground settlement and horizontal displacement of bracing structures. 2. Monitor the deformation of buildings besides foundation pit, ground surface and retaining structure and reserve grouting holes at buildings near the foundation pit; conduct grouting reinforcement if excess deformation of foundation is detected. |
| 10 | Shunchengjie station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | neighboring existing structures and buildings | distance from honhxinjiayuan number 1 building （7 floor，brick-concrete structure） | Class I | 1. Strength the construction monitoring for foundation pit bracing structure and traffic dispersion road surface. Strictly control the ground settlement and horizontal displacement of bracing structures. 2. Monitor the deformation of buildings besides foundation pit, ground surface and retaining structure and reserve grouting holes at buildings near the foundation pit; conduct grouting reinforcement if excess deformation of foundation is detected. |
|  |  |  |  | Passing under municipal pipeline | 1、Gas pipeline from west to east along xiadajie D250,about 2-3 meters depth.from north to south along shuncheng street,about 2-3 meters depth. 2、tap water pipe from east to west along xidajie D600,4-6 meters depth. | Class IIclass II | 1. Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. If the relocation method is used, it shall be kept away from the station foundation pit as possible. 2. Temporarily relocate main pipelines affecting the station, and monitor the stratum deformation at locations after relocation. Once exceeded alarm range, take measures such as grouting reinforcement. |
| 11 | Dongdajie station | underground 3-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a three-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 23 meters, and it is proposed to adopt continuous waterproof concrete walls for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | 1gas pipeline from west to east along dongdajie d250,about 2-3 meters depth,distance from the north side of the midline is about 12 meters.esat side of zijin mountain,from north to south ,2-5 meters depth. | Class IIclass II | 1. Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. If the relocation method is used, it shall be kept away from the station foundation pit as possible. 2. Temporarily relocate main pipelines affecting the station, and monitor the stratum deformation at locations after relocation. Once exceeded alarm range, take measures such as grouting reinforcement. |
| 12 | Chengdong Road station | underground 3-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a three-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 22 meters, and it is proposed to adopt continuous waterproof concrete walls for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  |  | Distance between Number 96 building of dongguangdongli (4-7floors, brick-concrete structure)and the line is sbout 11meters | Class I | 1. Strength the construction monitoring for foundation pit bracing structure and traffic dispersion road surface. Strictly control the ground settlement and horizontal displacement of bracing structures. 2. Monitor the deformation of buildings besides foundation pit, ground surface and retaining structure and reserve grouting holes at buildings near the foundation pit; conduct grouting reinforcement if excess deformation of foundation is detected. |
|  |  |  |  | Passing under municipal pipeline | 1gas pipeline from west to east along dongdajie d250,about 2-3 meters depth,distance from the north side of the midline is about 12 meters. from north to south along chengdong road ,2-3 meters depth.distance from east side of the middle line is about 13 meters,distance from west side is about 11.5 meters | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 13 | Weilaidadao station | underground 3-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  |  | gas pipeline from east to west along the zhengbian road d250,2-3meters depth ,distance from south side of middle line is about 25meters,distance from the north side ofweilaidadao is21 meters ,south side about 24 meters. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 14 | Fengtai South station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | 1、gas pipeline from north to south along the fengtai road,2-3meters depth ,distance from east side of middle line is about 15meters,located on the south side of zhengbian road,d250,from north to south ,2-3 meters depth,north side of the middleline.2、water pipe from west to east ,d600,about 6 meters depth | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 15 | Zhongzhoudadao station | underground 3-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a three-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 23 meters, and it is proposed to adopt continuous waterproof concrete walls for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | neighboring existing structures and buildings | zhongzhou dadao viaduct | Class I-CLASS II | 1.Generally optimal construction parameters may be adopted while strengthening the management of excavation parameters and status control, and carrying out simultaneous pressure grouting and necessary supplementary pressure grouting measure to guarantee its safety. In case of excessively large ground load, or close distance, compensatory filling may be adopted to duly reinforce the earth surrounding tunnel, or strengthen the pipe segment structure. 2.As for intrusion of bridge pile foundation into the tunnel structure, it is necessary to dismantle such pile foundations before arrival of the shield tunnel machine. It is possible to take pile foundation underpinning, or pile dismantlement for bridge reconstruction. 3. Grouting pipes shall be reserved in the tunnel to reinforce the surrounding soil. Meanwhile, high-pressure jet sprouting piles shall be established between the bridge pile foundation and the structure of the inter-zone tunnel for isolation. |
|  |  |  |  | Passing under municipal pipeline | east side of zhongzhoudadao,d250,from north to south ,about 2-5 meters depth,distance from the north sideof the junction is about 30 meters | Class CLASS IICLASS II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 16 | Tongtai Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | 1、Gas pipeline located on the east side of tongtai road d250,from south to north ,2-3meters depth.the north side gas pipeline,west to east ,2-5 meters depth2、From west to east along shangdu road,D600,3meters depth,located on the south side of the middleline. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 17 | Huanghe East Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | 1、Gas pipeline located on the east side of huanghe river road d250,from south to north , 3meters depth.the north side of shangdu roadd250,west to east ,2-5 meters depth 2、bothway tap water pipe from east to west along shangdu road D600,3 meters depth 3、The south side of the Power cable from west to east along shangdu road,2 meters depth | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 18 | Agriculture East Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | 1、Gas pipeline located on the east side of nongye road,from south to north ,2-3meters depth.distance from the east side of midline is 20.5 meters.the north side of shangdu road d250,west to east ,2-3 meters depth, 2、bothway tap water pipe from east to west along shangdu road D600,3 meters depth 3、The south side of the Power cable from west to east along shangdu road,2 meters depth | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 19 | Zhongxing Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | 1、Natural gas pipeline is located on the north of shangdu road D250,from west to east ,2-5 meters depth.2、 bothway tap water pipe from east to west along shangdu road D600,3 meters depth.3、south of power cable from east to west along shangdu road,2 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 20 | Boxue Road station | underground 2-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | 1、bothway tap water pipe from east to west along shangdu road D600,3 meters depth.2、south of power cable from east to west along haihang road D600,2 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |
| 21 | Hanghai East Road station | underground 3-floor island station | open cut normal method | Construction method risk and Geologic risk | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | Class IIclass II | 1. The main body of the station is constructed by means of open digging method with a bi-level three-span steel reinforcement rod and concrete rectangular framework structure. The depth of the base pit of the station is about 17 meters, and it is proposed to adopt drilling filling pile plus waterproof curtain for the bracing structure. 2. Stratified excavation, timely supporting and prohibition from over-excavation; the steel support shall have anti-releasing measures. 3. Properly carry out anti-seepage for station buildings to avoid the rise of underground water level and pollution of station interior; conduct foundation pit monitoring and phreatic water level observation and treatment; reinforce the waterproof design and treatment at bottom of foundation pit. |
|  |  |  |  | Passing under municipal pipeline | single tap water pipe from east to west along haihang road D600,3 meters depth. | Class IIclass II | Adopt measures such as permanent relocation, temporary relocation and temporary hanging for existing pipelines; the specific method shall be determined according to pipeline features, station construction method, station buried depth and other factors. The valves of water supply pipe and gas pipe newly set outside two ends of station shall be properly protected. |

Table 11.6-2d  Construction risks and measures of Interval

| No. | Station | Engineering proposal | Construction method | Risk engineering category | Description of basic risk conditions | Risk classifications | Solution |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | xinliu road station –hanghai road station | shield method | geology risk | K0+000-K25+200 | The aforesaid stratums belong to category I wall rock with uneven distribution of rock properties and ordinary engineering geological conditions. The stratums are composed of powdery earth, powdery clay, powdery sand and fine sand. The rock and soil layers are mainly earth with medium and high compressibility, low strength and poor stability. | class IIclass II | Adjust the shield tunneling parameters according to dynamic monitoring data; carry out reinforcement of mixing pile and rotary churning pile at shield tunneling in and out section; |
| 2 | shanmen road station –xinglongpu road station | shield method | Adjacent / Crossing Underneath Existing Buildings | K2+444～K2+495 | Huiji District’s office building of Land and Resources,7floor,5meters from the linefloor distance from the line is | CLASS II | 1. Adopt earth pressure balance shield and select optimal construction parameters to ensure stable cutting face; strength the synchronous grouting and necessary supplement measures to control the settlement of structures. 2. Adjust shield construction parameters at any time to minimize the over-excavation and under-excavation, eliminate the slump or squeezing of soils before the shield and reduce the lateral force applied on pile foundation from lateral deformation of foundation soil. 3. Adopt synchronous grouting, reduce the gap formed outside the tunnel after shield tail passed and reduce the horizontal displacement of soils around the tunnel and the resulted negative friction resistance. 4. Strengthen the monitoring and take related measures including monitoring of deformation and settlement of structures; the large deformation detected shall be timely feed back to design and construction unit so as to adjust the construction parameters or take necessary ground reinforcement measures. 5. During side channel construction: ① The design temperature and thickness of frozen soil curtain of side channel shall meet the requirement. ② Prepare preventive emergency plans such as freezing hole construction plan, freezing construction plan, excavation and pouring construction plan, frost heave and melting settlement prevention plan. 6. After shield passed, open the embedded grouting pipe in duct according to deformation of ground surface and building/structures, and timely carry out two-shot grouting reinforcement behind the wall for surrounding soils. 7. Control the uneven settlement difference of buildings of no more than ≤3‰ |
|  |  |  |  | K2+600～K2+619 | Peaceful residential homes, Building 8,，17floor floor，distance from the line is 9meters 。Frame structure | class II |  |
|  |  |  |  | K2+623～K2+663 | RCC family member courtyard (Gadameilin district),distance from the line is o meters 。17 floors，Frame structurefloor | class II |  |
|  |  |  |  | K2+800～K2+900 | CR City Concert (Xinyu Garden) district ,1 #, 5 # Buildingsfloor distance from the line is ,9meters | class II |  |
|  |  |  |  | K2+800～K2+910 | City bus company, family member courtyard，7floor floor，distance from the line is 15meters from the line | class II |  |
|  | xinglongpu road station –dongfeng road station |  |  | K3+280～K3+339 | National Food Authority’s Zhengzhou Institute of Science，3~6floor floor， distance from the line is 15m from the line。 | class class II |  |
|  |  |  |  | K3+410～K3+546 | Tractor plant family member building，5floor floor， distance from the line is 12meters。 | class II |  |
|  |  |  |  | K3+573～K3+600 | Nanyang Road 137，6floor floor ， distance from the line is 15meters from the line | class II |  |
|  |  |  |  | K3+610～ K3+723 | Tianxiu home district, 1 # ~ 4 # Building, distance from the line is 16meters from the line，7 floors，mixed structurefloor mixed structure | class II |  |
|  |  |  |  | K3+730～ K3+784 | Zhengzhou Oriental Tumor Courtyard，5floor ，distance from the line is 15m，mixed structure 。 | class II |  |
|  |  |  |  | K3+957～K3+990 | ICBC family member building，5floor ，distance from the line is 11m，mixed structure | class II |  |
|  |  |  |  | K4+000～K4+213 | 张砦村，2~7floor ，distance from the line is 17m，mixed structure | class II |  |
|  |  |  |  | K4+291～K4+463 | Fun district, 1 #, 2 #, 3 #, 4 #, 5 # Buildingfloor ，11meters from the line distance from the line is ，6--7 floors，mixed structuremixed structure | class II |  |
|  |  |  |  | K3+200～K3+328 | Grain transport community, Building 9, Building 10，6floor floor， distance from the line is 11m from the line，mixed structuremixed structure | class II |  |
|  |  |  |  | K3+611～K3+621 | Huiji District’s Board of Education family member building，7floor floor，mixed structuremixed structure ， distance from the line is 13meters from the line。 | class II |  |
|  |  |  |  | K3+635～K3+773 | Yuhua Wen Hui Garden District, Building 1 to 5，7floor floor，mixed structuremixed structure ， distance from the line is 16meters from the line。 | class II |  |
|  |  |  |  | K3+917～K4+049 | Yuhua Wen Qing Garden District Building 1 to 4，7floor ，mixed structure ，distance from the line is 13m。 | class II |  |
|  |  |  |  | K4+129～K4+211 | Yaxin good times area, 3 to 4 Building 7floor ，mixed structure ，distance from the line is 13m。 | class II |  |
|  |  |  |  | K4+217～K4+277 | Chuangye Homes，7floor ，mixed structure ，distance from the line is 9m。 | class II |  |
|  |  |  |  | K4+286～K4+500 | Sunshine Holiday district, 1 #, 2 # Building，7floor ，mixed structure ，distance from the line is 10m。 | class II |  |
| 4 | dongfeng road station-nonongye road station | shield method | Crossing Underneath Existing Buildings | K4+529～K4+558 | Nanyang Road, No. 111 Courtyard，6floor ，distance from the line is 6m。 | classII |  |
|  |  |  |  | K4+929～K5+010 | China Railway Bridge Bureau family member courtyard 1 #，7floor ，distance from the line is 8m。 | class II |  |
|  |  |  |  | K5+116～K5+247 | Zhengzhou Boiler Factory family member courtyard 1 #, 2 #，7floor ，distance from the line is 11m。 | class II |  |
|  |  |  |  | K5+268～K5+318 | Zhengrong Group Limited family member courtyard, 3 #, 6 # building，5floor ，distance from the line is 8m | class II |  |
|  |  |  |  | K5+328～K5+390 | Vision Garden 2 #, 3 # Building，7floor ，distance from the line is 11m。 | class II |  |
|  |  |  |  | K5+392～K5+456 | Old meat processing factory family member courtyard, 1 #, 3 #, 5 # Building，6floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K5+480～K5+679 | Nanyang Road 68 homes, 1 #, 2 #, 3 #, 10 #, 41 # Building，6floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K4+785～K4+833 | Mold factory family member courtyard 1 # building，6floor ，distance from the line is 12m。 | class class II |  |
|  |  |  |  | K4+845～K4+900 | Kaiyuan district, 1 #, 2 # Building，6floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K4+937～K5+025 | Nanyang Road, No. 239 Courtyard，6floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K5+390～K5+441 | Ronghua community, 1 # Building，5floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K5+477～K5+520 | Nanyang Road 253 (food company meat branch family member building) 1 #, 3 #，6floor ，distance from the line is 11m。 | class II |  |
| 5 | nongyeroad station –huanghe road station | shield method | Adjacent / Crossing Underneath Existing Buildings | K5+790～K5+890 | Zhengzhou ceramics factory family member courtyard, 1 #, 3 # Building, Nanyang Road 62 | class II |  |
|  |  |  |  | K5+900～K5+965 | Provincial Prospecting machinery factory family member courtyard 1 #, 5 #, 6 # building，6floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K6+043～K6+082 | Nanyang Road, No. 52 (Yuhua Wen Jinyuan), three buildings，7floor ，distance from the line is 13m。 | class II |  |
|  |  |  |  | K6+205～K6+234 | Sipo Road 9，8floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K6+429～K6+500 | Nanyang Road, No. 46，17floor ，distance from the line is 11m。 | class II |  |
|  |  |  |  | K6+517～K6+548 | Nanyang Road, No. 41 courtyard, 5 # Building，6floor ，distance from the line is 9m。 | class II |  |
|  |  |  |  | K6+613～K6+679 | Huafu Institute of Dermatology，5~7floor ，distance from the line is 10m。 | class II |  |
|  |  |  |  | K6+690～K6+762 | City No. 71 high school，5floor ，distance from the line is 11m。 | class II |  |
|  |  |  |  | K6+900～K7+073 | Zhengzhou Textile staff apartments, 29 #, 30 # Building，4floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K7+100～K7+177 | Nanyang Road, No.1 primary，3~6floor ，distance from the line is 9m。 | class II |  |
|  |  |  |  | K5+843～K5+878 | Transport company family member courtyard, (Nanyang Road No. 268 courtyard), 1 # Building，7floor ，distance from the line is 15m。 | class II |  |
|  |  |  |  | K5+889～K6+021 | Nanyang Road, No. 270 Courtyard, 2 #, 4 # Building，7floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K6+034～K6+085 | Nanyang Road, No. 279 Courtyard, 1 #, 2 # Building，5~7floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K6+100～K6+180 | Pearl Factory, family member courtyard, 1 #, 2 #, 3 # Building (Nanyang Road 275)，6floor ，distance from the line is 9m。 | class II |  |
|  |  |  |  | K6+260～K6+305 | Nanyang Road, No. 283 Courtyard，5floor ，distance from the line is 13m。 | class II |  |
|  |  |  |  | K6+600～K6+975 | Hengtian Heavy Industry Co., Ltd family area，3~6floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K7+032～K7+168 | Nanyang Road, No. 296 Courtyard, 1 #, 2 #, 3 #，6~12floor ，distance from the line is 15m。 | class II |  |
| 6 | huanghe road station –jinshuiroad station | shield method | Adjacent / Crossing Underneath Existing Buildings | K7+214～K7+696 | Zhengzhou Textile Machinery Co family member courtyard, 6 #, 5 #, 4 #, South 3 #, 2 # Building South，4floor ，distance from the line is 15m。 | class II |  |
|  |  |  |  | K7+900～K8+150 | Nanyang Road No. 12 courtyard, 1 #, 2 # Building，3~6floor ，distance from the line is 10m。 | class II |  |
|  |  |  |  | K7+970～K8+010 | Jinshui District Police Fire Brigade，7floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K8+174～K8+190 | Film Bureau, family member courtyard, 6 #, 7 # F (Nanyang Road 7)，5floor ，crossing underneath number 7 building | CLASS II |  |
|  |  |  |  | K8+190～K8+220 | Tingdao foreign language training，4floor ，crossing underneath。 | CLASS II |  |
|  |  |  |  | K8+250～K8+300 | Zhengzhou City Library，2~6floor ，distance from the line is 5m。 | CLASS II |  |
|  |  |  |  | K7+220～K7+320 | Garden community, (Nanyang Road 300) 5 # building，7floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K7+900～K8+020 | Zhongheng Garden, 2nd Courtyard, 1 #, 2 #, 3 # Building，5~6floor ，distance from the line is 8m。 | class II |  |
| 7 | jinshui road station –taikang road station | shield method | Adjacent / Crossing Underneath Existing Buildings | K8+485～K8+495 | Jinshui Road, 11th courtyard, 1 # building，4floor ，distance from the line is 11m。 | class II |  |
|  |  |  |  | K8+640～K8+690 | Minggong Road No. 67 courtyard, (Jinfeng Golden Coast International), 1 # Building，7floor ，distance from the line is 6m。 | CLASS II |  |
|  |  |  |  | K8+920～K9+017 | Minggong Road, No. 156 Courtyard, 1 #, 2 # Building，6floor ，distance from the line is 6m。 | CLASS II |  |
|  |  |  |  | K9+030～K9+100 | Jin Ming Yuan South, Building # 1，7floor ，distance from the line is 4m。 | CLASS II |  |
| 8 | taikang road station –erqi suquare station | shield method | Adjacent / Crossing Underneath Existing Buildings | K9+700～K9+860 | Huigang New Town 1 #, 2 #, 3 # Building，28floor ，distance from the line is 0m。 | CLASS II |  |
|  |  |  |  | K10+000～K10+059 | Small building mosques，4~6floor ，distance from the line is 6m。 | CLASS II |  |
|  |  |  |  | K9+275～K9+315 | West Cai district, (Ming Gong Road No. 240 Courtyard) 1 # ，4~7floor ，Crossing underneath | CLASS II |  |
|  |  |  |  | K9+325～K9+410 | Courtyard No. 85 West Front Street, 1 # Building (Ming Gong Road, No. 245 Courtyard)，2~7floor ，distance from the line is 9m。 | class II |  |
|  |  |  |  | K9+545～K9+608 | Ming Gong Road No. 272, (Rural Credit Cooperative Union, family member building)，6floor ，crossing underneath。 | CLASS II |  |
|  |  |  |  | K9+638～K9+674 | Yalong district, 17 # Building，7floor ，正下穿。 | CLASS II |  |
|  |  |  |  | K9+638～K9+674 | Yalong districtl 16 # Building, 1 #, 2 # Building，7floor ，distance from the line is 16m。 | class II |  |
|  |  |  |  | K9+687～K9+719 | Catholic Church，2~5floor ，distance from the line is 2m。 | CLASS II |  |
|  |  |  | Crossing Underneath bridge | K9+800～K10+000 | Jiefang Road overpass Pile foundationCrossing underneath | CLASS II |  |
| 9 | erqi suquare station –shuncheng street station | shield method | Adjacent / Crossing Underneath Existing Buildings | K10+510～K10+614 | Shangfuxin Village House 1#，18floor ，distance from the line is 6m。 | class II |  |
|  |  |  |  | K10+625～K10+779 | Fuchun Apartment 1 # building，7floor ，distance from the line is 15m。 | class II |  |
|  |  |  |  | K10+317～K10+348 | Zhengzhou Feb 7 Strike Monument，14floor ，钢筋混凝土结构。distance from the line is 3m。 | CLASS II |  |
|  |  |  |  | K10+528～K10+614 | Huating Apartments, Dehua Street community 1 #, 2 # Building，16floor ，distance from the line is 15m。 | class II |  |
|  |  |  |  | K10+630～K10+775 | Jinding Huafu House, front 1 #，11floor ，distance from the line is 13m。 | class II |  |
|  |  |  |  | K10+630～K10+775 | Jinding Huafu House, rear，5~7floor ，distance from the line is 8m。 | class II |  |
| 10 | shuncheng street station –dongdajie street station | shield method | Adjacent / Crossing Underneath Existing Buildings | K10+915～K10+990 | Hongxin Jia Yuan 1 # building，7floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K11+070～K11+151 | Xidan apartments, two buildings，7floor ，distance from the line is 8m。 | class II |  |
|  |  |  |  | K11+250～K11+286 | West Street, No. 231，16floor ，distance from the line is 13m。 | class II |  |
|  |  |  |  | K11+380～K11+446 | Zhongkai City Lights Clove Court, 1 #, 2 # Building，12floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K10+956～K11+025 | Ginza International，7floor ，distance from the line is 15m。15floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K11+038～K11+100 | 233 West Main Street (the third secondary school, family member building)，18floor ，distance from the line is 11m。 | class II |  |
|  |  |  |  | K11+230～K11+300 | Sun Moon Star City, 1 # building，20floor ，distance from the line is 15m。 | class II |  |
|  |  |  |  | K11+328～K11+566 | Zhongkai City Lights Clove Court, 1 #, 2 # Building，7floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K11+580～K11+666 | Yangtze River City in City，7floor ，distance from the line is 13m。 | class II |  |
| 11 | dongdajie road station-chengdong road station | shield method | Adjacent / Crossing Underneath Existing Buildings | K11+978～K12+105 | number 220 community in dongdajie，6floor ，distance from the line is 10m。 | class II |  |
|  |  |  |  | K12+133～K12+366 | Zhongkai City Lights Guangjingcui Court, 1 #, 2 # Building，7floor ，distance from the line is 8m。 | class II |  |
| 12 | chengdong road station-weilaidadao road station | shield method | Adjacent / Crossing Underneath Existing Buildings | K12+716～K12+830 | East Main Street, No. 1 Court, 1 # building，4~7floor ，distance from the line is 11m。 | class II |  |
|  |  |  |  | K12+992～K13+072 | Knitting mill family member courtyard, 1 # building，5floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K13+076～K13+226 | Yutong Garden 1 # building ，6floor ，distance from the line is 12m。 | class II |  |
|  |  |  |  | K13+230～K13+408 | Municipal underwear factory family member courtyard, 1 #, 2 #, 3 # Building，5~6floor ，distance from the line is 14m。 | class II |  |
|  |  |  |  | K12+820～K12+857 | Zheng Bian Road, Building 23,，5floor ，distance from the line is 7m。 | class II |  |
|  |  |  |  | K13+158～K13+225 | Cargo Terminal No. 23 North Street Courtyard, 1 #, (Phoenix Road Community)，5floor ，distance from the line is 18m。 | class II |  |
|  |  |  |  | K13+332～K13+390 | Boai ENT Hospital of Zhengzhou，6floor ，distance from the line is 9m。 | class II |  |
|  |  |  |  | K13+398～K13+430 | Zheng Bian Road, No. 49, family member courtyard, 1 # Building，5floor ，distance from the line is 13m。 | class II |  |
|  |  |  |  | K13+512～K13+650 | Dongming Road 30 Courtyard, (electric power district), 1 #, 2 # Building，6floor ，distance from the line is 9m。 | class II |  |
|  |  |  | Crossing Underneathwater and rivers | K12+900～K13+000 | Crossing underneath xionger river | class II |  |
| 13 | zhognzhoudadao road station-tongtai road station | shield method | Crossing Underneath bridge | K15+850～K15+950 | crossing underneath zhongzhoudadao overpass | CLASS II |  |
| 14 | tongtai road station –huanghedong road station | shield method | Adjacent / Crossing Underneath Existing Buildings | K17+206～K17+266 | guancheng chinese hospital，8 floor,,10meters from the line | class II |  |
|  |  |  | Crossing Underneathwater and rivers | K17+200～K17+400 | Underneathqili river,，The bottom to the top of tunnel is 10m | CLASS II |  |
| 15 | zhongxing road station –boxue road station | shield method | Crossing Underneath bridgeCrossing Underneath bridge | K20+800～K15+920 | Crossing underneath the high-speed rail bridge pile foundation | CLASS II |  |
| 16 | boxue road street station-hanghaidong road station | shield method | Adjacent / Crossing Underneath Existing Buildings | K24+300～K24+8000 | Dongyinggang cun,1-2floor,crossing undernath | CLASS II |  |
|  |  |  | Crossing Underneath railway | K23+250～K23+360 | underneath longhai railway,，ground line | class II |  |

Table 11.6-2e Noise control measures for ventilation pavilion and cooling tower

| SN | Name of sensitive spot | The measuring points | Mileage | Distence(m) | Superscalar of predicated value during the air conditioning period | Increment of predicated value from the current value | Measures | Investment (10,000 yuan) | Contribution value in the air conditioning period after taking measures | Increment of predicated value after taking measures |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Exhaust wind pavilion | Exhaust wind pavilion | Exhaust wind pavilion | Exhaust wind pavilion | Day | Night | Day | Night |  |  | Day | Night | Day | Night |
| 1 | Yuhua 9th City 1# building | Layer 1 | K0+090～K0+100 | 30 | 30 | 30 | / | 6.72 | 11.28 | 0.02 | 0.08 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; | 15 | 28.13 | 29.12 | 0.00 | 0.01 |
| 1 | Yuhua 9th City 1# building | Layer 2 | K0+090～K0+100 | 30 | 30 | 30 | / | 7.12 | 11.77 | 0.02 | 0.07 |  |  | 28.07 | 29.07 | 0.00 | 0.01 |
| 1 | Yuhua 9th City 1# building | Layer 5 | K0+090～K0+100 | 30 | 30 | 30 | / | 7.61 | 10.19 | 0.01 | 0.09 |  |  | 27.36 | 28.35 | 0.00 | 0.01 |
| 1 | Yuhua 9th City 1# building | Layer 8 | K0+090～K0+100 | 30 | 30 | 30 | / | 6.31 | 10.17 | 0.01 | 0.07 |  |  | 26.13 | 27.12 | 0.00 | 0.01 |
| 2 | Hualian Family Area 3# Building | Layer 1 | K1+436～K1+460 | 26 | 26 | 26 | 30 | 4.78 | 10.79 | 0.18 | 0.49 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）Use Ultra-low noise cooling tower （4）The cooling tower is provided with noise hood at the outside | 45 | 32.51 | 33.01 | 0.01 | 0.03 |
| 2 | Hualian Family Area 3# Building | Layer 3 | K1+436～K1+460 | 26 | 26 | 26 | 30 | 5.64 | 11.22 | 0.14 | 0.42 |  |  | 35.60 | 35.84 | 0.01 | 0.04 |
| 3 | Hualian Family Area 4# building | Layer 1 | K1+436～K1+460 | 23 | 25 | 20 | 26 | / | 0.41 | 0.13 | 0.71 |  |  | 36.89 | 37.19 | 0.01 | 0.08 |
| 3 | Hualian Family Area 4# building | Layer 3 | K1+436～K1+460 | 23 | 25 | 20 | 26 | / | 1.06 | 0.11 | 0.56 |  |  | 33.21 | 33.82 | 0.01 | 0.03 |
| 4 | Hualian Family Area5# building | Layer 1 | K1+436～K1+460 | 20 | 19 | 23 | 16 | / | 0.02 | 0.29 | 1.82 |  |  | 40.26 | 40.37 | 0.03 | 0.22 |
| 4 | Hualian Family Area5# building | Layer 3 | K1+436～ K1+460 | 20 | 19 | 23 | 16 | / | / | 0.45 | 1.84 |  |  | 39.60 | 39.72 | 0.05 | 0.22 |
| 5 | Chengshi Bei’an Residence Community 1# building | Layer 1 | K1+615～ K1+650 | 33 | 33 | 33 | / | / | / | 0.03 | 0.15 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）The wind pavilion is moved 10m to the north | 15 | 27.38 | 28.38 | 0.00 | 0.02 |
| 5 | Chengshi Bei’an Residence Community 1# building | Layer 2 | K1+615～K1+650 | 33 | 33 | 33 | / | / | / | 0.03 | 0.18 |  |  | 27.34 | 28.33 | 0.00 | 0.02 |
| 5 | Chengshi Bei’an Residence Community 1# building | Layer 5 | K1+615～K1+650 | 33 | 33 | 33 | / | / | / | 0.02 | 0.16 |  |  | 26.74 | 27.73 | 0.00 | 0.02 |
| 6 | Chengshi Bei’an Residence Community 4# building | Layer 1 | K1+615～K1+650 | 16 | 19 | 13 | / | 7.55 | 8.55 | 0.05 | 0.55 |  |  | 30.75 | 32.48 | 0.00 | 0.04 |
| 6 | Chengshi Bei’an Residence Community 4# building | Layer 2 | K1+615～K1+650 | 16 | 19 | 13 | / | 6.26 | 9.06 | 0.06 | 0.46 |  |  | 30.65 | 32.34 | 0.00 | 0.03 |
| 6 | Chengshi Bei’an Residence Community 4# building | Layer 5 | K1+615～K1+650 | 16 | 19 | 13 | / | 6.44 | 8.60 | 0.04 | 0.30 |  |  | 29.35 | 30.76 | 0.00 | 0.02 |
| 7 | Zhengzhou Public Transportation Company Family Area 2# building | Layer 1 | K2+787～K2+803 | 26 | 23 | 31 | / | / | / | 0.01 | 0.25 | （1）Main exhaust port backing to the sensitive spot. |  | 29.39 | 30.12 | 0.00 | 0.03 |
| 7 | Zhengzhou Public Transportation Company Family Area 2# building | Layer 2 | K2+787～K2+803 | 26 | 23 | 31 | / | / | / | 0.01 | 0.23 |  |  | 29.32 | 30.05 | 0.00 | 0.02 |
| 7 | Zhengzhou Public Transportation Company Family Area 2# building | Layer 5 | K2+787～K2+803 | 26 | 23 | 31 | / | / | / | 0.01 | 0.17 |  |  | 28.36 | 29.13 | 0.00 | 0.02 |
| 8 | Changjian Yufeng (in construction) | Layer 1 | K3+070～K3+090 | 48 | 48 | 48 | 40 | 12.52 | 15.19 | 0.02 | 0.09 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）Use low noise cooling tower | 35 | 33.13 | 33.28 | 0.00 | 0.01 |
| 9 | Nanyang Road No.219 Yard 6# building | Layer2 | K4+405～K4+425 | 14 | 18 | 1 | / | / | 2.44 | 0.03 | 0.84 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）The location of wind pavilion is adjusted, and moved 6m to the center of the road | 15 | 33.63 | 39.89 | 0.00 | 0.09 |
| 9 | Nanyang Road No.219 Yard 6# building | Layer 4 | K4+405～K4+425 | 14 | 18 | 1 | / | / | 1.38 | 0.03 | 0.28 |  |  | 32.17 | 34.39 | 0.00 | 0.03 |
| 10 | Nanyang Road No.219 Yard 4# building | Layer 1 | K4+405～K4+425 | 26 | 30 | 15 | / | 4.54 | 10.57 | 0.04 | 0.17 |  |  | 29.11 | 31.45 | 0.00 | 0.02 |
| 10 | Nanyang Road No.219 Yard 4# building | Layer 3 | K4+405～K4+425 | 26 | 30 | 15 | / | 3.74 | 9.02 | 0.04 | 0.22 |  |  | 28.84 | 30.98 | 0.00 | 0.02 |
| 11 | Sunshine Holiday Community 3# Building | Layer 1 | K4+405～K4+425 | 6 | 6 | 6 | / | 7.87 | 12.67 | 0.27 | 1.27 |  |  | 35.29 | 36.28 | 0.01 | 0.04 |
| 11 | Sunshine Holiday Community 3# Building | Layer 3 | K4+405～K4+425 | 6 | 6 | 6 | / | 7.44 | 12.38 | 0.14 | 0.58 |  |  | 34.15 | 35.14 | 0.01 | 0.03 |
| 12 | Sunshine Holiday Community 2# Building | Layer 1 | K4+405～K4+425 | 17 | 14 | 21 | / | / | 1.81 | 0.07 | 0.21 |  |  | 31.42 | 32.14 | 0.01 | 0.02 |
| 12 | Sunshine Holiday Community 2# Building | Layer 3 | K4+405～K4+425 | 17 | 14 | 21 | / | / | 1.11 | 0.08 | 0.21 |  |  | 30.95 | 31.70 | 0.01 | 0.02 |
| 13 | Tongle Community 46th building | Layer 1 | K4+600～K4+637 | 30 | 25 | 39 | 16 | 4.07 | 8.66 | 0.57 | 2.46 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB;； （3）Use Ultra-low noise cooling tower （4）The location of wind pavilion is adjusted, and moved 3m to the center of the road | 45 | 34.36 | 34.50 | 0.02 | 0.09 |
| 13 | Tongle Community 46th building | Layer 3 | K4+600～K4+637 | 30 | 25 | 39 | 16 | 4.62 | 7.65 | 0.42 | 2.75 |  |  | 33.93 | 34.08 | 0.01 | 0.11 |
| 14 | Tongle Community 61th building | Layer 1 | K4+600～K4+637 | 28 | 23 | 31 | 23 | 5.43 | 7.84 | 0.23 | 1.54 |  |  | 32.73 | 33.02 | 0.01 | 0.06 |
| 14 | Tongle Community 61th building | Layer 3 | K4+600～K4+637 | 28 | 23 | 31 | 23 | 5.98 | 7.12 | 0.18 | 1.72 |  |  | 32.47 | 32.78 | 0.01 | 0.07 |
| 15 | Food Machinery Plant Family Area 2# Building | Layer 1 | K4+600～K4+637 | 28 | 28 | 28 | 35 | 8.46 | 8.56 | 0.06 | 0.66 |  |  | 34.76 | 35.03 | 0.01 | 0.07 |
| 15 | Food Machinery Plant Family Area 2# Building | Layer 3 | K4+600～K4+637 | 28 | 28 | 28 | 35 | 8.16 | 8.45 | 0.06 | 0.65 |  |  | 34.59 | 34.85 | 0.01 | 0.07 |
| 16 | Xincun Community 3# Building | Layer 1 | K5+640～K5+660 | 31 | 35 | 20 | / | 9.11 | 8.78 | 0.01 | 0.18 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; | 15 | 27.75 | 29.74 | 0.00 | 0.02 |
| 16 | Xincun Community 3# Building | Layer 3 | K5+640～K5+660 | 31 | 35 | 20 | / | 8.41 | 8.09 | 0.01 | 0.19 |  |  | 27.56 | 29.46 | 0.00 | 0.02 |
| 17 | Ronghua Community 2# | Layer 1 | K5+640～K5+660 | 12 | 12 | 12 | / | 3.89 | 6.90 | 0.19 | 1.40 |  |  | 33.55 | 34.54 | 0.01 | 0.11 |
| 17 | Ronghua Community 2# | Layer 3 | K5+640～K5+660 | 12 | 12 | 12 | / | 4.72 | 6.77 | 0.12 | 1.07 |  |  | 32.78 | 33.77 | 0.01 | 0.09 |
| 18 | Ronghua Community 3# | Layer 1 | K5+640～K5+660 | 25 | 21 | 29 | / | 6.53 | 7.86 | 0.03 | 0.26 |  |  | 29.77 | 30.52 | 0.00 | 0.03 |
| 18 | Ronghua Community 3# | Layer 3 | K5+640～K5+660 | 25 | 21 | 29 | / | 5.24 | 8.03 | 0.04 | 0.23 |  |  | 29.45 | 30.21 | 0.00 | 0.02 |
| 19 | Xiaoyuzhai (Nanyang Road 266# Yard) 3# building | Layer 2 | K5+816～K5+836 | 21 | 15 | 26 | 16 | / | / | 0.74 | 3.20 | （1）Main exhaust port backing to the sensitive spot. （2）moved 10m to the center of the road （3）Use Ultra-low noise cooling tower | 30 | 34.66 | 34.90 | 0.02 | 0.14 |
| 19 | Xiaoyuzhai (Nanyang Road 266# Yard) 3# building | Layer 5 | K5+816～K5+836 | 21 | 15 | 26 | 16 | / | / | 0.63 | 2.26 |  |  | 33.29 | 33.56 | 0.02 | 0.10 |
| 20 | Transport Company Family Area (Nanyang Road No. 268) 1# building | Layer 1 | K5+843～K5+878 | 21 | 26 | 10 | 19 | / | / | 0.46 | 2.69 |  |  | 35.22 | 36.56 | 0.02 | 0.18 |
| 20 | Transport Company Family Area (Nanyang Road No. 268) 1# building | Layer 3 | K5+843～K5+878 | 21 | 26 | 10 | 19 | / | / | 0.34 | 2.68 |  |  | 34.76 | 35.84 | 0.01 | 0.17 |
| 21 | Zhengzhou Textile Machinery Apartment 29# | Layer 1 | K7+000～K7+030 | 4 | 1 | 9 | 1 | 2.09 | 16.59 | 9.19 | 18.79 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）Use Ultra-low noise cooling tower （4）moved 8m to the center of the road | 45 | 61.53 | 61.53 | 2.38 | 9.28 |
| 21 | Zhengzhou Textile Machinery Apartment 29# | Layer 3 | K7+000～K7+030 | 4 | 1 | 9 | 1 | / | 3.43 | 0.91 | 5.13 |  |  | 46.76 | 46.84 | 0.10 | 0.89 |
| 22 | Zhengzhou Textile Machinery Apartment 30# | Layer 1 | K7+000～K7+030 | 12 | 16 | 4 | 25 | / | 0.38 | 0.15 | 2.18 |  |  | 38.65 | 41.34 | 0.02 | 0.27 |
| 22 | Zhengzhou Textile Machinery Apartment 30# | Layer 3 | K7+000～K7+030 | 12 | 16 | 4 | 25 | / | / | 0.13 | 1.29 |  |  | 38.02 | 39.10 | 0.01 | 0.15 |
| 23 | Zhengzhou Textile Machinery Apartment 18# | Layer 1 | K7+000～K7+030 | 16 | 16 | 16 | 11 | 7.34 | 10.34 | 0.54 | 4.04 |  |  | 34.94 | 35.25 | 0.01 | 0.11 |
| 23 | Zhengzhou Textile Machinery Apartment 18# | Layer 2 | K7+000～K7+030 | 16 | 16 | 16 | 11 | 8.11 | 10.25 | 0.41 | 3.65 |  |  | 34.82 | 35.14 | 0.01 | 0.10 |
| 23 | Zhengzhou Textile Machinery Apartment 18# | Layer 5 | K7+000～K7+030 | 16 | 16 | 16 | 11 | 7.33 | 8.49 | 0.23 | 2.29 |  |  | 33.42 | 33.77 | 0.01 | 0.08 |
| 24 | Zhengzhou Textile Machinery Apartment 19# | Layer 1 | K7+000～K7+030 | 38 | 34 | 42 | 19 | 5.96 | 9.07 | 0.26 | 1.47 |  |  | 34.12 | 34.27 | 0.01 | 0.06 |
| 24 | Zhengzhou Textile Machinery Apartment 19# | Layer 2 | K7+000～K7+030 | 38 | 34 | 42 | 19 | 5.01 | 8.89 | 0.31 | 1.49 |  |  | 34.01 | 34.16 | 0.01 | 0.06 |
| 24 | Zhengzhou Textile Machinery Apartment 19# | Layer 5 | K7+000～K7+030 | 38 | 34 | 42 | 19 | 4.36 | 8.05 | 0.26 | 1.25 |  |  | 32.65 | 32.84 | 0.01 | 0.05 |
| 25 | Huayuan Community 5# | Layer 1 | K7+240～K7+320 | 13 | 11 | 18 | / | 2.45 | 7.22 | 0.25 | 1.02 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; | 15 | 34.87 | 35.43 | 0.03 | 0.11 |
| 25 | Huayuan Community 5# | Layer 3 | K7+240～K7+320 | 13 | 11 | 18 | / | 3.84 | 8.30 | 0.14 | 0.60 |  |  | 33.82 | 34.44 | 0.01 | 0.06 |
| 26 | Huayuan Community6# | Layer 1 | K7+240～K7+320 | 37 | 32 | 42 | / | 3.23 | 7.34 | 0.03 | 0.14 |  |  | 26.67 | 27.44 | 0.00 | 0.01 |
| 26 | Huayuan Community6# | Layer 3 | K7+240～K7+320 | 37 | 32 | 42 | / | 4.32 | 5.51 | 0.02 | 0.21 |  |  | 26.52 | 27.31 | 0.00 | 0.02 |
| 27 | Film Bureau Family Area 6# building | Layer 1 | K8+200～K8+330 | 22 | 25 | 10 | 15 | / | 0.02 | 0.25 | 2.22 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）Use low noise cooling tower | 35 | 40.60 | 41.04 | 0.03 | 0.28 |
| 27 | Film Bureau Family Area 6# building | Layer 2 | K8+200～K8+330 | 22 | 25 | 10 | 15 | / | 0.50 | 0.33 | 1.80 |  |  | 40.41 | 40.82 | 0.03 | 0.22 |
| 27 | Film Bureau Family Area 6# building | Layer 5 | K8+200～K8+330 | 22 | 25 | 10 | 15 | / | / | 0.16 | 1.14 |  |  | 38.28 | 38.56 | 0.02 | 0.13 |
| 28 | Film Bureau Family Area 5# building | Layer 1 | K8+200～K8+330 | 45 | 45 | 45 | 35 | 7.17 | 10.07 | 0.07 | 0.37 |  |  | 34.10 | 34.24 | 0.01 | 0.04 |
| 28 | Film Bureau Family Area 5# building | Layer 2 | K8+200～K8+330 | 45 | 45 | 45 | 35 | 7.66 | 9.71 | 0.06 | 0.41 |  |  | 34.07 | 34.20 | 0.01 | 0.04 |
| 28 | Film Bureau Family Area 5# building | Layer 5 | K8+200～K8+330 | 45 | 45 | 45 | 35 | 6.77 | 9.20 | 0.07 | 0.40 |  |  | 33.55 | 33.69 | 0.01 | 0.04 |
| 29 | Zhengzhou City Library | Layer 1 | K8+200～K8+330 | 32 | 29 | 41 | 31 | 9.85 | / | 0.05 | / |  |  | 35.32 | 35.44 | 0.00 | #VALUE! |
| 30 | Downtown Community Phase II 1# building | Layer 1 | K8+400～K8+420 | 31 | 31 | 31 | / | 2.65 | 6.73 | 0.05 | 0.23 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; | 15 | 27.87 | 28.86 | 0.00 | 0.02 |
| 30 | Downtown Community Phase II 1# building | Layer 2 | K8+400～K8+420 | 31 | 31 | 31 | / | 3.64 | 6.07 | 0.04 | 0.27 |  |  | 27.82 | 28.82 | 0.00 | 0.03 |
| 30 | Downtown Community Phase II 1# building | Layer 5 | K8+400～K8+420 | 31 | 31 | 31 | / | 3.73 | 5.65 | 0.03 | 0.25 |  |  | 27.15 | 28.14 | 0.00 | 0.03 |
| 30 | Downtown Community Phase II 1# building | Layer 8 | K8+400～K8+420 | 31 | 31 | 31 | / | 3.42 | 6.07 | 0.02 | 0.17 |  |  | 25.97 | 26.97 | 0.00 | 0.02 |
| 31 | Nanyang Road No. 326 (Zhengzhou National Oil Reserve Base Family Area) 1# | Layer 1 | K8+400～K8+420 | 39 | 37 | 45 | / | 2.73 | 8.01 | 0.03 | 0.11 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; | 15 | 26.14 | 26.91 | 0.00 | 0.01 |
| 31 | Nanyang Road No. 326 (Zhengzhou National Oil Reserve Base Family Area) 1# | Layer 3 | K8+400～K8+420 | 39 | 37 | 45 | / | 4.42 | 8.20 | 0.02 | 0.10 |  |  | 26.01 | 26.79 | 0.00 | 0.01 |
| 32 | Xicai Community (Minggong Road 240# Yard) 2#, 3# building | Layer 1 | K9+275～K9+315 | 44 | 40 | 48 | 27 | / | / | 0.19 | 1.15 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）Use Ultra-low noise cooling tower （4）moved 8m to the center of the road | 45 | 35.95 | 36.03 | 0.02 | 0.13 |
| 32 | Xicai Community (Minggong Road 240# Yard) 2#, 3# building | Layer 3 | K9+275～K9+315 | 44 | 40 | 48 | 27 | / | / | 0.20 | 1.22 |  |  | 35.71 | 35.79 | 0.02 | 0.14 |
| 33 | Minggong Road No.245 (Xiqian Street 85# Yard 1#, 2# building ) | Layer 1 | K9+340～K9+375 | 20 | 17 | 24 | 4 | / | 6.76 | 1.53 | 6.16 |  |  | 39.09 | 39.21 | 0.01 | 0.10 |
| 33 | Minggong Road No.245 (Xiqian Street 85# Yard 1#, 2# building ) | Layer 3 | K9+340～K9+375 | 20 | 17 | 24 | 4 | / | 3.02 | 0.48 | 3.22 |  |  | 37.73 | 37.88 | 0.01 | 0.09 |
| 34 | Huigang New Town 3# building | Layer 1 | K9+890～K9+980 | 21 | 25 | 10 | / | 12.51 | 10.41 | 0.01 | 0.31 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; | 15 | 30.75 | 33.79 | 0.00 | 0.03 |
| 35 | Female Mosque | Layer 2 | K10+010～K10+020 | 41 | 41 | 41 | / | / | / | 0.01 | / |  |  | 25.66 | 26.65 | 0.00 | #VALUE! |
| 35 | Female Mosque | Layer 5 | K10+010～K10+020 | 41 | 41 | 41 | / | / | / | 0.01 | / |  |  | 25.25 | 26.25 | 0.00 | #VALUE! |
| 36 | Hongxin Garden 1# building | Layer 2 | K10+915～K10+990 | 35 | 32 | 39 | 32 | / | / | 0.04 | 0.59 | （1）Main exhaust port backing to the sensitive spot. |  | 34.95 | 35.09 | 0.00 | 0.06 |
| 36 | Hongxin Garden 1# building | Layer 5 | K10+915～K10+990 | 35 | 32 | 39 | 32 | / | / | 0.03 | 0.45 |  |  | 34.33 | 34.47 | 0.00 | 0.05 |
| 37 | Xidan Apartment 3# | Layer 1 | K11+070～K11+151 | 36 | 36 | 36 | 26 | / | / | 0.07 | 0.84 |  |  | 36.36 | 36.48 | 0.01 | 0.09 |
| 37 | Xidan Apartment 3# | Layer 3 | K11+070～K11+151 | 36 | 36 | 36 | 26 | / | / | 0.08 | 0.73 |  |  | 36.10 | 36.22 | 0.01 | 0.08 |
| 38 | Xidan Apartment 1# | Layer 1 | K11+070～K11+151 | 41 | 46 | 30 | 39 | / | / | 0.05 | 0.44 |  |  | 33.46 | 33.78 | 0.00 | 0.05 |
| 38 | Xidan Apartment 1# | Layer 3 | K11+070～K11+151 | 41 | 46 | 30 | 39 | / | / | 0.04 | 0.49 |  |  | 33.34 | 33.65 | 0.00 | 0.05 |
| 39 | East Street 220# Yard | Layer 1 | K11+978～K12+105 | / | / | / | 5 | / | 4.52 | 2.70 | 7.92 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）Use low noise cooling tower | 35 | 48.75 | 48.75 | 0.36 | 1.82 |
| 39 | East Street 220# Yard | Layer 3 | K11+978～K12+105 | / | / | / | 5 | / | 1.05 | 1.35 | 5.25 |  |  | 44.51 | 44.51 | 0.16 | 0.92 |
| 40 | Shangcheng Licun (East Street 248# Yard) | Layer 1 | K12+110～K12+200 | / | / | / | 5 | / | 4.96 | 0.80 | 6.16 |  |  | 48.75 | 48.75 | 0.09 | 1.18 |
| 41 | Shangcheng Garden 1# building | Layer 1 | K12+600～K12+650 | 60 | 56 | 53 | 43 | 7.74 | 9.68 | 0.04 | 0.28 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; （3）Use low noise cooling tower | 35 | 32.43 | 32.58 | 0.00 | 0.03 |
| 41 | Shangcheng Garden 1# building | Layer 3 | K12+600～K12+650 | 60 | 56 | 53 | 43 | 7.54 | 10.71 | 0.04 | 0.21 |  |  | 32.33 | 32.48 | 0.00 | 0.02 |
| 42 | Dongguandongli 96# Yard 1# building | Layer 1 | K12+716～K12+830 | 29 | 32 | 16 | / | / | / | 0.03 | 0.50 | （1）Main exhaust port backing to the sensitive spot. （2）Extend the silencer to more than 3m to reduce the noise of ventilation pavilion for 10dB; | 15 | 28.29 | 30.77 | 0.00 | 0.05 |
| 42 | Dongguandongli 96# Yard 1# building | Layer 3 | K12+716～K12+830 | 29 | 32 | 16 | / | / | / | 0.04 | 0.20 |  |  | 28.08 | 30.35 | 0.00 | 0.02 |
| 43 | Dongguandongli 96# Yard 2# building | Layer 1 | K12+716～K12+830 | 28 | 32 | 16 | / | 4.14 | 8.64 | 0.04 | 0.24 |  |  | 28.54 | 30.90 | 0.00 | 0.02 |
| 43 | Dongguandongli 96# Yard 2# building | Layer 3 | K12+716～K12+830 | 28 | 32 | 16 | / | 5.72 | 8.71 | 0.02 | 0.21 |  |  | 28.30 | 30.49 | 0.00 | 0.02 |
| 44 | Dongguandongli 96# Yard 6# building | Layer 1 | K12+716～K12+830 | 37 | 39 | 28 | / | 7.51 | 7.94 | 0.01 | 0.14 |  |  | 26.43 | 27.99 | 0.00 | 0.01 |
| 44 | Dongguandongli 96# Yard 6# building | Layer 3 | K12+716～K12+830 | 37 | 39 | 28 | / | 5.32 | 4.23 | 0.02 | 0.33 |  |  | 26.30 | 27.82 | 0.00 | 0.03 |

Table 11.6-2f .Table Of Sensitive Point Vibration Control Measures

| SN | Target Name | Mileage | Relationship with the line position（m） | Location | Using function | Prediction point Location | VLZmax(dB) | VLZ10（dB) | Structural noise prediction | Superscalar of VLZmax | Superscalar of Structural noise prediction | Sensitive Point Vibration Control Measures | Mileage of Sensitive Point Vibration Control Measures | Length (m) | Total investment(Ten thousand yuan) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | Day | Night | Day | Night |  |  |  |  |
| 1 | New Hope Ao Garden, 17 #, 3 # | K00-195～K00-472 | 47 | Right | House | Outdoor 0.5m | 59.0 | 54.6 | / | / | / | / | / |  |  |  |  |
| 2 | Fuwa beauty area, Building 3, Building 1, | K00+843～K00+921 | 18 | Left | House | Outdoor 0.5m | 69.5 | 55.2 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K0+793～K1+150 | 357 | 178.5 |
| 3 | Taili community, Building 1, | K00+940～K00+968 | 16 | Left | House | Outdoor 0.5m | 68.1 | 56.0 | / | / | / | / | / |  |  |  |  |
| 4 | Hongda district, 11 #, 10 #, 9 #, 5 # Buildinsg | K00+986～K01+100 | 18 | Left | House | Outdoor 0.5m | 69.7 | 56.4 | / | / | / | / | / |  |  |  |  |
| 5 | Huiji District, Changxing Road, Street office | K01+454～K01+537 | 15 | Left | institution | Outdoor 0.5m | 69.6 | 56.9 | / | / | / | / | / |  |  |  |  |
| 6 | Changxing Road, No. 2 Courtyard | K01+476～K01+539 | 38 | Left | House | Outdoor 0.5m | 61.7 | 57.1 | / | / | / | / | / |  |  |  |  |
| 7 | Yuhua ninth city, Building 1 #~ 3 # | K00+100～K00+280 | 46 | Right | House | Outdoor 0.5m | 58.2 | 57.6 | / | / | / | / | / |  |  |  |  |
| 8 | Angel Kindergarten | K00+310～K00+320 | 18 | Right | House | Outdoor 0.5m | 68.6 | 57.6 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K0+260～K0+370 | 110 | 55 |
| 9 | Sanquan Food Co., Ltd., staff quarters | K00+644～K00+670 | 20 | Right | House | Outdoor 0.5m | 71.6 | 57.7 | / | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K0+594～K0+720 | 126 | 126 |
| 10 | ChengHuang 5-rings Mansion | K01+010～K01+030 | 25 | Right | institution | Outdoor 0.5m | 66.0 | 57.7 | / | / | / | / | / |  |  |  |  |
| 11 | Hualian family member courtyard, Buildings 2, 4, 5, | K01+362～K01+450 | 23 | Right | House | Outdoor 0.5m | 66.8 | 57.8 | / | / | / | / | / |  |  |  |  |
| 12 | Cityorth Shore District, 1 # building | K01+450～K01+540 | 18 | Right | House | Outdoor 0.5m | 66.6 | 57.8 | / | / | / | / | / |  |  |  |  |
| 13 | Baiwen courtyard, 1 #, 2 #,6#,7# Buildings | K01+587～K01+700 | 17 | Left | House | Outdoor 0.5m | 66.9 | 57.8 | / | / | / | / | / |  |  |  |  |
| 14 | Phosphate fertilizer factory family member courtyard, 1 #, 2 # Buildings | K02+411～K02+440 | 17 | Left | House | Outdoor 0.5m | 69.6 | 58.1 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K2+361～K2+573 | 212 | 106 |
| 15 | Huiji District’s office building of Land and Resources | K02+444～K02+495 | 5 | Left | institution | Outdoor 0.5m | 73.8 | 58.2 | 47.3 | / | 1.8 | 2.3 | 5.3 |  |  |  |  |
| 15 | Huiji District’s office building of Land and Resources | K02+444～K02+495 | 5 | Left | institution | Indoor | 73.8 | 58.3 | 47.3 | / | 1.8 | 2.3 | 5.3 |  |  |  |  |
| 16 | Peaceful residential homes, Building 8, | K02+500～K02+619 | 9 | Left | House | Outdoor 0.5m | 68.2 | 58.5 | 38.7 | / | / | / | / |  |  |  |  |
| 16 | Peaceful residential homes, Building 8, | K02+500～K02+619 | 9 | Left | House | Indoor | 68.2 | 58.7 | 38.7 | / | / | / | / |  |  |  |  |
| 17 | RCC family member courtyard (Gadameilin district) | K02+623～K02+663 | 0 | Left | House | Outdoor 0.5m | 72.3 | 59.2 | 42.8 | / | 0.3 | / | 0.8 | Steel springs, floating slab,or The same level of vibration reduction measures | K2+573～K2+950 | 377 | 565.5 |
| 17 | RCC family member courtyard (Gadameilin district) | K02+623～K02+663 | 0 | Left | House | Indoor | 72.3 | 59.6 | 42.8 | / | 0.3 | / | 0.8 |  |  |  |  |
| 18 | CR City Concert (Xinyu Garden) district ,1 #, 5 # Buildings | K02+800～K02+900 | 9 | Left | House | Outdoor 0.5m | 70.6 | 59.7 | 44.2 | / | / | / | 2.2 |  |  |  |  |
| 18 | CR City Concert (Xinyu Garden) district ,1 #, 5 # Buildings | K02+800～K02+900 | 9 | Left | House | Indoor | 70.6 | 59.8 | 44.2 | 0.6 | 3.6 | / | 2.2 |  |  |  |  |
| 19 | Changxing Building | K01+650～K01+790 | 32 | Right | House | Outdoor 0.5m | 62.8 | 59.8 | / | / | / | / | / |  |  |  |  |
| 20 | Huiji District, Tumor Courtyard of Traditional Chinese Medicine | K01+801～K01+871 | 29 | Right | Hospital | Outdoor 0.5m | 65.8 | 60.0 | / | / | / | / | / |  | // |  |  |
| 21 | City bus company, family member courtyard | K02+800～K02+910 | 15 | Right | House | Outdoor 0.5m | 69.5 | 60.2 | / | / | 2.5 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K2+750～K2+960 | 210 | 105 |
| 22 | Zhongji urban spring | K03+080～K03+140 | 33 | Left | House | Outdoor 0.5m | 60.8 | 60.2 | / | / | / | / | / |  |  |  |  |
| 23 | Jianye Yihao Chengbang District, 1 #, 7 #, 8 # Building | K03+144～K03+266 | 33 | Left | House | Outdoor 0.5m | 60.8 | 60.4 | / | / | / | / | / |  |  |  |  |
| 24 | National Food Authority’s Zhengzhou Institute of Science and family Courtyard | K03+280～K03+550 | 15 | Left | institution | Outdoor 0.5m | 73.1 | 60.7 | / | / | 1.1 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K3+230～K3+378 | 148 | 148 |
| 24 | National Food Authority’s Zhengzhou Institute of Science and family Courtyard | K03+280～K03+550 | 44 | Left | House | Outdoor 0.5m | 66.5 | 60.9 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K3+378～K3+560 | 182 | 91 |
| 25 | Tianxiu home district, 1 # ~ 4 # Building | K03+610～K03+723 | 16 | Left | House | Outdoor 0.5m | 72.0 | 61.1 | / | / | 0.0 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K3+560～K4+479 | 919 | 919 |
| 26 | Zhengzhou Oriental Tumor Courtyard | K03+730～K03+784 | 15 | Left | Hospital | Outdoor 0.5m | 72.1 | 61.3 | / | 2.1 | 5.1 | / | / |  |  |  |  |
| 27 | ICBC family member building | K03+957～K03+990 | 11 | Left | House | Outdoor 0.5m | 72.7 | 61.5 | / | 2.7 | 5.7 | / | / |  |  |  |  |
| 28 | Zhang Zhaicun | K04+000～K04+213 | 17 | Left | House | Outdoor 0.5m | 71.9 | 62.1 | / | / | / | / | / |  |  |  |  |
| 29 | Fun district, 1 #, 2 #, 3 #, 4 #, 5 # Building | K04+291～K04+463 | 11 | Left | House | Outdoor 0.5m | 70.5 | 62.2 | / | / | / | / | / |  |  |  |  |
| 29 | Fun district, 6 # - 11 # building | K04+291～K04+463 | 28 | Left | House | Outdoor 0.5m | 65.9 | 62.4 | / | / | / | / | / |  |  |  |  |
| 30 | Projects under construction (Chang Jian.Yufeng) | K02+940～K03+170 | 50 | Right | House | Outdoor 0.5m | 57.6 | 62.5 | / | / | / | / | / |  |  |  |  |
| 31 | Grain transport community, Building 9, Building 10 | K03+200～K03+328 | 11 | Right | House | Outdoor 0.5m | 74.7 | 62.6 | / | / | 2.7 | / | / | Steel springs, floating slab,or The same level of vibration reduction measures | K3+150～K3+378 | 228 | 342 |
| 31 | Grain transport community, 3 #~ 8 # Building | K03+200～K03+328 | 23 | Right | House | Outdoor 0.5m | 71.2 | 62.6 | / | / | / | / | / |  |  |  |  |
| 32 | Huiji District’s Board of Education family member building | K03+611～K03+621 | 13 | Right | House | Outdoor 0.5m | 72.7 | 62.7 | / | / | 0.7 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K3+561～K4+167 | 606 | 606 |
| 33 | Yuhua Wen Hui Garden District, Building 1 to 5 | K03+635～K03+773 | 16 | Right | House | Outdoor 0.5m | 69.9 | 62.8 | / | / | / | / | / |  |  |  |  |
| 34 | Yuhua Wen Qing Garden District Building 1 to 4 | K03+917～K04+049 | 13 | Right | House | Outdoor 0.5m | 70.4 | 62.8 | / | / | / | / | / |  |  |  |  |
| 35 | City Brewery, family member courtyard north courtyard Building 25, | K04+056～K04+120 | 18 | Right | House | Outdoor 0.5m | 71.4 | 62.8 | / | / | / | / | / |  |  |  |  |
| 36 | Yaxin good times area, 3 to 4 Building | K04+129～K04+211 | 13 | Right | House | Outdoor 0.5m | 72.8 | 62.9 | / | / | 0.8 | / | / |  |  |  |  |
| 37 | Chuangye Homes | K04+217～K04+277 | 9 | Right | House | Outdoor 0.5m | 74.4 | 62.9 | 47.9 | 4.4 | 7.4 | 2.9 | 5.9 | Steel springs, floating slab,or The same level of vibration reduction measures | K4+167～K4+550 | 383 | 574.5 |
| 37 | Chuangye Homes | K04+217～K04+277 | 9 | Right | House | Indoor | 74.4 | 62.9 | 47.9 | 4.4 | 7.4 | 2.9 | 5.9 |  |  |  |  |
| 38 | Sunshine Holiday district, 1 #, 2 # Building | K04+286～K04+500 | 10 | Right | House | Outdoor 0.5m | 70.8 | 63.0 | 44.4 | / | / | / | 2.4 |  |  |  |  |
| 38 | Sunshine Holiday district, 1 #, 2 # Building | K04+286～K04+500 | 10 | Right | House | Indoor | 70.8 | 63.0 | 44.4 | 0.8 | 3.8 | / | 2.4 |  |  |  |  |
| 38 | Sunshine Holiday district Building 3# ~ 9 # | K04+286～K04+500 | 30 | Right | House | Outdoor 0.5m | 65.4 | 63.2 | / | / | / | / | / |  |  |  |  |
| 39 | Nanyang Road, No. 111 Courtyard | K04+529～K04+558 | 6 | Left | House | Outdoor 0.5m | 72.0 | 63.2 | 45.5 | 2.0 | 5.0 | 0.5 | 3.5 | Steel springs, floating slab,or The same level of vibration reduction measures | K4+479～K4+608 | 129 | 193.5 |
| 39 | Nanyang Road, No. 111 Courtyard | K04+529～K04+558 | 6 | Left | House | Indoor | 72.0 | 63.3 | 45.5 | / | / | 0.5 | 3.5 |  |  |  |  |
| 39 | Fun district, Southern District, fun district building 46, 61 | K04+560～K04+600 | 36 | Left | House | Outdoor 0.5m | 64.1 | 63.5 | / | / | / | / | / |  |  |  |  |
| 40 | Xinyuan Garden 3 #, 4 # | K04+620～K04+700 | 52 | Left | House | Outdoor 0.5m | 61.2 | 63.6 | / | / | / | / | / |  |  |  |  |
| 41 | Nanyang Road, No. 97 Courtyard (Henan Engineering College family member courtyard), 1 #, 4 #, 5 # Building | K04+720～K04+900 | 16 | Left | House | Outdoor 0.5m | 72.3 | 63.6 | / | / | 0.3 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K4+670～K4+879 | 209 | 209 |
| 42 | Henan Engineering college family member courtyard’s five buildings | K04+720～K04+900 | 34 | Left | House | Outdoor 0.5m | 68.2 | 63.7 | / | / | 1.2 | / | / |  |  |  |  |
| 43 | China Railway Bridge Bureau family member courtyard 1 # | K04+929～K05+010 | 8 | Left | House | Outdoor 0.5m | 73.4 | 63.8 | 46.9 | / | 1.4 | 1.9 | 4.9 | Steel springs, floating slab,or The same level of vibration reduction measures | K4+879～K5+060 | 181 | 271.5 |
| 43 | China Railway Bridge Bureau family member courtyard 1 # | K04+929～K05+010 | 8 | Left | House | Indoor | 73.4 | 63.8 | 46.9 | / | 1.4 | 1.9 | 4.9 |  |  |  |  |
| 44 | Home world community 1 #, 2 # Building | K05+024～K05+105 | 27 | Left | House | Outdoor 0.5m | 66.3 | 63.8 | / | / | / | / | / |  |  |  |  |
| 45 | Zhengzhou Boiler Factory family member courtyard 1 #, 2 # | K05+116～K05+247 | 11 | Left | House | Outdoor 0.5m | 72.7 | 63.8 | / | / | 0.7 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K5+066～K5+218 | 152 | 152 |
| 45 | Zhengzhou Boiler Factory, family member courtyard 3 # - 8 # | K05+116～K05+247 | 27 | Left | House | Outdoor 0.5m | 69.4 | 63.9 | / | / | / | / | / |  |  |  |  |
| 46 | Zhengrong Group Limited family member courtyard, 3 #, 6 # building | K05+268～K05+318 | 8 | Left | House | Outdoor 0.5m | 73.2 | 63.9 | 46.8 | / | 1.2 | 1.8 | 4.8 | Steel springs, floating slab,or The same level of vibration reduction measures | K5+218～K5+368 | 150 | 225 |
| 46 | Zhengrong Group Limited family member courtyard, 3 #, 6 # building | K05+268～K05+318 | 8 | Left | House | Indoor | 73.2 | 64.2 | 46.8 | 3.2 | 6.2 | 1.8 | 4.8 |  |  |  |  |
| 47 | Home world community 1 # Building | K05+328～K05+390 | 13 | Left | House | Outdoor 0.5m | 72.4 | 64.2 | / | / | 0.4 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K5+368～K5+740 | 372 | 372 |
| 47 | Home world community 3 #, 2 # Building | K05+328～K05+390 | 33 | Left | House | Outdoor 0.5m | 68.3 | 64.3 | / | / | / | / | / |  |  |  |  |
| 48 | Old meat processing factory family member courtyard, 1 #, 3 #, 5 # Building | K05+392～K05+456 | 12 | Left | House | Outdoor 0.5m | 73.4 | 64.5 | / | / | 1.4 | / | / |  |  |  |  |
| 49 | Nanyang Road 68 homes, 1 #, 2 #, 3 #, 10 #, 41 # Building | K05+480～K05+679 | 12 | Left | House | Outdoor 0.5m | 70.4 | 64.6 | / | 0.4 | 3.4 | / | / |  |  |  |  |
| 50 | Fu Tian Lijing Garden District, 39 #, 40 # Building | K04+585～K04+774 | 17 | Right | House | Outdoor 0.5m | 66.8 | 64.6 | / | / | / | / | / |  |  |  |  |
| 51 | Mold factory family member courtyard 1 # building | K04+785～K04+833 | 12 | Right | House | Outdoor 0.5m | 73.4 | 64.7 | / | 3.4 | 6.4 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K4+735～K5+075 | 340 | 340 |
| 52 | Vision garden, 1 # building | K04+845～K04+900 | 14 | Right | House | Outdoor 0.5m | 72.5 | 64.8 | / | / | 0.5 | / | / |  |  |  |  |
| 53 | Nanyang Road, No. 239 Courtyard | K04+937～K05+025 | 14 | Right | House | Outdoor 0.5m | 72.1 | 64.8 | / | / | 0.1 | / | / |  |  |  |  |
| 53 | Mineral Homeworld 2 # ~ 5 # | K04+937～K05+025 | 37 | Right | House | Outdoor 0.5m | 67.5 | 65.0 | / | / | / | / | / |  |  |  |  |
| 54 | Nanyang Road, No. 244 Courtyard # 1 (aquaculture company family member courtyard) | K05+325～K05+349 | 16 | Right | House | Outdoor 0.5m | 71.8 | 65.0 | / | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K5+275～K5+427 | 152 | 152 |
| 55 | Ronghua community, 1 # Building | K05+390～K05+441 | 12 | Right | House | Outdoor 0.5m | 73.3 | 65.1 | / | 3.3 | 6.3 | / | / |  |  |  |  |
| 56 | Nanyang Road 253 (food company meat branch family member building) 1 #, 3 # | K05+477～K05+520 | 11 | Right | House | Outdoor 0.5m | 74.2 | 65.1 | / | 4.2 | 7.2 | / | / | Steel springs, floating slab,or The same level of vibration reduction measures | K5+427～K5+570 | 143 | 214.5 |
| 56 | Residential Community of Meat Product Branch of Food Company | K05+570～K05+700 | 40 | Right | House | Outdoor 0.5m | 63.4 | 65.2 | / | / | / | / | / |  |  |  |  |
| 57 | Zhengzhou ceramics factory family member courtyard, 1 #, 3 # Building, Nanyang Road 62 | K05+790～K05+890 | 10 | Left | House | Outdoor 0.5m | 70.9 | 65.2 | 44.5 | / | / | / | 2.5 | Steel springs, floating slab,or The same level of vibration reduction measures | K5+740～K6+132 | 392 | 588 |
| 57 | Zhengzhou ceramics factory family member courtyard, 1 #, 3 # Building, Nanyang Road 62 | K05+790～K05+890 | 10 | Left | House | Indoor | 70.9 | 65.2 | 44.5 | / | / | / | 2.5 |  |  |  |  |
| 57 | Zhengzhou ceramics factory family member courtyard, 2 #, 4 #, 5 #, 6 # | K05+790～K05+890 | 25 | Left | House | Outdoor 0.5m | 66.7 | 65.2 | / | / | / | / | / |  |  |  |  |
| 58 | Provincial Prospecting machinery factory family member courtyard 1 #, 5 #, 6 # building | K05+900～K05+965 | 12 | Left | House | Outdoor 0.5m | 74.6 | 65.2 | / | / | 2.6 | / | / |  |  |  |  |
| 59 | Henan Geology and Mineral Resources Building | K05+986～K06+032 | 22 | Left | institution | Outdoor 0.5m | 67.6 | 65.3 | / | / | / | / | / |  |  |  |  |
| 60 | Nanyang Road, No. 52 (Yuhua Wen Jinyuan), three buildings | K06+043～K06+082 | 13 | Left | House | Outdoor 0.5m | 74.4 | 65.4 | / | / | 2.4 | / | / |  |  |  |  |
| 61 | Sipo Road 9 | K06+205～K06+234 | 12 | Left | House | Outdoor 0.5m | 70.6 | 65.5 | / | 0.6 | 3.6 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K6+132～K6+467 | 335 | 335 |
| 62 | Nantong district, (Sipo Road 7th courtyard) 1 # | K06+250～K06+350 | 34 | Left | House | Outdoor 0.5m | 68.7 | 65.5 | / | / | / | / | / |  |  |  |  |
| 63 | College family member courtyard 1 # 3 # | K06+364～K06+406 | 28 | Left | House | Outdoor 0.5m | 70.1 | 65.6 | / | / | / | / | / |  |  |  |  |
| 64 | Nanyang Road, No. 46） | K06+429～K06+500 | 11 | Left | House | Outdoor 0.5m | 69.3 | 65.6 | / | / | / | / | / |  |  |  |  |
| 65 | Nanyang Road, No. 41 courtyard, 5 # Building | K06+517～K06+548 | 9 | Left | House | Outdoor 0.5m | 74.0 | 65.6 | 47.6 | 4.0 | 7.0 | 2.6 | 5.6 | Steel springs, floating slab,or The same level of vibration reduction measures | K6+467～K6+598 | 131 | 196.5 |
| 65 | Nanyang Road, No. 41 courtyard, 5 # Building | K06+517～K06+548 | 9 | Left | House | Indoor | 74.0 | 65.6 | 47.6 | / | 2.0 | 2.6 | 5.6 |  |  |  |  |
| 66 | Taiji Kindergarten, Beijia Education | K06+550～K06+590 | 6 | Left | School | Outdoor 0.5m | 70.8 | 65.6 | 41.3 | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K6+598～K7+123 | 525 | 262.5 |
| 66 | Taiji Kindergarten, Beijia Education | K06+550～K06+590 | 6 | Left | School | Indoor | 70.8 | 65.6 | 41.3 | / | / | / | / |  |  |  |  |
| 67 | Huafu Institute of Dermatology, | K06+613～K06+679 | 10 | Left | institution | Outdoor 0.5m | 73.8 | 65.6 | 47.3 | / | 1.8 | 2.3 | 5.3 |  |  |  |  |
| 67 | Huafu Institute of Dermatology, | K06+613～K06+679 | 10 | Left | institution | Indoor | 73.8 | 65.7 | 47.3 | / | 1.8 | 2.3 | 5.3 |  |  |  |  |
| 68 | City No. 71 high school | K06+690～K06+762 | 11 | Left | School | Outdoor 0.5m | 71.4 | 66.1 | / | / | / | / | / |  |  |  |  |
| 69 | The 2nd Hospital, Zhengzhou University | K06+825～K06+878 | 23 | Left | Hospital | Outdoor 0.5m | 69.8 | 66.1 | / | / | / | / | / |  |  |  |  |
| 70 | Zhengzhou Textile staff apartments, 29 #, 30 # Building | K06+900～K07+073 | 14 | Left | House | Outdoor 0.5m | 69.8 | 66.2 | / | / | / | / | / |  |  |  |  |
| 71 | Zhengzhou Textile staff apartments, 18 # to 20 # buildings | K07+000～K07+100 | 37 | Left | House | Outdoor 0.5m | 63.9 | 66.3 | / | / | / | / | / |  |  |  |  |
| 72 | Small Yuzhai (Nanyang Road courtyard 266--279 ) | K05+753～K06+085 | 15 | Right | House | Outdoor 0.5m | 69.5 | 66.3 | / | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K5+703～K6+050 | 347 | 173.5 |
| 73 | Pearl Factory, family member courtyard, 1 #, 2 #, 3 # Building (Nanyang Road 275) | K06+100～K06+180 | 9 | Right | House | Outdoor 0.5m | 75.6 | 66.3 | 49.1 | 0.6 | 3.6 | 4.1 | 7.1 | Steel springs, floating slab,or The same level of vibration reduction measures | K6+050～K6+355 | 305 | 457.5 |
| 73 | Pearl Factory, family member courtyard, 1 #, 2 #, 3 # Building (Nanyang Road 275) | K06+100～K06+180 | 9 | Right | House | Indoor | 75.6 | 66.4 | 49.1 | 0.6 | 3.6 | 4.1 | 7.1 |  |  |  |  |
| 74 | Nanyang Road, No. 283 Courtyard | K06+260～K06+305 | 13 | Right | House | Outdoor 0.5m | 74.4 | 66.4 | / | 4.4 | 7.4 | / | / |  |  |  |  |
| 75 | Municipal Corporation family member courtyard (Nanyang Road No. 289 courtyard), 1 #, 2 #, 3 #, 4 # Building | K06+455～K06+511 | 36 | Right | House | Outdoor 0.5m | 66.6 | 66.5 | / | / | / | / | / |  |  |  |  |
| 76 | Hengtian Heavy Industry Co., Ltd family area | K06+600～K06+975 | 14 | Right | House | Outdoor 0.5m | 72.4 | 66.5 | / | / | 0.4 | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K6+598～K7+170 | 572 | 286 |
| 77 | Nanyang Road, No. 296 Courtyard, 1 #, 2 #, 3 # | K07+032～K07+168 | 15 | Right | House | Outdoor 0.5m | 67.7 | 66.5 | / | / | 0.7 | / | / |  |  |  |  |
| 78 | Zhengzhou Jianguo Medicine Institute | K07+280～K07+400 | 15 | Left | Hospital | Outdoor 0.5m | 69.7 | 66.5 | / | / | / | / | / |  |  |  |  |
| 79 | Nanyang Road branch of Shiyan Kindergarten, Zhengzhou | K07+280～K07+400 | 54 | Left | School | 室外0.6m | 61.5 | 66.6 | / | / | / | / | / |  |  |  |  |
| 80 | Buildings 6#, 5#, 4#, and Buildings 3# and 2# in the south of Community of Zhengzhou Textile Machinery Co., Ltd. | K07+214～K07+696 | 15 | Left | House | Outdoor 0.5m | 72.2 | 66.6 | / | / | 0.2 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K7+164～K7+780 | 616 | 616 |
| 81 | Hongyihua Hong Kong City | K07+770～K07+900 | 20 | Left | House | Outdoor 0.5m | 65.6 | 66.7 | / | / | / | / | / |  |  |  |  |
| 82 | Nanyang Road No. 12 courtyard, 1 #, 2 # Building | K07+900～K08+150 | 10 | Left | House | Outdoor 0.5m | 71.9 | 66.7 | 45.4 | 1.9 | 4.9 | 0.4 | 3.4 | Steel springs, floating slab,or The same level of vibration reduction measures | K7+850～K8+350 | 500 | 750 |
| 82 | Nanyang Road No. 12 courtyard, 1 #, 2 # Building | K07+900～K08+150 | 10 | Left | House | Indoor | 69.4 | 66.8 | 42.9 | / | / | / | 0.9 |  |  |  |  |
| 83 | Jinshui District Police Fire Brigade | K07+970～K08+010 | 14 | Left | institution | Outdoor 0.5m | 68.6 | 66.8 | / | / | / | / | / |  |  |  |  |
| 84 | Nanyang Road No. 8courtyard, | K08+110～K08+180 | 14 | Left | House | Outdoor 0.5m | 68.6 | 66.9 | / | / | / | / | / |  |  |  |  |
| 85 | Film Bureau, family member courtyard, 6 #, 7 # F (Nanyang Road 7)） | K08+190～K08+220 | 0 | Left | House | Outdoor 0.5m | 74.5 | 67.0 | 48.0 | 4.5 | 7.5 | 3.0 | 6.0 |  |  |  |  |
| 85 | Film Bureau, family member courtyard, 6 #, 7 # F (Nanyang Road 7)） | K08+190～K08+220 | 0 | Left | House | Indoor | 74.5 | 67.0 | 48.0 | / | 2.5 | 3.0 | 6.0 |  |  |  |  |
| 86 | Zhengzhou City Library | K08+250～K08+300 | 5 | Left | Library | Outdoor 0.5m | 74.7 | 67.0 | 48.3 | / | 2.7 | 3.3 | 6.3 |  |  |  |  |
| 86 | Zhengzhou City Library | K08+250～K08+300 | 5 | Left | Library | Indoor | 74.7 | 67.1 | 48.3 | / | 2.7 | 3.3 | 6.3 |  |  |  |  |
| 87 | Garden community, (Nanyang Road 300) 5 # building | K07+220～K07+320 | 14 | Right | House | Outdoor 0.5m | 70.2 | 67.2 | / | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K7+170～K7+370 | 200 | 200 |
| 88 | Zhongheng Garden | K07+420～K07+580 | 40 | Right | House | Outdoor 0.5m | 65.8 | 67.4 | / | / | / | / | / |  |  |  |  |
| 89 | Zhongheng | K07+710～K07+825 | 32 | Right | House | Outdoor 0.5m | 63.0 | 67.4 | / | / | / | / | / |  |  |  |  |
| 90 | Nanyang Road No. 309--314 courtyard, | K07+900～K08+020 | 8 | Right | House | Outdoor 0.5m | 72.0 | 67.4 | 45.5 | / | / | 0.5 | 3.5 | Steel springs, floating slab,or The same level of vibration reduction measures | K7+780～K8+070 | 290 | 435 |
| 90 | Nanyang Road No. 309--314 courtyard, | K07+900～K08+020 | 8 | Right | House | Indoor | 72.0 | 67.4 | 45.5 | / | / | 0.5 | 3.5 |  |  |  |  |
| 91 | Zhongheng garden, 4 # to 10 # | K07+830～K07+950 | 27 | Right | House | Outdoor 0.5m | 68.0 | 67.5 | / | / | / | / | / |  |  |  |  |
| 92 | Qinghua Garden A, B, D, E Block | K08+136～K08+280 | 25 | Right | House | Outdoor 0.5m | 62.7 | 67.6 | / | / | / | / | / |  |  |  |  |
| 93 | Zhengzhou National Oil Reserve Depot, family member courtyard 1 # building | K08+290～K08+360 | 20 | Right | House | Outdoor 0.5m | 68.1 | 67.6 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K8+350～K8+410 | 60 | 30 |
| 94 | Jinshui Road, 11th courtyard, 1 # building | K08+485～K08+495 | 11 | Left | House | Outdoor 0.5m | 70.8 | 67.6 | / | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K8+435～K8+545 | 110 | 110 |
| 95 | Municipal Supply and Marketing Trading Corporation, family member courtyard, 1 #, 10 #, 11 # building | K08+985～K09+058 | 20 | Left | House | Outdoor 0.5m | 69.2 | 67.7 | / | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K8+935～K9+108 | 173 | 86.5 |
| 96 | Minggong Road No. 67 courtyard, (Jinfeng Golden Coast International), 1 # Building | K09+158～K09+183 | 33 | Left | House | Outdoor 0.5m | 60.8 | 67.8 | / | / | / | / | / |  |  |  |  |
| 97 | Minggong Road, No. 139 Courtyard(Grain Bureau family member building) | K08+640～K08+690 | 6 | Right | House | Outdoor 0.5m | 72.6 | 67.8 | 46.1 | / | 0.6 | 1.1 | 4.1 | Steel springs, floating slab,or The same level of vibration reduction measures | K8+590～K9+150 | 560 | 840 |
| 97 | Minggong Road, No. 139 Courtyard(Grain Bureau family member building) | K08+640～K08+690 | 6 | Right | House | Indoor | 72.6 | 67.8 | 46.1 | / | 0.6 | 1.1 | 4.1 |  |  |  |  |
| 98 | Minggong Road, No. 156 Courtyard, 1 #, 2 # Building | K08+920～K09+017 | 6 | Right | House | Outdoor 0.5m | 71.8 | 67.8 | 45.4 | / | / | 0.4 | 3.4 |  |  |  |  |
| 98 | Minggong Road, No. 156 Courtyard, 1 #, 2 # Building | K08+920～K09+017 | 6 | Right | House | Indoor | 71.8 | 67.8 | 45.4 | / | / | 0.4 | 3.4 |  |  |  |  |
| 99 | Jin Ming Yuan building and the building of South | K09+030～K09+100 | 4 | Right | House | Outdoor 0.5m | 72.0 | 67.9 | 44.6 | / | 0.0 | / | 2.6 |  |  |  |  |
| 99 | Jin Ming Yuan building and the building of South | K09+030～K09+100 | 4 | Right | House | Indoor | 72.0 | 67.9 | 44.6 | / | 0.0 | / | 2.6 |  |  |  |  |
| 100 | Huarun Yue House (under construction) | K09+245～K09+610 | 45 | Left | House | Outdoor 0.5m | 60.6 | 68.0 | / | / | / | / | / |  |  |  |  |
| 101 | Huigang New Town 1 #, 2 #, 3 # Building | K09+700～K09+860 | 0 | Left | House | Outdoor 0.5m | 70.4 | 68.0 | 40.9 | / | / | / | / | Steel springs, floating slab,or The same level of vibration reduction measures | K9+650～K10+109 | 459 | 688.5 |
| 101 | Huigang New Town 1 #, 2 #, 3 # Building | K09+700～K09+860 | 0 | Left | House | Indoor | 70.4 | 68.2 | 40.9 | / | / | / | / |  |  |  |  |
| 102 | Small building mosques | K10+000～K10+059 | 6 | Left | Religion | Outdoor 0.5m | 68.2 | 68.2 | 41.7 | / | / | / | / |  |  |  |  |
| 102 | Small building mosques | K10+000～K10+059 | 6 | Left | Religion | Indoor | 68.2 | 68.4 | 41.7 | / | / | / | / |  |  |  |  |
| 103 | West Cai district, (Ming Gong Road No. 240 Courtyard) 1 # | K09+275～K09+315 | 0 | Right | House | Outdoor 0.5m | 74.8 | 68.4 | 48.4 | / | 2.8 | 3.4 | 6.4 | Steel springs, floating slab,or The same level of vibration reduction measures | K9+225～K9+769 | 544 | 816 |
| 103 | West Cai district, (Ming Gong Road No. 240 Courtyard) 1 # | K09+275～K09+315 | 0 | Right | House | Indoor | 74.8 | 68.4 | 48.4 | / | 2.8 | 3.4 | 6.4 |  |  |  |  |
| 103 | West Cai district, (Ming Gong Road, No. 240 Courtyard), 2 #, 3 # Building | K09+275～K09+315 | 16 | Right | House | Outdoor 0.5m | 69.3 | 68.4 | / | / | / | / | / |  |  |  |  |
| 104 | Courtyard No. 85 West Front Street, 1 # Building (Ming Gong Road, No. 245 Courtyard) | K09+325～K09+410 | 9 | Right | House | Outdoor 0.5m | 71.4 | 68.4 | 44.9 | / | / | / | 2.9 |  |  |  |  |
| 104 | Courtyard No. 85 West Front Street, 1 # Building (Ming Gong Road, No. 245 Courtyard) | K09+325～K09+410 | 9 | Right | House | Indoor | 71.4 | 68.4 | 44.9 | / | / | / | 2.9 |  |  |  |  |
| 106 | Ming Gong Road No. 272, (Rural Credit Cooperative Union, family member building) | K09+545～K09+608 | 0 | Right | House | Outdoor 0.5m | 75.6 | 68.6 | 49.2 | 0.6 | 3.6 | 4.2 | 7.2 |  |  |  |  |
| 106 | Ming Gong Road No. 272, (Rural Credit Cooperative Union, family member building) | K09+545～K09+608 | 0 | Right | House | Indoor | 75.6 | 68.7 | 49.2 | 0.6 | 3.6 | 4.2 | 7.2 |  |  |  |  |
| 107 | Yalong district, 17 # Building | K09+638～K09+674 | 0 | Right | House | Outdoor 0.5m | 75.1 | 68.8 | 48.7 | 0.1 | 3.1 | 3.7 | 6.7 |  |  |  |  |
| 107 | Yalong district, 17 # Building | K09+638～K09+674 | 0 | Right | House | Indoor | 75.1 | 68.8 | 48.7 | 0.1 | 3.1 | 3.7 | 6.7 |  |  |  |  |
| 108 | Yalong districtl 16 # Building, 1 #, 2 # Building | K09+638～K09+674 | 16 | Right | House | Outdoor 0.5m | 70.7 | 68.8 | / | / | / | / | / |  |  |  |  |
| 109 | Catholic Church | K09+687～K09+719 | 2 | Right | Religion | Outdoor 0.5m | 74.6 | 68.9 | 48.1 | / | 2.6 | 3.1 | 6.1 |  |  |  |  |
| 109 | Catholic Church | K09+687～K09+719 | 2 | Right | Religion | Indoor | 74.6 | 68.9 | 48.1 | / | 2.6 | 3.1 | 6.1 |  |  |  |  |
| 110 | Jiefang Road Elementary School | K09+719～K09+750 | 42 | Right | School | Outdoor 0.5m | 65.1 | 69.0 | / | / | / | / | / |  |  |  |  |
| 111 | Shangfuxin Village House 1# | K10+510～K10+614 | 6 | Left | House | Outdoor 0.5m | 68.6 | 69.0 | 39.1 | / | / | / | / | Steel springs, floating slab,or The same level of vibration reduction measures | K10+460～K10+664 | 204 | 306 |
| 111 | Shangfuxin Village House 1# | K10+510～K10+614 | 6 | Left | House | Indoor | 68.6 | 69.0 | 39.1 | / | / | / | / |  |  |  |  |
| 111 | Shangfuxin Village 2 #, 3# | K10+510～K10+614 | 41 | Left | House | Outdoor 0.5m | 61.3 | 69.0 | / | / | / | / | / |  |  |  |  |
| 112 | Fuchun Apartment 1 # building | K10+625～K10+779 | 15 | Left | House | Outdoor 0.5m | 70.0 | 69.0 | / | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K10+664～K10+829 | 165 | 82.5 |
| 113 | Huating Apartments, Dehua Street community 1 #, 2 # Building | K10+528～K10+614 | 15 | Right | House | Outdoor 0.5m | 66.8 | 69.0 | / | / | / | / | / |  |  |  |  |
| 114 | Jinding Huafu House, front 1 # | K10+630～K10+775 | 13 | Right | House | Outdoor 0.5m | 66.0 | 69.0 | / | / | / | / | / |  |  |  |  |
| 114 | Jinding Huafu House, rear | K10+630～K10+775 | 8 | Right | House | Outdoor 0.5m | 71.4 | 69.1 | 45.0 | / | / | / | 3.0 | Steel springs, floating slab,or The same level of vibration reduction measures | K10+580～K10+825 | 245 | 367.5 |
| 114 | Jinding Huafu House, rear | K10+630～K10+775 | 8 | Right | House | Indoor | 71.4 | 69.1 | 45.0 | / | / | / | 3.0 |  |  |  |  |
| 115 | Modern XingYuan 1 # | K10+800～K10+873 | 23 | Right | House | Outdoor 0.5m | 63.2 | 69.2 | / | / | / | / | / |  |  |  |  |
| 116 | Hongxin Jia Yuan 1 # building | K10+915～K10+990 | 14 | Left | House | Outdoor 0.5m | 67.8 | 69.2 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K10+865～K11+020 | 155 | 77.5 |
| 117 | Xidan apartments, two buildings | K11+070～K11+151 | 8 | Left | House | Outdoor 0.5m | 69.3 | 69.3 | 41.9 | / | / | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K11+020～K11+201 | 181 | 181 |
| 117 | Xidan apartments, two buildings | K11+070～K11+151 | 8 | Left | House | Indoor | 73.4 | 69.3 | 46.0 | / | 1.4 | 1.0 | 4.0 |  |  |  |  |
| 118 | West Street, No. 231 | K11+250～K11+286 | 13 | Left | House | Outdoor 0.5m | 69.5 | 69.3 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K11+201～K11+400 | 199 | 99.5 |
| 119 | Zhongkai City Lights Clove Court, 1 #, Building | K11+380～K11+446 | 12 | Left | House | Outdoor 0.5m | 70.0 | 69.3 | / | / | / | / | / |  |  |  |  |
| 120 | Fuhua Building | K11+450～K11+550 | 8 | Left | House | Outdoor 0.5m | 71.7 | 69.3 | 42.1 | / | / | / | 0.1 | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K11+400～K11+600 | 200 | 200 |
| 120 | Fuhua Building | K11+450～K11+550 | 8 | Left | House | Indoor | 72.2 | 69.4 | 42.5 | / | 0.2 | / | 0.5 |  |  |  |  |
| 121 | Zi Yan Huating 1 #, 2 # Building | K11+821～K11+917 | 23 | Left | House | Outdoor 0.5m | 63.2 | 69.4 | / | / | / | / | / |  |  |  |  |
| 122 | Ginza International | K10+956～K11+025 | 14 | Right | House | Outdoor 0.5m | 65.9 | 69.5 | / | / | / | / | / |  |  |  |  |
| 123 | 233 West Main Street (the third secondary school, family member building) | K11+038～K11+100 | 11 | Right | House | Outdoor 0.5m | 66.8 | 69.5 | / | / | / | / | / |  |  |  |  |
| 124 | 218 West Main Street | K11+168～K11+221 | 20 | Right | House | Outdoor 0.5m | 65.7 | 69.6 | / | / | / | / | / |  |  |  |  |
| 125 | Sun Moon Star City, 1 # building | K11+230～K11+300 | 14 | Right | House | Outdoor 0.5m | 65.2 | 69.6 | / | / | / | / | / |  |  |  |  |
| 126 | Zhongkai City Lights Clove Court, 1 #, 2 # Building | K11+328～K11+450 | 15 | Right | House | Outdoor 0.5m | 67.3 | 69.6 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K11+278～K11+716 | 438 | 219 |
| 127 | Tangzi Lane (Bo’ai Street Community) | K11+328～K11+666 | 38 | Right | House | Outdoor 0.5m | 63.7 | 69.6 | / | / | / | / | / |  |  |  |  |
| 128 | Changcheng City in City | K11+460～K11+666 | 13 | Right | House | Outdoor 0.5m | 67.6 | 69.7 | / | / | / | / | / |  |  |  |  |
| 129 | Yuhong Garden, 1 #, 2 #, 3 # Buildings | K11+675～K11+800 | 25 | Right | House | Outdoor 0.5m | 62.6 | 69.7 | / | / | / | / | / |  |  |  |  |
| 130 | Municipal Guancheng State Taxation office services hall | K11+929～K11+978 | 33 | Left | institution | Outdoor 0.5m | 62.8 | 69.7 | / | / | / | / | / |  |  |  |  |
| 131 | First People's Courtyard of Zhengzhou | K11+990～K12+055 | 22 | Left | Hospital | Outdoor 0.5m | 65.5 | 69.8 | / | / | / | / | / |  | / / |  |  |
| 132 | Guancheng District Education Center | K12+133～K12+211 | 21 | Left | institution | Outdoor 0.5m | 65.9 | 70.1 | / | / | / | / | / |  |  |  |  |
| 133 | Zhigong Road, Building 1 | K12+230～K12+335 | 18 | Left | House | Outdoor 0.5m | 71.2 | 70.1 | / | / | / | / | / | Steel springs, floating slab,or The same level of vibration reduction measures | K12+180～K12+450 | 270 | 405 |
| 134 | Residential community of Zhengzhou Electric Power College | K12+400～K12+500 | 43 | Left | House | Outdoor 0.5m | 65.6 | 70.2 | / | / | / | / | / |  |  |  |  |
| 135 | 220 East Main Street | K11+978～K12+105 | 10 | Right | House | Outdoor 0.5m | 69.1 | 70.2 | 42.6 | / | / | / | 0.6 | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K11+928～K12+083 | 155 | 77.5 |
| 135 | 220 East Main Street | K11+978～K12+105 | 10 | Right | House | Indoor | 69.1 | 70.2 | 42.6 | / | / | / | 0.6 |  |  |  |  |
| 136 | Mall Village, (248 East Main Street courtyard) | K12+000～K12+500 | 28 | Right | House | Outdoor 0.5m | 68.5 | 70.2 | / | / | / | / | / |  |  |  |  |
| 137 | Zhongkai City Lights Guangjingcui Court, 1 #, 2 # Building | K12+133～K12+366 | 8 | Right | House | Outdoor 0.5m | 72.3 | 70.3 | 44.8 | / | 0.3 | / | 2.8 | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K12+083～K12+450 | 367 | 367 |
| 137 | Zhongkai City Lights Guangjingcui Court, 1 #, 2 # Building | K12+133～K12+366 | 8 | Right | House | Indoor | 72.3 | 70.4 | 44.8 | / | 0.3 | / | 2.8 |  |  |  |  |
| 138 | East Main Street, No. 1 Court, Building 2 | K12+550～K12+600 | 38 | Right | House | Outdoor 0.5m | 61.1 | 70.4 | / | / | / | / | / |  |  |  |  |
| 139 | Dolidongguan96,1# | K12+716～K12+830 | 11 | Left | House | Outdoor 0.5m | 68.6 | 70.4 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K12+666～K12+880 | 214 | 107 |
| 139 | Dolidongguan96,2# | K12+716～K12+830 | 32 | Left | House | Outdoor 0.5m | 64.3 | 70.4 | / | / | / | / | / |  |  |  |  |
| 140 | Knitting mill family member courtyard, 1 # building | K12+992～K13+072 | 12 | Left | House | Outdoor 0.5m | 72.5 | 70.4 | / | / | 0.5 | / | / | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K12+942～K13+458 | 516 | 516 |
| 140 | Knitting mill family member courtyard, 2 # Building | K12+992～K13+072 | 32 | Left | House | Outdoor 0.5m | 68.4 | 70.4 | / | / | / | / | / |  |  |  |  |
| 141 | Yutong Garden Building 1# | K13+076～K13+226 | 12 | Left | House | Outdoor 0.5m | 73.1 | 70.7 | / | / | 1.1 | / | / |  |  |  |  |
| 141 | Yutong Garden Building 2# | K13+076～K13+226 | 36 | Left | House | Outdoor 0.5m | 67.8 | 70.8 | / | / | / | / | / |  |  |  |  |
| 142 | Municipal underwear factory family member courtyard, 1 #, 2 #, 3 # Building | K13+230～K13+408 | 14 | Left | House | Outdoor 0.5m | 73.4 | 70.8 | / | / | 1.4 | / | / |  |  |  |  |
| 142 | Municipal underwear factory, family member courtyard, 5 #, 4 # Building | K13+230～K13+408 | 34 | Left | House | Outdoor 0.5m | 68.5 | 70.8 | / | / | / | / | / |  |  |  |  |
| 143 | Zheng Bian Road, Building 60, | K13+414～K13+473 | 28 | Left | House | Outdoor 0.5m | 65.8 | 70.8 | / | / | / | / | / |  |  |  |  |
| 144 | Zheng Bian Road, Building 23, | K12+820～K12+857 | 7 | Right | House | Outdoor 0.5m | 67.2 | 71.0 | 39.7 | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K12+770～K12+907 | 137 | 68.5 |
| 144 | Zheng Bian Road, Building 23, | K12+820～K12+857 | 7 | Right | House | Indoor | 67.2 | 71.0 | 39.7 | / | / | / | / |  |  |  |  |
| 145 | Great Wall Cambridge Garden | K13+038～K13+091 | 21 | Right | House | Outdoor 0.5m | 66.9 | 71.2 | / | / | / | / | / |  |  |  |  |
| 146 | Cargo Terminal No. 23 North Street Courtyard, 1 #, (Phoenix Road Community) | K13+158～K13+180 | 18 | Right | House | Outdoor 0.5m | 70.0 | 71.4 | / | / | / | / | / | adopt GJ-III vibration reduction fasteners or equivalent moderate shock-absorbing measures. | K13+108～K13+282 | 174 | 87 |
| 146 | Cargo Terminal No. 23 North Street Courtyard, 3 #, (Phoenix Road Community) | K13+180～K13+225 | 18 | Right | House | Outdoor 0.5m | 68.0 | 71.4 | / | / | / | / | / |  |  |  |  |
| 147 | Langui district 1 # Building | K13+230～K13+325 | 16 | Right | House | Outdoor 0.5m | 68.6 | 71.4 | / | / | / | / | / |  |  |  |  |
| 148 | Boai ENT Hospital of Zhengzhou | K13+332～K13+390 | 9 | Right | Hospital | Outdoor 0.5m | 72.6 | 71.4 | 45.2 | / | 0.6 | 0.2 | 3.2 | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K13+282～K13+700 | 418 | 418 |
| 148 | Boai ENT Hospital of Zhengzhou | K13+332～K13+390 | 9 | Right | Hospital | Indoor | 72.6 | 71.5 | 45.2 | / | 0.6 | 0.2 | 3.2 |  |  |  |  |
| 149 | Zheng Bian Road, No. 49, family member courtyard, 1 # Building | K13+398～K13+430 | 13 | Right | House | Outdoor 0.5m | 73.7 | 71.5 | / | / | 1.7 | / | / |  |  |  |  |
| 150 | Dongming Road 30 Courtyard, (electric power district), 1 #, 2 # Building | K13+512～K13+650 | 9 | Right | House | Outdoor 0.5m | 73.2 | 71.6 | 45.7 | / | 1.2 | 0.7 | 3.7 |  |  |  |  |
| 150 | Dongming Road 30 courtyard (electric power district), 3 #, 4 # Building | K13+512～K13+650 | 9 | Right | House | Indoor | 73.2 | 71.6 | 45.7 | / | 1.2 | 0.7 | 3.7 |  |  |  |  |
| 150 | Zhengzhou Huimin High School | K13+512～K13+650 | 45 | Right | House | Outdoor 0.5m | 64.5 | 71.6 | / | / | / | / | / |  |  |  |  |
| 151 | Zhengzhou City Public Security Bureau Police Detachment | K14+686～K14+769 | 47 | Left | School | Outdoor 0.5m | 60.1 | 71.7 | / | / | / | / | / |  |  |  |  |
| 152 | Henan Provincial People's Procuratorate | K14+793～K14+942 | 27 | Left | institution | Outdoor 0.5m | 62.2 | 71.7 | / | / | / | / | / |  |  |  |  |
| 153 | Dongming Road 30 Courtyard, (electric power district), 1 #, 2 # Building | K14+942～K15+052 | 26 | Left | institution | Outdoor 0.5m | 66.2 | 71.7 | / | / | / | / | / |  |  |  |  |
| 154 | Yingxie Garden 1 #, 2 # Building | K15+194～K15+485 | 55 | Left | House | Outdoor 0.5m | 60.6 | 71.8 | / | / | / | / | / |  |  |  |  |
| 155 | District under construction 1 #, 2 # Building | K16+878～K17+052 | 54 | Left | House | Outdoor 0.5m | 59.4 | 71.8 | / | / | / | / | / |  |  |  |  |
| 156 | Henan Zhongdu Dermatology Hospital | K17+147～K17+199 | 24 | Left | Hospital | Outdoor 0.5m | 66.2 | 72.1 | / | / | / | / | / |  |  |  |  |
| 157 | Guancheng Traditional Chinese Medicine Hospital | K17+206～K17+266 | 10 | Left | Hospital | Outdoor 0.5m | 71.0 | 72.1 | 43.6 | / | / | / | 1.6 | Flexible short sleeper and monolithic track bedb,or The same level of vibration reduction measures | K17+156～K17+316 | 160 | 160 |
| 157 | Guancheng Traditional Chinese Medicine Hospital | K17+206～K17+266 | 10 | Left | Hospital | Indoor | 71.0 | 72.6 | 43.6 | / | / | / | 1.6 |  |  |  |  |
| 158 | Caixin Triana district, 1 #, 2 #, 3 #, 4 # Building | K17+390～K17+766 | 51 | Right | House | Outdoor 0.5m | 59.9 | 72.6 | / | / | / | / | / |  |  |  |  |
| 159 | Zhengshang Eastern Harbour, 1 #, 2 # Building | K19+152～K19+300 | 56 | Left | House | Outdoor 0.5m | 60.7 | 72.6 | / | / | / | / | / |  |  |  |  |
| 160 | Sinosun New World | K20+320～K20+680 | 60 | Left | House | 室外0.6m | 60.7 | 72.6 | / | / | / | / | / |  |  |  |  |
| 161 | Dongyinggang Village | K24+300～K24+800 | 0 | Left and Right | House | Outdoor 0.5m | 80.7 | 77.7 | 56.2 | 5.7 | 8.7 | 11.2 | 14.2 | Steel springs, floating slab,or The same level of vibration reduction measures | K24+250～K24+850 | 1200 | 1800 |
| 161 | Dongyinggang Village | K24+300～K24+800 | 0 | Left and Right | House | Indoor | 80.7 | 77.7 | 56.2 | 5.7 | 8.7 | 11.2 | 14.2 |  |  |  |  |

Table 11.6-2g  List for vibration control measures for cultural relics sensitive spots

| No. | Target to be protected | Mileage | District where it is located | Position relative to the line | Line type | Current value of vibration speed (mm/s) | Predicted value of vibration speed (mm/s) | Exceedance | Measures | Extend 50 from both ends | Length (m) | Investment (×104RMB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | Start | end |  |  |
| 1 | Shanhaimomuduha Tomb | K09+900～K09+930 | Jinshui District | Left | Underground | 0.08 | 2.019858 | 1.57 | Steel springs, floating slab,or The same level of vibration reduction measures | 9850 | 9980 | 130 | 195 |
| 2 | 2/7 Strike Monument | K10+317～K10+348 | Erqi district | Right | Underground | 0.09 | 1.333207 | 1.18 |  | 10267 | 10398 | 131 | 196.5 |
| 3 | Zhengzhou Confucius Temple | K12+340～K12+400 | Guancheng Hui-ethnic district | Left | Underground | 0.08 | 1.226718 | 0.96 |  | 12290 | 12450 | 160 | 240 |
| 4 | Shang-dynasty relic, Zhegnzhou | K12+500～K12+580 | Ditto | Both left and right | Underground | 0.08 | / | 0.00 |  | 12450 | 12630 | 180 | 270 |

# 4 Environmental Monitoring

## 4.1 Purpose of Monitoring

Environmental monitoring under the project mainly include monitoring of impacts on environment (water, air, noise, vibration environment, electromagnetic) along the line during construction period and operational period, and is intended to take all the necessary measures to learn about the scope and extent and period of impacts caused by various engineering behaviors during the project construction period and operational period on the objects under environmental protection so as to take corresponding mitigation measures on the engineering behaviors that cause environmental impacts, and verify the preventional and control effect of the environmental protection measures taken thereby and control the environmental impacts due to project construction within the permitted scope to the greatest extent.

## 4.2 Monitoring Plan

According to the engineering characteristics of various projects, phased environmental monitoring plans will be formulated for the construction period and operational period. See Table 4.1

Table 4-1 List of the Environmental Protection Monitoring Plan for Phase I Project of the Zhengzhou Rail Transit Line3 Funded with the World Bank Loan

| Stage | Monitoring Objects | Monitoring Sites | Monitoring Items | Frequency | Total Expense (RMB10,000) | Monitoring Organ | Responsible Organization | Supervisory Organ | Executive Standards and Norms |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Construction Period | Ambient air | Building 1 of Yuhua ninth city,Huiji District Changxing Road Subdistrict Office, Changxing Road 2# Yard 13#, 10# buildin, Baiwen Garden 1#, 2#, 6#, 7# building, Chengshi Bei’an Community 1# building, Huarun Chengshi Zhiyin (Xinyu Yayuan) Community 1#, 5# building, City bus company, family member courtyard, Projects under construction (Chang Jian.Yufeng), Fun district, Northern District, fun district building 1#、2#、3#、4#、5#, Zhengzhou Huimin High School and Dongyinggang Village so on. | TSP | Carry out monitoring once every quarter during the peak the construction period, and 3 continuous days each time. Monitor daily average value every day according to the specific requirements of “Quality Standards for Ambient Air” (GB3095-1996) | 60 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Comprehensive Emission Standards for Atmospheric Pollutants” GB16297-1996 |
|  | Noise | Station construction site and surrounding senstivie points ,and same as above(Ambient air) | Equivalent A sound level | Monitor once every month during the construction period, and 1 day each time; The daily monitoring periods are 8：00~10：00, 14：00~16：00, 20：00~22：00 | 65 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Limit for Noise on Architectural Construction Site” GB12523-90 |
|  | Vibration | Dept construction site and surrounding sensitive points and sensitive points the project line runs under(represented by Fuwa beauty area, Building 3, Building 1, Film Bureau Family Area 2# building, Tingdao Foreign Language training, Minggong Road 240# Yard)2#, 3# building, Minggong Road N0.245 (Xiqian Street 85# Yard 1#, 2# building), Guancheng Traditional Chinese Medicine Hospital and Dongyinggang Village so on. | Vibration level | Monitor once every monthduring the construction period, and 1 day each time; The daily monitoring periods are 8：00~10：00, 14：00~16：00, 20：00~22：00 | 20 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Measurement Methods for Urban Environmental Vibration”(GB10071-88) |
|  |  | Memorial Tower for February 7th Strike, Zhengzhou Confucius Temple，Zhengzhou Shang Dynasty Ruins | Vibration speed | Carry out continuous monitoring in case of shield tunneling, and 1 monitor every day; | 20 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Technical Regulations for Prevention against Industrial Vibration for Ancient Buildings”(GB/T50452-2008) |
|  | Surface Water | Discharge outlets of treatment facilities for vehicle cleaning water and slurry sewage | pH, SS, Oil, COD | Carry 1 monitor each month before 6 month, monitored once per quarter after then; 1 day each time | 10 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Comprehensive Discharge Standards for Sewage”(GB8978-1996) |
|  | Underground Water | Surrounding buildings of the base pit at the station, sensitive points the project runs under | Ground settlement | Rainfall period during construction, 1 time every day | 60 | Professional testing organ | Project Owner | Municipal and district environmental protection bureau | / |
|  |  | Station and sections constructed w ith open digging | Underground water level | Rainfall period during construction, 1 time every day |  |  |  |  | / |
|  |  | Station and sections constructed w ith open digging | Water quality | Rainfall period during construction, 1 time every day |  |  |  |  | “Quality Standard for Underground Water” Class III |
| Operational Period | Water Environment | Sewage at Depots | Discharge outlet of sewage treatment plant at depots | pH, SS, oil, COD | 2 time in the first year, 1 day per time; irregular monitoring thereafter; | 20 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Comprehensive Sewage Discharge Standards” (GB8978-1996) |
|  | Noise | Sensitive points around depots construction site, air kiosk of the stations and cooling tower（Building 1 of Yuhua ninth city，Hualian family member courtyard’s, Buildings 4，Cityorth Shore District, 1 # ,4#building，City bus company, family member courtyard 2#，Projects under construction (Chang Jian.Yufeng)，and Nanyang Road, No. 219 Courtyard4#,6# Sunshine Holiday district, 3 #, 2 # Building so on | Equivalent sound level A | 2 time in the first year,; to be carried out in 2 periods(daytimne and night); 1 day per time | 20 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Quality Standards for Sound Environment” GB3096-2008 and “Discharge Standard for Environmental Noise in Factory Area of Industrial Enterprise” GB12348-2008 |
|  | Vibration | New Hope Ao Garden, 17 #, 3 #，Fuwa beauty area, Building 3, Building 1，Taili community, Building 1, Hongda district, 11 #, 10 #, 9 #, 5 # Buildinsg，Huiji District, Changxing Road, Street office，Changxing Road, No. 2 Courtyard and Dongyinggang Village so on. | Vibration level | 2 time in the first year,; to be carried out in 2 periods(daytimne and night); 1 day per time | 20 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Measurement Methods for Urban Environmental Vibration”(GB10071-88) |
|  |  | Memorial Tower for February 7th Strike, Zhengzhou Confucius Temple，Zhengzhou Shang Dynasty Ruins | Vibration speed | 1 time in the 3 year period during the operational period; to be carried out in 2 periods(daytimne and night); 1 day per time | 20 | The project owner entrusts qualified organ to undertake the work by contract | Project Owner | Municipal and district environmental protection bureau | “Technical Regulations on Prevention of Industrial Vibration for Ancient Buildings”(GB/T50452-2008) |
|  | Electromagnetic Radiation | The main substation field | Power frequenxcy electromagnetic field, strong radio interference field | 1 time in the first 3 years, 1 hour per time | 5 |  |  |  |  |

# 5 Estimation of Environmental Protection Expenses and Analysis of Econoic Profit and Losses

## 5.1 Estimation of Environmental Protection Expesnes

The total environmental protection investement listed for rail transit line 3 of Zhengzhou City is 225419000yuan. See Table 5-1 for summary table of project environmental protection measures and investment:

Table 5-1 Summary Table for Estimated Envrionmental Protection Investment

| environmental elements | content of measures | investment estimation (10,000 yuan) |
| --- | --- | --- |
| Noise | Ventilation kiosk silencers at 16 ventilation kiosk areas are extended from 2m to 3m or 4m in length. | 240 |
|  | 3 cooling towers adopt ultra-low noise cross-flow type. | 90 |
|  | 3 cooling towers adopt low noise cross-flow type. | 100 |
|  | Jialu River Parking Lot is surrounded by enclosing walls (high enclosing wall at west) and green belt with width of 10m. | 60.9 |
|  | The car depot on East Hanghai Road is set with acoustic barrier with height of 2m. | 135 |
|  | Temporary sound insulation measures during construction period. | 225 |
|  | Subtotal | 850.9 |
| Vibration | For three cultural relics protection units of Shanhaimomuduha Tomb ,Zhengzhou Memorial Tower for February 7th Strike, Zhengzhou Confucius Temple and Zhengzhou Shang Dynasty Relics 4 along both sides of the line in this project, set the steel spring floating slab ballast beds or equivalent moderate shock-absorbing measures., totaling 780m at both sides and requiring 1.95million yuan investment. | 195 |
|  | For 38 over-limit sensitive spots where the line passes just through (in 5m range from the outer rail center line just above track) such as school, hospital and residence areas, including RCC family member courtyard (Gadameilin district) so on, arrange the steel spring floating slab integral ballast beds, totaling 7052m at both sides and requiring investment of 105.78 million yuan.. | 10578 |
|  | For 45 over-limit sensitive spots within 10--15m range mainly including City bus company, family member courtyard, and Tianxiu courtyard so on, use the flexible support block type integral ballast bed or equivalent moderate shock-absorbing measures, totaling 8753m for double line and the investment of 87.53 million yuan.. | 8753 |
|  | For the environment sensitive spot with over-limit environment vibration VLz10, or VLz10 is qualified, but VLzmax exceeds the standard environment requirements, including 28 locations of Peaceful residential homes, Building 8 and so on,, use type III vibration reduction fasteners or equivalent moderate shock-absorbing measures, totaling for 5239mm and investment of 17.45 million yuan.. | 1745 |
|  | Subtotal | 21271 |
| Water environment | Charges for sewage treatment during construction period | 50 |
| Electromagnetic environment | It is suggested to rationally arrange land for main transformer station and rationally plan surrounding land of the main transformer station to make enclosing walls of main transformer station at least 15m from residential areas. | / |
| Environmental monitoring fees during construction period | Monitoring for noise, vibration, water, air, groundwater level and sedimentation etc. | 275 |
| Environmental monitoring fees during operational period | Monitoring for noise, vibration, water and electromagnetism etc. | 90 (each year) |
| Total investment (excluding investment for monitoring during operational period) | 22541.9 |

## 5.2 Analysis of Economic Gains and Lossed due to Environmental Impacts

Analysis of economic gains and losses due to environmental impacts is mainly intended to measure the environmental protection effect that can be achieved through the environmental protection investment to be input for the construction project, and make general economic assessment of environmental impacts through comprehensive calculation of economic losses caused by factors of environmental impacts, benefits of environmental protection measures and engineering environmental benefits. Thus in addition to calculating investment and expenses for controlling pollution, the possible environmental and economic effects shall be accounted during analysis of economic gains and losses due to environmental impact.

### 5.2.1Means of Assessment and Analysis

The economic gains and losses due to environmental impacts of the project are comprehensively assessed by means of static analysis method, and conclusion is drawn from environmental and economic perspectives.

(1)Net Benefits of Evironmental Protection Investment

Calculation of net benefits of environmental protection investment is intended to assess the dominant environmental impacts of the project(beneficial or adverse impacts). The calculation formula is as follows:

B总=(B措-K)+B工–L前:

As shown in the formula：B总: Net benefits of environmental protection investment;

B措: Environmental economic benefits produced by environmental protection investment;

K :  Environmental protection investment and expenses;

B工: Environmenal and economic benefits due to environmental impacts of the project;

L前: Environmental and economic lossed in case of no environmental protection funds

(2)Investment Efficiency Ratio in Environmental Protection

The benefits and expenses ratio of investment on environmental protection must be calculated to assess the rationality of investment on environmental protection, and feasibility of environmental protection. The calculation formula is as follows:

E总=(B措+B工–L前)/K

In case E总≥1, it shows that the environmental economic benefits of the project are larger than the environmental protection expenses, and the project is accpetab le. In case E总<1, it shows the environmental protection expenses of the project is larger than the benefits obtained, and the project shall be given up. The larger E总 is, the better effect of environmental protection investment will be.

(1) Ratio between Environmental Protection Investment and Capital Construction Investment

Comparison of the index with that of similar domestic projects can confirm the rationality of the project.

### 5.2.2 Analysis of Economic Gains an Losses due to Environmental Impacts

The economic gains and losses due to environmental impacts of the project are comprehensively assessed by means of static analysis method, and conclusion is drawn from environmental and economic perspectives.

(I) Major Factors Influencing Environment

The major factors influencing environment entered into analysis of economic gains and losses due to environmental impacts are noise, ecological landscape and water pollution etc. according to characteristics of the project and specific local environmental conditions:

(II) Environmental economic losses produced before input of environmental protection funds L前

(1) Environmental economic losses caused by noise: L前声

According to the characteristics of the project, the populations around the air kiosk, cooling tower and depots as well as the ground lines of entrance/exit depot will be influenced by noise to various extents. Thus the project mainly assesses the environmental economic losses caused to surrounding populations due to subway noise. The report has selected the assessment coefficiency for environmental and economic lossed caused by noise of rail transit in Germany to passengers adopted by Planco in 1992 in a similar case, i.e. RMB 1.2 yuan per 100 persons km.

Suppose the average running speed of the train is 35km per hour(daily operational hour: 18 hours). As rail transit is a rapid means of transport, if the short interval between the trains is omitted, the trains running on the route can be seen as continuous, and the social populations around the noise source will receive constant impacts by the noise. And such people are influenced by the noise as if they travel by subway at 35km per hour for 18 years. It is estimated 10101 persons will be influenced by the noise of the project, and L前声is 27.87 million yuan per year.

(2) Environmental economic losses(L前水) caused by water pollution:

If the sewage discharged by the project is directly discharged without being disposed, the receiving water body will be polluted, and environmental economic losses will be caused due to deterioration of water quality. Such environmental economic losses is approximately replaced by the sewage discharge expenses payable for discharge of sewage of the same water quality and quantity. According to the current charging standards and provisions of relevant department, in case the sewage produced by the project is directly discharged without being disposed, the construction unit will pay 310,000 yuan per year as the sewage discharge expenses. Thus L前水is 310,000 yuan per year.

(3)Total environmental and economic losses(L前 ) caused before input of environmental protection funds:

Environmental and economic losses caused before input of environmental protection funds: L前= L前声+ L前水=28.18 Million yuan per year

(III) Investment on Environmental Protection K

The investment on environmental protection of the project is 225419000 yuan, which will be amortized over 4.25 years. Thus K is 53039764 yuan.

(IV)Environmental economic benefits(B措) caused by investment on environmental protection:

(1)Environmental economic benefits(B措声) caused due to decrease in the number of people influenced by noise after noise control

According to the prediction results for impacts on sound environment, the noise level at the sensitive points along the project line is basically maintained at the level before project construction after noise and pollution prevention and control measures are taken, that is the project construction will not increase the noise level of various sensitive points. B措声 is 27.87 million yuan per year.

(1) Environmental economic benefits(B措水) caused by control of water pollution:

According to relevant provisions, the sewage of the project will be discharged after reaching standard through treatment. The sewage discharge fee in the amount of 50,000 yuan per year shall be paid after sewage treatment through calculation, and 310,000 yuan per year shall be paid before sewage treatment. Thus the environmental economic benefits produced through treatment of water pollution(B措水 ) is 260,000 yuan per year.

(1) Total environmental economic losses produced by investment on environmental protection(B措):

B措= B措声 + B措房 + B措水 =28.13 Million yuan per year

(V) Environmental economic benefits caused by engineering environmental impacts(B工):

The extent of environmental pollution will be different in case road traffic instead of rail transit is adopted to meet the ever increasing demands for traffic by economic and social development along the route of the project in Zhengzhou City.

(1)Comparison of Environmental Economic Losses due to Noise Pollution:

To compare the environmental economic losses casued by noise due to two means of transport, the function of road traffic shall be the same as that of the means of transport of the project, and the travelling speed per hour is 35km per hour, with the daily operational period being 18 hours and the same quantity of passengers. Moreover, as road traffic is totally on the ground, the number of people influenced by noise on the two sides of the traffil route will be larger than that of subway, and is estimated to be 104,000. The populations along the road are influenced by noise as if they travel by road at the speed of 35km per hour for 18 hours.

According to relevant data of Germany, the estimation coefficient for environmental economic losses caused by road traffic noise on the passengers is RMB 1.7 yuan per 100 persons km.

The environmental economic losses caused by road traffic noise(L路声) is 406.55 million yuan per year through calculation.

The environmental economic benefits(B工声) caused by noise pollution in the two ways is B工声= L路声- L后声=406.55 Million yuan per year.

(2)Comparison of Environmental Economic Losses due to Atmospheric Pollution:

As rail transit utilizes power as energy, it produces less atmospheric pollution, thus the environmental economic losses caused by its atmospheric pollution is approximately 0.

According to the conclusion of atmospheric environmental impact assessment, the emission of automobile exhaust will be reduced due to project construction. The environmental economic losses due to road atmospheric pollution is estimated according to the environmental economic losses caused by the road traffic exhaust on passengers in Germany, that is RMB 0.2 yuan per 100 persons km. B工气=47.83 Million yuan per Year.

(3)Total environmental economic benefits(B工) due to engineering environmental impacts:

B工= B工声 + B工气 =454.38 Million yuan Per Year

(VI) Analysis of Economic Gains and Losses due to Environmental Impacts:

(1) In case B总is larger than 0, it shows the environmental impacts of the project are mainly beneficial.

Net benefits from envrionemental protection investment B总=(B措-K)+B工-L前=397,610,000 yuan per year.

(2)  Environmental protection investment efficiency E总=(B措+B工-L前)/K=8.01

E总>1, which shows that the environmental economic benefits of the project is larger than the environmental protection expenses, and the environmental protection investment effect is good.

(3)Environmental protection investment/capital construction investment ratio:

The environmental protection investment of the project is 225419000 yuan, and the estimated total investment of the project is 197699790000 yuan, thus the environmental protection investment/capital construction investment is 1.14%, which is similar to that of the environmental protection investment of similar domestic project. Thus the environmental protection investment is rational.

## 5 .3Conclusion:

The completion and operation of the project will positively promote social economy and urban environment in areas along the routes of the project. The environmental economic losses caused by project construction will be controlled within a small scope after several environmental protection measures are taken. Project construction will produce significant social benefits and environmental benefits, which complies with the principle of simultaneous growth of economic benefits, social benefits and environmental benefits.

# 6 Sources of funds

According to the current financial strength of Zhengzhou, the capital of Zhengzhou rail transit Line 3 project to be considered the mode of direct government investment, Adopted government financial sources of funding are: government budget funds for construction, special funds for urban construction(with civil air defense special funds) and Land transfer revenue and so on. Debt funds are mainly considered loans of domestic bank and World Bank.

# 7  Information management of the Environmental and Social Management Plan

## 7.1 Reorganize and save of monitoring data

The monitoring information involved in this project is reorganized by qualified units commissioned by Zhengzhou track Limited.

## 7.2 Information exchange

Environmental management requires the necessary exchange of information between different departments and different positions within the organization, at the same time, the organization also need communicate relevant information to the outside (stakeholders, public and so on).

Internal information exchange can be carried out in a variety of ways of meeting and internal briefings, but a formal meeting must be hold monthly, all exchange of information should be recorded and archived.

External information exchanges is held once every six months or one year, the exchange of information with collaboration unit should be formed the minutes and archived.

## 7.3 Record

For the effective operation of the environmental management system, the owners must be organized to establish a sound system of record, and retain the records of the following aspects:

- Legal and regulatory requirements;

- Related review and approval to the project;

- Environmental factors and the related environmental impact;

- Training;

- Examination, checking and maintenance activities;

- Monitoring data;

- Problems in environmental management and environmental protection work;

- Mitigation measures effectiveness;

- Relevant project information.

Complementary, necessary control must to be done to the above types of recording, including: the identification, collection, cataloging, archiving, storage, management, maintenance, inquiry, shelf life, disposal and other links.

## 7.4 Report

Environmental Management Office, contractors, monitoring units of zhenghzou rail transit Line 3  project should record the progress of the project, the implementation of the management plan (EMP), environmental quality monitoring results in the process of implementation of the project and report them to the authorities in a timely manner. These include:

- Monitoring units and contractors should record the implementation of the EMP in detail, and promptly report it to the PMO;

- The PMO must complete the project progress report (Such as the semi-annual report, etc.) timely according to the World Bank's requirements and submit it to the World Bank. The report mainly includes the followings:

- The implementation of environmental protection measures, environmental management, environmental monitoring, and training programs, etc, in the ESMP.

- The state of progress of the project, such as the progress;

- Whether there are complaints from the public, in case of a complaint, record the main content of complaints, solutions and public satisfaction;

- Execution plan of ESMP for the next year.

# Text boxes

E4437 V3 REV

Contractor

Internal Environmental Management

World Bank

External Environmental Management

State Ministry of Environmental Protection

Henan Provincial Environmental Protection Bureau

Zhengzhou Municipal Environmental Protection Bureau

Environmental Assessment Unit

Design unit

Project supervision agency organization

Project Office of Zhengzhou Rail Transit Line 2 Funded with the Loan of World Bank,

Zhengzhou Rail Transit Co., Ltd.

The third party environment monitoring unit

Risk Consultation unit

Safety supervision agency organization

Contract, Management Relations                Coordination and Cooperation Relations

Internal Environmental Management

External Environmental Management

State Ministry of Environmental Protection

Henan Provincial Environmental Protection Bureau

Zhengzhou  Municipal Environmental Protection Bureau

Project Office of Zhengzhou Rail Transit Line 3 Funded with the Loan of World Bank,

Zhengzhou Rail Transit Co., Ltd., Environmental Assessment Unit

Zhengzhou Rail Transit Operation Management Company

The third Party Environment Monitoring Unit

Contract and management relationship

Coordination and cooperation relationship

Zhengzhou Rail Transit Group Co., Ltd.

Site Circuit Inspection, Auxiliary Monitoring, Analysis of Monitoring Data

Contract and relevant policies

Fail to pass

Pass

Inspect, accept and assess

Implement measures

Contractor

Discover Problems, Analyze Reason and Issue Instructions

Environmental Supervisory Engineer

Chief Supervisory Engineer

Project Supervisory Agency

Figure 3.2-1 Environmental Supervisory Organ and Working Process in Construction Period